## Slide 1: Harmonization of entropy coding methods in H.BWC
Document VCEG-BX14
Fraunhofer HHI

## Slide 2
Current H.BWC: Two entropy coding paths:
  Huffman (used for LMS)
  CABAC (used for all other cases)
Goal: Investigate possibility to unify entropy coding methods
Reason: Makes standard simpler
Motivation and goal

## Slide 3: Experiment I: „LMS-only“ baseline of H.BWC
LMS-baseline:
Configure H.BWC to use only LMS path (thus: always Huffman coding) and single blocksize 2048:
  --CodecMode=1,
  --LOG2_MAX_BLOCK_SIZE=11,
  --MAX_SPLIT_DEPTH=0
Compression performance of LMS-only baseline relative to H.BWC-anchor:
Experiment I:
Replace Huffman coding by CABAC coding in LMS-baseline
Anchor: LMS-baseline with Huffman. Test: LMS-baseline with CABAC.
 | Bit-rate change | Enc-time | Dec-time
ECG | 48.35 % | 3.13 % | 82.66 %
EEG (CHB-MIT) | 12.88 % | 1.78 % | 118.66 %
EMG | 2.88 % | 2.95 % | 110.95 %

## Slide 4: Results for Experiment I (Anchor: LMS-baseline)
Simple scalar quantization:
Scalar quantization with RDOQ:
Trellis coded quantization:
Anchor: LMS-baseline with Huffman.
Test: LMS-baseline with CABAC

## Slide 5: Experiment II: Combination of LMS and other prediction modes
Investigate for EEG, LMS most effective here
„EEG-baseline“: No LMS, only inter-channel prediction, constanst block-size 2048, only DCT-transform, CABAC-entropy coding, trellis coded quantization
Compression performance of „EEG-baseline“ relative to H.BWC-anchor:
Experiment II:
Use LMS on prediction residuals of EEG baseline. CABAC entropy coding.
Anchor: EEG-baseline. Test: EEG-baseline, LMS always on.
 | Bit-rate change | Enc-time | Dec-time
EEG (CHB-MIT) | 10.28% | 8.85% | 108.04%

## Slide 6: Results for Experiment II
Anchor: EEG-baseline
Test: EEG-baseline, LMS always on
Simple scalar quantization:
Scalar quantization with RDOQ:
Trellis coded quantization:
 | Bit-rate change | Enc-time | Dec-time
EEG (CHB-MIT) | - 8.94 % | 98.71 % | 153.98 %
 | Bit-rate change | Enc-time | Dec-time
EEG (CHB-MIT) | - 11.77 % | 117.89 % | 151.13 %
 | Bit-rate change | Enc-time | Dec-time
EEG (CHG-MIT) | - 16.10 % | 197.90 % | 152.56 %

## Slide 7: Experiment III
Anchor: H.BWC with CTC
Test: EEG-baseline with LMS always on (same as Experiment II)
Simple sclar quantization:
Scalar quantization with RDOQ:
Trellis coded quantization:
 | Bit-rate change | Enc-time | Dec-time
EEG (CHB-MIT) | - 0.03 % | 8.74 % | 166.36 %
 | Bit-rate change | Enc-time | Dec-time
EEG (CHB-MIT) | - 3.22 % | 10.44 % | 163.28 %
 | Bit-rate change | Enc-time | Dec-time
EEG (CHG-MIT) | - 7.77 % | 17.52 % | 164.83 %

## Slide 8: Conclusions and Suggestion
Conclusion from Experiment I:
  Can increase compression performance of LMS-only mode when replacing Huffman by CABAC. Very limited impact on encoder runtime
Conclusion from Experiment II/III:
  Can signifciantly increase compression performance of H.BWC at significantly decreased encoder runtime by combinging LMS with prediction and CABAC coding
Suggested to study proposed technologies in CE