## Slide 1
CE11 Report on Prediction Unit Dependent Coefficient Scanning For Inter Frame

## Slide 2: Background
A prediction unit dependent coefficient scanning order selection scheme (PDCS) for inter coding is proposed in the last meeting.

## Slide 3: Proposal Scheme
Because NSQT has been adopt into HM4.0 software, PDCS has to combine with NSQT. The relationship among PU partition, TU partition and scanning pattern is shown in Table.
PU partition | TU partition | Scanning pattern
SIZE_2NxN | NSQT(horizontal stripe) | Vertical scan
SIZE_2NxnU | NSQT(horizontal stripe) | Vertical scan
SIZE_2NxnD | NSQT(horizontal stripe) | Vertical scan
SIZE_Nx2N | NSQT(vertical stripe) | Horizontal scan
SIZE_nLx2N | NSQT(vertical stripe) | Horizontal scan
SIZE_nRx2N | NSQT(vertical stripe) | Horizontal scan
SIZE_2Nx2N | SQT | Zig-zag scan
SIZE_NxN | SQT | Zig-zag scan

## Slide 4: Proposal Scheme
Figure 1 Horizontal Scan
Figure 2 Vertical Scan

## Slide 5: Simulations & Results
 | Random Access LC |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.2% | 0.2% |  |  | 
Class B | -0.1% | -0.5% | -0.3% | -0.1% | -0.7% | -0.5%
Class C | 0.0% | -0.2% | -0.1% | 0.0% | -0.3% | -0.5%
Class D | 0.0% | -0.2% | -0.1% | -0.1% | -0.2% | -0.3%
Class E |  |  |  | -0.3% | -0.1% | -0.2%
Overall | 0.0% | -0.2% | -0.1% | -0.1% | -0.4% | -0.4%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 100% |  | 
Thanks Samsung for the crosschecking efforts