## Slide 1: JCTVC-H0496: On bitstreams starting with CRA pictures
Ye-Kui Wang, Ying Chen, and Marta Karczewicz

## Slide 2: Background
Follow-up of JCTVC-G319
Notes from the previous meeting
  “It was remarked that it may be difficult to specify conformance of a bitstream in such a case, as there would be implied dangling references to non-existing information. A bitstream needs to be testable for conformance (without access to unavailable data).
  “The concept seems useful, if it is possible to specify the bitstream conformance clearly, and the decoder behaviour as well. Further study is encouraged.”

## Slide 3
CRA
Poc 0
CRA
Poc 0
P
Poc 6
B
Poc -5
B
Poc -1
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
P
Poc 6
B
Poc 1
B
Poc 5
B
Poc 2
B
Poc 3
B
Poc 4
B
Poc -5
B
Poc -1
B
Poc -4
B
Poc -3
B
Poc -2
P
Poc -6
…..
…..
leading pictures:
Follow the CRA picture in decoding order but precede it in output order
normal pictures:
Follow the CRA picture in both decoding order and output order
Decoding order: from left to right, Poc: relative POC
Output order: from left to right, Poc: relative POC
B
Poc 7
B
Poc 8
B
Poc 9
B
Poc 7
B
Poc 8
B
Poc 9
P
Poc 10
P
Poc 10
lagging pictures: prior to the CRA in decoding order but follow it in output order
CRA picture:
I slices only
For each normal picture: inter prediction only from the CRA picture and/or other normal pictures (i.e., never from any picture other than the CRA picture or a normal picture)
Lagging pictures shall not exist
The CRA picture concept

## Slide 4: Introduction
In broadcasting, streaming, and multi-party video conferencing, random access points are frequently inserted
  Herein CRA outperforms IDR in coding efficiency
  Performing random access at CRA pictures is common, e.g., the recently finalized MPEG Dynamic Adaptive Streaming over HTTP (DASH) explicitly allows signaling of open-GOP random access points, which are effectively CRA pictures
  However, a bitstream starting from CRA picture is not a confirming bitstream
    It is not guaranteed that a conforming decoder may be able to handle random accessing from CRA pictures
    A practical problem: when the leading pictures are not present, is that the CPB may overflow, because the coded bits of pictures after the leading pictures in decoding order flow into the CPB earlier than when the leading pictures are not present, while the decoding times of these pictures are unchanged

## Slide 5: Proposal
To specify that a bitstream starting from a CRA picture is a conforming bitstream
Benefits
  Convenient for decoder implementations that are capable of performing random access from CRA pictures, thanks to
    Normative behaviors are clearly specified for random access from CRA pictures
  No unexpected decoding behaviors when performing random access from CRA pictures

## Slide 6: Addressing comments from the previous meeting
The main concern noted at the previous meeting was how to clearly specify bitstream conformance, particular due to the implied dangling references to non-existing information
We think that bitstream conformance can be clearly specified, as documented in the proposal. In particular, the issue of dangling references to non-existing information can be avoided by ignoring the leading pictures

## Slide 7: More details of the proposal (1/2)
Definition of leading pictures
  leading picture: a coded picture associated with a CRA picture, that follows the CRA picture in decoding order but precedes the CRA picture in output order
Leading pictures may or may not be present in the bitstream starting with a CRA picture. When present, a leading picture is ignored in the decoding process
The CPB overflow problem and the solution
  When the leading pictures are not present, the CPB may overflow
    Bits of the pictures following the starting CRA picture in decoding order flow into the CPB earlier (than when the leading pictures are present)
    If the CPB removal times of these pictures are kept unchanged, the CPB may overflow
  Solution to this problem
    To shift earlier the decoding time of pictures following the starting CRA picture
    The time shift is signaled in the buffering period SEI message

## Slide 8: More details of the proposal (2/2)
Bitstream conformance requirement
  The first coded picture, in decoding order, of a conforming bitstream may be an IDR picture or a CRA picture
  For a conforming bitstream starting with a CRA picture, the bitstream subset generated by discarding the access units that contain any leading picture associated with the starting CRA picture, when present, shall still be a conforming bitstream (i.e. fulfill all the bitstream requirements)