## Slide 1: Comparison of Compression Performance of HEVC Draft 7 with AVC High Profile
Bin Li, Gary J. Sullivan, Jizheng Xu
University of Science and Technology of China
Microsoft Corp.

## Slide 2: Performance Comparison
HEVC Draft 7 (HM-7.0)
  HM-7.0 Main
AVC High Profile (JM-18.3)
  Identical to those used in JCTVC-I0409
PNSR based objective measurement
Further study of JCTVC-G399, JCTVC-H0360, JCTVC-I409

## Slide 3: AVC High Profile vs. HEVC Draft 7 Main Profile
 | All Intra | Random Access | Low Delay
Class A | −23.4% | −36.9% | 
Class B | −22.8% | −39.5% | −41.1%
Class C | −20.3% | −30.4% | −32.5%
Class D | −16.9% | −28.2% | −29.7%
Class E | −28.8% |  | −42.9%
Class F | −22.7% | −26.0% | −29.9%
Average | −22.2% | −32.5% | −35.1%
Average without F | −22.1% | −34.1% | −36.4%

## Slide 4: Lossless Coding Performance
AVC lossless coding setting
  High 4:4:4 Predictive Profile (244)
  Set LosslessCoding to 1 in cfg file of JM
  Set all QPs to 0
Two issues
  For lossless coding AVC reports PSNR in a strange way
  Mismatch for U and V as reported in https://ipbt.hhi.fraunhofer.de/mantis/view.php?id=228
    We apply the solution provided at that link

## Slide 5: HM lossless coding
HM-7.0-dev r2461
Set all QPs to 0
LosslessCuEnabled : 0
TransquantBypassEnableFlag : 1
CUTransquantBypassFlagValue: 1

## Slide 6: Lossless coding performance
 | Average Compression ratio of AVC | Average Compression ratio of HEVC | Average delta bitrate (HEVC−AVC)/AVC%
AI | 3.29 | 3.14 | 4.7%
RA | 8.26 | 8.20 | −0.3%
LB | 12.03 | 12.27 | −0.0%
Compression ratio = original YUV rate / compressed bitrate
Original YUV rate is calculated as 12 bits / sample

## Slide 7: HEVC “High Efficiency” Tool Test
Excluding Class F
Main Profile used as anchor
Individual tool is enabled in each test

## Slide 8: “High Efficiency” Tool Performance
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV | Y | U | V | YUV
10-bit | −1.1% | −1.3% | −1.6% | −1.1% | −1.7% | −4.4% | −5.6% | −2.2% | −1.9% | −3.5% | −4.3% | −2.2%
 | Enc./Dec. 100%/103% |  |  |  | Enc./Dec. 100%/106% |  |  |  | Enc./Dec. 100%/106% |  |  | 
ALF | −1.3% | −3.0% | −3.2% | −1.7% | −2.6% | −2.6% | −2.5% | −2.5% | −1.3% | −2.9% | −3.1% | −1.6%
 | Enc./Dec. 103%/113% |  |  |  | Enc./Dec. 101%/114% |  |  |  | Enc./Dec. 100%/113% |  |  | 
LM | −0.7% | −8.2% | −6.6% | −1.8% | −0.3% | −10.1% | −7.1% | −1.6% | −0.1% | −2.4% | −2.1% | −0.5%
 | Enc./Dec. 103%/101% |  |  |  | Enc./Dec. 100%/100% |  |  |  | Enc./Dec. 100%/101% |  |  | 
TS* | 0.0% | 0.0% | −0.2% | 0.0% | 0.0% | −0.2% | −0.3% | −0.1% | 0.0% | 0.2% | 0.1% | 0.0%
 | Enc./Dec. 130%/100% |  |  |  | Enc./Dec. 102%/100% |  |  |  | Enc./Dec. 101%/100% |  |  | 
NSQT |  |  |  |  | −0.4% | −0.8% | −0.7% | −0.5% | −1.0% | −2.6% | −2.2% | −1.2%
 |  |  |  |  | Enc./Dec. 102%/100% |  |  |  | Enc./Dec. 102%/100% |  |  | 
*TS brings about 7.5%, 5.5%, and 3.3% Y BD-Rate saving for AI, RA, and LB respectively.

## Slide 9: HEVC Fast Encoding Algorithms Evaluation
Existing fast encoding algorithms (names are from the help message of HM encoder)
  Fast intra transform skipping
  Early CU
  Cbf fast mode
  Early SKIP detection
Two other simple method for Intra mode decision
  Only check one mode with smallest SATD cost and MPMs (set every element in g_aucIntraModeNumFast[] to 1 )
  Only check DM and LM for chroma

## Slide 10: Y BD-Rate of fast encoding algorithms
 | AI-Main | AI-HE10 | RA-Main | RA-HE10 | LD-Main | LD-HE10
Class A | 1.2% | 1.0% | 2.0% | 1.9% |  | 
Class B | 1.3% | 1.1% | 2.5% | 2.4% | 1.7% | 1.8%
Class C | 2.0% | 1.8% | 2.8% | 2.8% | 1.5% | 1.6%
Class D | 2.4% | 2.1% | 2.9% | 2.8% | 1.6% | 1.8%
Class E | 2.0% | 1.7% |  |  | 2.2% | 2.3%
Overall | 1.8% | 1.5% | 2.5% | 2.5% | 1.7% | 1.8%
Enc. Time | 62% | 60% | 48% | 48% | 48% | 48%
Dec. Time | 100% | 100% | 99% | 99% | 99% | 99%