## Slide 1: Improvement of the rate control for HEVC (JCTVC-K0229)
J. Yoo, J. Nam, H. Choi, D. Sim
KwangWoon Univ (KWU)

## Slide 2: Unified rate control in HM8.0
In random access
  BD-BITRATE and BD-PSNR losses are up to 31.51% and 1.27dB, respectively.
    Inaccurate target-bit computation for a frame.
    The bits for periodic IDR frames takes a large portion of 19.6% for a sequence.
In low delay
  Large fluctuation: Maximum and minimum bits are 312% 17% of the uniform target bits
    No RQ-model for the first frames in all the GOPs
    RDO depending TIDs and it leads a large amount of bits for the frames having TID of zero, compared to predicted ones.

## Slide 3: The proposed method for random access case (1/2)
Complexity weighting factors in the proposed RC
 No additional computation for the MAD(j) and the lambda()
Target-bit computation in HM8.0 RC
is virtual buffer based on remaining budget
is virtual buffer based on buffer occupancy
The complexity weighting factors are based on the generated bits and the QP.
To estimate frame complexity, the weighting factors are derived from distortion and bits.

## Slide 4: The proposed method for random access case (2/2)
Two types of virtual buffer (VB) for the HM8.0 RC
  Initial buffer with exceeded bits influences the following frames to reduce the target-bit.
  Virtual buffer with exceeded bits affects the target-bit of the next frame.
exceeded bits
target bits
Extended virtual buffer (VB) for the proposed RC
  The long-term VB distributes exceeded bits to the consecutive frames until the next IDR frame.
  The short-term VB immediately allocates the exceeded bits to the next frame in the same way as the HM8.0 rate control except for IDR frames.
Initial VB
d
d
IDR
IDR
burden
.......
1th frame
General VB
Jth frame
encoding jth frame

## Slide 5: The proposed method for low delay case (1/2)
The firstly coded frame in a GOP
  RQ-model is not applied to all of the first frames in each GOP for the HM8.0 RC.
  The first frames not being the RQ-model make periodic fluctuation large as well as target-bit prediction model worse.
   To reduce bit fluctuation, RQ model is applied to all of the first frames except for the first frame of a sequence in the proposed method.
Figure 1. bit fluctuation effect of the first frames in each GOP
BasketballPass 209 Kbps, 48FPS

## Slide 6: The proposed method for low delay case (2/2)
The rate control according to the temporal layer ID in the HM8.0
  The different lambda depending on the TID affects actual generated bits in RDO.
 The proposed RC employs only lambda regardless of the temporal layer ID.
Figure 2. bit fluctuation according to the lambda
BasketballPass 209 Kbps

## Slide 7: Performance evaluation of the improved RC for RA
① Modification of the complexity weighting factors
 | The proposed RC |  |  | 
 | Δkbps | ΔPSNR | BD-PSNR | BD-BR
ClassA | 1.64 | -1.01 | 0.36 | -7.01
ClassB | 1.41 | -0.52 | 0.63 | -19.08
ClassC | 0.41 | -0.27 | 1.24 | -24.99
ClassD | 0.57 | -0.24 | 1.01 | -21.85
ClassE |  |  |  | 
Average | 1.01 | -0.51 | 0.81 | -18.23
Measures
  BD-PSNR and BD-BR are evaluated, compared to the HM8.0 RC.

## Slide 8: Actual generated bits over frame index for RA
①+② the proposed rate control
 | The HM8.0 RC |  | The proposed RC |  |  | 
 | Δkbps | ΔPSNR | Δkbps | ΔPSNR | BD-PSNR | BD-BR
ClassA | 1.04 % | -1.44 dB | 1.32 % | -1.05 dB | 0.31 dB | -6.24 %
ClassB | 0.81 % | -1.22 dB | 1.25 % | -0.59 dB | 0.55 dB | -17.37 %
ClassC | 0.66 % | -1.46 dB | 0.26 % | -0.34 dB | 1.16 dB | -23.58 %
ClassD | 0.70 % | -1.17 dB | 0.36 % | -0.34 dB | 0.89 dB | -19.54 %
ClassE |  |  |  |  |  | 
Average | 0.80 % | -1.32 dB | 0.80 % | -0.58 dB | 0.73 dB | -16.68 %
② VBs, long-term and short-term Management
 | The proposed RC |  |  | 
 | Δkbps | ΔPSNR | BD-PSNR | BD-BR
ClassA | 0.72% | -1.12 dB | 0.25 dB | -5.28 %
ClassB | 0.78% | -0.73 dB | 0.42 dB | -13.77 %
ClassC | 0.19% | -0.44 dB | 1.07 dB | -21.99%
ClassD | 0.61% | -0.42 dB | 0.81 dB | -17.7%
ClassE |  |  |  | 
Average | 0.47% | -0.68 dB | 0.63 dB | -14.68 %

## Slide 9: Status of accumulated occupancy of VB for RA
Traffic 13141 Kbps, 32 FPS
BasketballDrive 17817 Kbps, 48 FPS
BasketballDrill 3,614 Kbps, 48 FPS
BasketballPass 197 Kbps, 48 FPS

## Slide 10: PSNR over frame index for RA
BasketballDrive 17817 Kbps, 48 FPS
Traffic 13141 Kbps, 32 FPS
BasketballDrill 3,614 Kbps, 48 FPS
BasketballPass 197 Kbps, 48 FPS

## Slide 11: Performance evaluation of the improved RC for LD
Low delay
 | The HM8.0 RC |  |  | The proposed RC |  |  |  |  | ΔVAR
 | Δkbps | ΔPSNR | VAR | Δkbps | ΔPSNR | BD-PSNR | BD-BR | VAR | 
ClassA |  |  |  |  |  |  |  |  | 
ClassB | 0.19 % | -0.86 dB | 70722 | 0.29 % | -1.87 dB | -1.23 dB | 47.73 % | 38191 | 46.00%
ClassC | 0.26 % | -0.53 dB | 17265 | 0.18 % | -1.16 dB | -1.23 dB | 18.65 % | 2864 | 83.41%
ClassD | 0.14 % | -0.45 dB | 2876 | 0.19 % | -0.87 dB | -0.72 dB | 13.41 % | 1744 | 39.36%
ClassE | 0.50 % | -0.71 dB | 9377 | 0.73 % | -1.42 dB | -0.51 dB | 30.46 % | 6026 | 35.74%
Average | 0.27 % | -0.64 dB | 25060 | 0.35 % | -1.33 dB | -0.92 dB | 27.56 % | 12206 | 51.13%
Low delay P
 | The HM8.0 RC |  |  | The proposed RC (LB) |  |  |  |  | ΔVAR
 | Δkbps | ΔPSNR | VAR | Δkbps | ΔPSNR | BD-PSNR | BD-BR | VAR | 
ClassA |  |  |  |  |  |  |  |  | 
ClassB | 0.26 % | -0.93 dB | 70460 | 0.34 % | -2.07 dB | -1.08 dB | 40.62 % | 32029 | 54.54 %
ClassC | 0.38 % | -0.56 dB | 15734 | 0.19 % | -1.26 dB | -0.63 dB | 16.96 % | 2692 | 82.89 %
ClassD | 0.13 % | -0.45 dB | 2785 | 0.17 % | -0.92 dB | -0.44 dB | 11.62 % | 1581 | 43.23 %
ClassE | 0.50 % | -0.77 dB | 7778 | 0.72 % | -1.48 dB | -0.72 dB | -1.45 % | 6270 | 19.39 %
Average | 0.32 % | -0.68 dB | 24189 | 0.35 % | -1.43 dB | -0.72 dB | 16.94 % | 10643 | 50.01 %

## Slide 12: Actual generated bits over frame index for LB
BasketballPass 209 Kbps, The HM8.0 RC
BasketballDrill 418 Kbps with HM8.0 RC
BasketballDrill 418 Kbps with proposed RC
BasketballPass 209 Kbps, The proposed.0 RC

## Slide 13: Status of accumulated occupancy of VB for LB
BQMall 4,184K
BlowingBubble 821K
Johnny 1,506K
BQTerrace 1,986K

## Slide 14: Status of accumulated occupancy of VB for LP
BQTerrace 2,351K
BQMall 4,586K
BlowingBubble 8,57K
Johnny 1,862K

## Slide 15: Conclusion
  For the RA, RD performance is improved
    average BD-PSNR increases by 0.73 dB, compared to the HM8.0 RC
  For the LD, reduction of bit fluctuation is achieved
    Variation of bits fluctuation is reduced by 50.57%