## Slide 1: JCTVC-M0154 Combination of Merge and GRP
Wenjing Zhu
Haitao Yang
Huawei Technologies

## Slide 2: Motivation(1)
For merge PU, the motion information is inherited from neighbor PUs.
The inherited motion information may not be accurate for current PU
Residual of merge PU tends to be larger than ordinary inter PU.

## Slide 3: Motivation(2)
Generalized Residual Prediction utilizes information of BL_Col and BL_Ref to generate more accurate EL_Pred.
For PU with GRP, residual tends to be smaller than PU without GRP.
From the feature of residual of merge PU and GRP PU, it is natural to combine merge and GRP.

## Slide 4: Motivation(3)
Do a statistical experiment on merge and GRP, result shows that when utilizing GRP only on 2Nx2N PU, 95% of the PU with GRP is merge mode.
Just doing GRP on merge PU can take advantage of GRP
Because of the low percentage of GRP in ordinary inter PU, it is a waste of time to do RDO on GRP and also a waste of bitrate to signal the PU’s mode (GRP or normal temporal prediction).
Spatial Ratio | Conditional probability | BL_QP/EL_QP |  |  |  |  |  |  | 
 |  | (22,22) | (26,26) | (30,30) | (34,34) | (22,24) | (26,28) | (30,32) | (34,36)
1.5 | MRGInGRP | 0.9291 | 0.9382 | 0.9468 | 0.9593 | 0.9256 | 0.94 | 0.958 | 0.9737
 | GRPInMerge | 0.7074 | 0.6309 | 0.5969 | 0.5713 | 0.7518 | 0.688 | 0.6616 | 0.6509
2.0 | MRGInGRP | 0.9063 | 0.9236 | 0.9414 | 0.9559 | 0.9143 | 0.9348 | 0.9532 | 0.9635
 | GRPInMRG | 0.5117 | 0.4176 | 0.3841 | 0.339 | 0.5465 | 0.4921 | 0.4738 | 0.4193

## Slide 5: Motivation(4)
Res-1,Res-0.5 and Diff-0.5 are three GRP modes proposed by many contribution and also evaluated in JCTVC-M0157.
The three modes show much gain.

## Slide 6: Proposed Method
Utilize 3 GRP modes(Res-1, Res-0.5 and Diff-0.5)
To avoid too high memory bandwidth burden, just do GRP on 2Nx2N PU.
To achieve more accurate prediction and less head information in the same time, propose doing GRP only on 2Nx2N PU with merge.

## Slide 7: Simulation Results
 | RA- 2x | RA-1.5x | RA-SNR | LDP-2x | LDP-1.5x | LDP-SNR | LDB-2x | LDB-1.5 | LDB-SNR
Y | -1.7% | -2.6% | -2.1% | -3.5% | -5.0% | -4.4% | -3.5% | -5.1% | -3.8%
U | -2.9% | -4.7% | -3.4% | -2.5% | -4.5% | -4.3% | -3.7% | -6.7% | -4.3%
V | -3.1% | -5.1% | -3.4% | -1.8% | -3.5% | -3.9% | -3.5% | -6.4% | -3.8%
Enc | 120.6% | 113.3% | 114.9% | 121.4% | 111.9% | 116.5% | 115.7% | 109.1% | 111.9%
Dec | 105.1% | 107.7% | 106.3% | 104.5% | 105.9% | 105.9% | 108.6% | 111.8% | 109.1%

## Slide 8: Proposed Syntax Table
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
merge_flag[ x0 ][ y0 ] | ae(v)
if( merge_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
… | 
} | 
if ( layerId > 0 && ( cu_skip_flag[ x0 ][ y0 ] ¦ ¦ ( merge_flag[ x0 ][ y0 ] && PartMode = = 2Nx2N ) ) | 
inter_pred_mode | ae(v)
} | 

## Slide 9
Thank Interdigital for crosscheck