## Slide 1: Non-RCE2: Rice parameter initialization for higher bit depth coding
Seung-Hwan Kim, Kiran Misra, Andrew Segall
(JCTVC-O0327)

## Slide 2: Background
The binarization of the syntax element coeff_abs_level_remaining depends on the Rice parameter.
The parameter (cRiceParam) is set to 0 at the beginning of each 4×4 sub-block of transform coefficients.
JCTVC-N0181 and JCTVC-N0189 presented methods to initialize the Rice parameter based on previously coded coefficients.
A simple Rice parameter initialization method based on bit depth information is introduced for higher bit depth coding

## Slide 3: Proposed Method
Proposed method includes two modifications;
1) Rice parameter initialization
2) Maximum rice parameter is extended up to 16
Rice parameter is initialized based on bit depth (BD) information as follows
If (extended_precision_processing_flag)
{
if (transform_skip_flag || cu_transquant_bypass_flag) uiGoRiceParam = BD-8;
else uiGoRiceParam = (BD-8) >>1;
}
else uiGoRiceParam = 0;

## Slide 4: Comparison of Results
 | All Intra |  | 
 | Y | U | V
12-bit | -6.8% | -6.4% | -6.4%
14-bit | -18.4% | -18.2% | -18.1%
16-bit | -28.2% | -28.1% | -28.2%
 | All Intra |  | 
 | Y | U | V
12-bit | -3.6% | -3.3% | -3.5%
14-bit | -11.3% | -11.2% | -11.3%
16-bit | -23.7% | -23.6% | -23.7%
A1 (JCTVC-O0206, method 2)
 | All Intra |  | 
 | Y | U | V
12-bit | -7.1% | -6.8% | -6.8%
14-bit | -18.7% | -18.4% | -18.3%
16-bit | -28.6% | -28.5% | -28.5%
D1 (JCTVC-O0239)
Proposed Method (JCTVC-O0327), Max=16
 | 12-bit | 14-bit | 16-bit
A1 vs. D1 | 3.5% | 7.4% | 4.9%
Proposed vs. D1 | 0.3% | 0.3% | 0.4%

## Slide 5: Comparison of Results (Luma)
 | All Intra |  | 
 | 12-bit | 14-bit | 16-bit
129 / Max 9 | -1.9 % | -8.4% | -14.1 %
A1 / Max 7 | -1.8 % | -10.4 % | -23.6 %
A1 / Max 9 | -3.6 % | -11.3 % | -23.7 %
327 + A1 / Max 9 | -6.6 % | -18.4 % | - 28.2 %
Coding Impact of Initialize RP | - 3.0 % | -7.1 % | -4.5 %