## Slide 1: JCTVC-P0126 SEI message for Colour Mapping Information
P. Andrivon, P. Bordes, E. François
16th JCT-VC Meeting: San José, 9 – 17 Jan. 2014

## Slide 2: Colour Mapping Info SEI
  Context
    Migrating to WCG: Rec.2020/XYZ-based colorspaces
        Rec.2020/XYZ future-proof colour encoding systems
    Different display technologies, different gamut
      LCD, LED, OLED…
  Rationales
    Smooth colour space transition
      No Rec.2020 reference screen (production side)  Gamut mapping
        Important quality variations w.r.t. employed algo
        Gamut difference between produced WCG/Rec.709 content to increase with years
    Preserving artistic intent for movies
      Bring quality from the Studios to the Home
      But… keeping TV sets differentiation (if required)
        E.g. mapping between Rec.2020/XYZ and mastering display (not TV set)
    Transmit metadata with bitstreams: SEI
      To avoid data pruning during distribution
      To avoid sync issues

## Slide 3: Colour Mapping Info SEI
  Applications
    UHDTV forward compatibility scenario
      e.g. UHD-1 Rec.2020 phase 2 signal with UHD-1 phase 1 Rec.709 devices
    HD/UHD Rec.709 streams with WCG support
      Use legacy workflow while deploying new displays with new formats
    High quality stored content (Blu-ray…)
      Preserving colorist intent
    Colour mapping for specific applications
      Highlight content in content
      Non destructive content personalization
      …

## Slide 4: Colour Mapping Info SEI
  Proposition
    Syntax inspired from SEI tone mapping information
    Output format parameters : same as VUI
    Several models (colour _map_model_id)
      1D LUT + 3x3 matrix + 1D LUT
        Leverage displays exisiting resources
      3D CLUT
        Generic model adressing low/high complexity mapping models
        Already used in production
      …

## Slide 5: Colour Mapping Info SEI
  Proposition: 1D LUT + 3x3 matrix + 1D LUT
    Configurable model
    1D LUT: Piecewise linear (same as tone_map_model_id 3)

## Slide 6: Colour Mapping Info SEI
  Conclusion
    Demo showing benefits (last meeting)
    Addressing upcoming applications
    Simplified model: 1D LUT + 3x3 matrix + 1D LUT
      address complexity concerns
      use limited resources from display