## Slide 1: JCTVC-P0xxx Non-RCE4: A true-padding method for intra-block copying prediction
Kai Zhang, Xiaozhong Xu, Jicheng An, Xianguo Zhang, Shan Liu, Shawmin Lei

## Slide 2: Overall Summary
The Problem in Intra BC
  The reference block cannot be overlapped with the current block.
  Horizontal/vertical padding has an intrinsic contradiction
Proposed
  Two padding methods
  An unreconstructed sample in the reference block is estimated by its prediction directly
Results
  Achieve 0.9%, 0.8%, 1.5% and 1.6% BD-rate reduction respectively for RGB SC, YUV SC, optional RGB SC, and optional YUV SC sequences in AI HE Main-Tier configurations.

## Slide 3: The problem in Intra BC
The reference block cannot be overlapped with the current block.
  Horizontal/vertical padding has an intrinsic contradiction
  A sample in the overlapped area is in the reference block as well as in the current block.
  As a sample in the current block, it should be predicted to a prediction value in the prediction process.
  As a sample in the reference block, it should be padded to a padding value in the padding process on the other hand.
  The estimation for sample may be contrary in the prediction and padding process in horizontal/vertical padding.

## Slide 4: The problem in Intra BC
An example
  In the Intra BC prediction process, sample A is estimated to be equal to sample B (white).
  But it is also estimated to be equal to sample D (black) in the horizontal padding process

## Slide 5: Proposed Method A
  A true padding method is proposed
    The prediction value for a sample in the prediction process is treated as the padding value directly.
  Example
    In the Intra BC prediction process, sample A is estimated to be equal to sample B (white).
    So A is estimated to be equal to its predicted value, i.e. white, in the true padding process.
  There should be some replicated pattern in a block if the Intra BC is applied mode with overlapped blocks
    True padding method can reflect the replicated pattern in the reference block much better

## Slide 6: Proposed Method B
Overlapped area is divided by two regions, using the extended BV along the same line towards the overlapped area

## Slide 7: Results (Method A)
Lossless results
 | AI |  |  |  |  |  |  |  |  |  |  | 
 | Compression ratio |  |  |  |  |  |  |  | Bit-rate increase |  |  | 
 | Total |  | Average |  | Min |  | Max |  | Total | Avg | Min | Max
 | Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
Class F | 4.58 | 4.59 | 5.59 | 5.59 | 2.27 | 2.27 | 11.20 | 11.21 | -0.1% | -0.1% | -0.2% | 0.0%
Class B | 2.25 | 2.25 | 2.26 | 2.26 | 2.08 | 2.08 | 2.44 | 2.44 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 9.40 | 9.43 | 11.7 | 11.79 | 6.50 | 6.50 | 19.62 | 20.07 | -0.2% | -0.4% | -2.2% | 0.0%
RGB 4:4:4 Animation | 2.83 | 2.83 | 2.9 | 2.86 | 2.41 | 2.41 | 3.14 | 3.14 | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 11.17 | 11.21 | 13.5 | 13.61 | 7.96 | 7.97 | 21.63 | 22.11 | -0.3% | -0.5% | -2.2% | 0.0%
YCbCr 4:4:4 Animation | 3.05 | 3.05 | 3.2 | 3.22 | 2.62 | 2.62 | 3.98 | 3.98 | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 1.98 | 1.98 | 2.44 | 2.44 | 1.52 | 1.52 | 4.43 | 4.43 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 30.91 | 31.22 | 34.30 | 34.74 | 17.27 | 17.28 | 48.88 | 49.29 | -1.0% | -1.1% | -2.4% | -0.1%
YCbCr 4:4:4 SC (Optional) | 35.53 | 36.00 | 38.63 | 39.18 | 24.30 | 24.37 | 58.96 | 59.83 | -1.3% | -1.3% | -2.1% | -0.3%
Enc Time[%] | 100% |  |  |  |  |  |  |  |  |  |  | 
Dec Time[%] | 89% |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Results (Method A)
Lossless results
 | RA |  |  |  |  |  |  |  |  |  |  | 
 | Compression ratio |  |  |  |  |  |  |  | Bit-rate increase |  |  | 
 | Total |  | Average |  | Min |  | Max |  | Total | Avg | Min | Max
 | Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
Class F | 8.64 | 8.64 | 35.85 | 35.87 | 3.01 | 3.01 | 88.86 | 88.94 | 0.0% | 0.0% | -0.1% | 0.0%
Class B | 2.60 | 2.60 | 2.60 | 2.60 | 2.57 | 2.57 | 2.64 | 2.64 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 56.83 | 56.88 | 140.5 | 141.67 | 20.03 | 20.04 | 290.96 | 297.49 | -0.1% | -0.4% | -2.2% | 0.0%
RGB 4:4:4 Animation | 3.67 | 3.67 | 3.7 | 3.68 | 3.47 | 3.47 | 3.86 | 3.86 | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 71.01 | 71.09 | 161.3 | 162.55 | 24.73 | 24.74 | 321.23 | 328.18 | -0.1% | -0.4% | -2.1% | 0.0%
YCbCr 4:4:4 Animation | 3.87 | 3.87 | 4.5 | 4.49 | 2.79 | 2.79 | 5.70 | 5.70 | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 2.14 | 2.14 | 2.57 | 2.57 | 1.59 | 1.59 | 4.50 | 4.50 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 70.95 | 71.17 | 329.65 | 337.21 | 19.93 | 19.94 | 498.73 | 516.71 | -0.3% | -1.5% | -3.5% | -0.1%
YCbCr 4:4:4 SC (Optional) | 109.02 | 109.63 | 356.47 | 363.04 | 32.52 | 32.61 | 601.48 | 612.10 | -0.6% | -1.3% | -2.0% | -0.3%
Enc Time[%] | 99% |  |  |  |  |  |  |  |  |  |  | 
Dec Time[%] | 97% |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Results (Method A)
Lossless results
 | LB |  |  |  |  |  |  |  |  |  |  | 
 | Compression ratio |  |  |  |  |  |  |  | Bit-rate increase |  |  | 
 | Total |  | Average |  | Min |  | Max |  | Total | Avg | Min | Max
 | Ref. | Tested | Ref. | Tested | Ref. | Tested | Ref. | Tested |  |  |  | 
Class F | 8.84 | 8.84 | 56.21 | 56.24 | 3.00 | 3.00 | 163.08 | 163.19 | 0.0% | 0.0% | -0.1% | 0.0%
Class B | 2.61 | 2.61 | 2.61 | 2.61 | 2.57 | 2.57 | 2.64 | 2.64 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | 63.65 | 63.62 | 485.60 | 491.16 | 21.03 | 21.03 | 2111.85 | 2146.05 | 0.0% | -0.2% | -1.6% | 0.7%
RGB 4:4:4 Animation | 3.65 | 3.66 | 3.67 | 3.67 | 3.45 | 3.45 | 3.83 | 3.83 | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | 80.58 | 80.62 | 544.80 | 551.06 | 25.92 | 25.93 | 2333.65 | 2370.92 | -0.1% | -0.3% | -1.6% | 0.0%
YCbCr 4:4:4 Animation | 3.88 | 3.88 | 4.53 | 4.53 | 2.78 | 2.78 | 5.75 | 5.75 | 0.0% | 0.0% | 0.0% | 0.0%
RangeExt | 2.13 | 2.13 | 2.57 | 2.57 | 1.59 | 1.59 | 4.50 | 4.50 | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | 77.21 | 77.31 | 1334.89 | 1358.94 | 20.09 | 20.11 | 3012.92 | 3075.88 | -0.1% | -1.0% | -2.0% | -0.1%
YCbCr 4:4:4 SC (Optional) | 125.19 | 125.68 | 1294.26 | 1321.83 | 33.08 | 33.17 | 2516.65 | 2561.30 | -0.4% | -1.6% | -2.8% | -0.3%
Enc Time[%] | 99% |  |  |  |  |  |  |  |  |  |  | 
Dec Time[%] | 101% |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Results (Method A)
Lossy
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.3% | -0.2% | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.9% | -0.9% | -0.9% | -0.9% | -0.9% | -0.8% | -0.8% | -0.9% | -0.8%
RGB 4:4:4 Animation | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.8% | -0.7% | -0.6% | -0.8% | -0.7% | -0.6% | -0.8% | -0.6% | -0.7%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -1.5% | -1.5% | -1.5% | -1.4% | -1.6% | -1.5% | -1.4% | -1.6% | -1.5%
YCbCr 4:4:4 SC (Optional) | -1.6% | -1.2% | -1.3% | -1.6% | -1.3% | -1.5% | -1.5% | -1.4% | -1.5%
Enc Time[%] | 98% |  |  | 98% |  |  | 98% |  | 
Dec Time[%] | 90% |  |  | 88% |  |  | 80% |  | 

## Slide 11: Results (Method A)
Lossy
 | Random Access Main-tier |  |  | Random Access High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.2% | -0.3% | -0.2% | -0.2% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.7% | -0.7% | -0.7% | -0.7% | -0.7% | -0.6%
RGB 4:4:4 Animation | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.5% | -0.5% | -0.4% | -0.6% | -0.5% | -0.5%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -1.3% | -1.2% | -1.1% | -1.6% | -1.4% | -1.4%
YCbCr 4:4:4 SC (Optional) | -1.6% | -1.4% | -1.4% | -1.6% | -1.4% | -1.4%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 99% |  | 

## Slide 12: Results (Method A)
Lossy
 | Low delay B Main-tier |  |  | Low delay B High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | -0.4% | 0.5% | 0.0% | -0.3% | 0.2%
Class B | 0.0% | 0.2% | -0.1% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.8% | -0.7% | -0.7% | -0.7% | -0.7% | -0.6%
RGB 4:4:4 Animation | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 SC | -0.6% | -0.3% | -0.4% | -0.6% | -0.3% | -0.3%
YCbCr 4:4:4 Animation | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC (Optional) | -2.4% | -2.4% | -2.6% | -1.8% | -1.6% | -1.7%
YCbCr 4:4:4 SC (Optional) | -0.6% | -0.4% | -0.3% | -0.3% | -0.3% | -0.1%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 91% |  |  | 84% |  | 

## Slide 13: Results (Method B)
Lossless results

## Slide 14: Results (Method B)
Lossy

## Slide 15: Conclusion
Two padding methods are proposed
Method A: Achieve 0.9%, 0.8%, 1.5% and 1.6% BD-rate reduction respectively for RGB SC, YUV SC, optional RGB SC, and optional YUV SC sequences in AI HE Main-Tier configurations
Method B: Achieve 0.5%, 0.x%, 1.7% and 1.1% BD-rate reduction respectively for RGB SC, YUV SC, optional RGB SC, and optional YUV SC sequences in AI HE Main-Tier configurations
Suggest one to be adopted

## Slide 16: Thank you for your attention!