## Slide 1
Robert Brondijk / Wiebe de Haan
Research
February 19, 2016
CE6 experiments 4.3 and 4.6a

## Slide 2
Brief overview
Philips CE6 system is adapted from the Philips CfE system (described in m36266) in the following ways:
  Automatic reshaper parameter derivation
  4:2:0 processing in gamma domain instead of 4:4:4 processing in linear light domain
Two experiments have been done
  CE6.4.3: Reshaper curve transmitted as limited number of curve parameters
  CE6.4.6a: Reshaper curve transmitted as piece-wise linear approximation to fit the SEI format proposed in m37285
Following slides include a high level description of the system and test results.
Details can be found in document JCTVC-W0063 and the software that was provided.

## Slide 3
Key characteristics of Philips CE6 model
Enables SDR compatible transmission of HDR
Before coding: SDR (YCbCr 4:2:0, BT.1886) is automatically derived from HDR
  Gamma and 4:2:0 conversion done before the reshaper
  Automatic Parameter Derivation (APD) on frame basis in the reshaper
Coded SDR bitstream is transmitted with HDR reconstruction data
  Reconstruction data has very low bitrate and is assumed to be transmitted by SEI messages (alternatively PPS could be used)
After decoding: inverse process is used to reconstruct HDR
Quality of reconstructed HDR on par with CE anchors
Notes
  The Philips system transmits a “single layer” bitstream, but is not a “single signal” system in the sense that the decoder can produce differently graded SDR and HDR signals (depending on the connected display).
  In this CE we used automatic parameter derivation, but the same format can support manual grading.

## Slide 4
Philips parameter based single layer HDR solution

## Slide 5
High level processing overview
SDR transmission
Gamma
to 4:2:0
Reshaper
Desat.
Linear Light RGB
Gamma YUV
Gamma
to 4:4:4
Reshaper
Sat.
(Auto)
Metadata

## Slide 6
Automatic Parameter Derivation (AutoMetaData)
Automatic metadata derivation consists of two steps:
  Automatic parameter generation from an HDR image
  Temporal filtering
Following mapping curve parameters for an image are automatically derived from HDR image characteristics like black and peak-white levels and average luminance:
  BlackLevel
  WhiteLevel
  ShadowGain
  MidToneWidth
  HighlightGain
Separate asymmetric temporal filtering is applied on BlackLevel, WhiteLevel and ShadowGain, while other 2 are derived. Only values from previous and current frame are used for temporal filtering.
See next slide for examples.

## Slide 8
Philips 4:2:0 reshaper at encoder side

## Slide 9
HDR to SDR Tone Mapping

## Slide 10
Philips 4:2:0 reshaper at decoder side

## Slide 11
Metadata channel bitrate and curve approximation
CE6.4.3 (parameters transmitted directly)
  With some overhead the total amount of metadata per frame was 71 bytes
  This number can get down to <50 bytes per frame after some optimizations
  For 60 Hz: < 24 kbps
CE6.4.6a (piece-wise linear reshaping curve transmitted)
  From experimental data we found a good curve approximation with 30 pairs of 16-bit points for the parabolic part
  With this approximation we find similar results for CE6.4.6a and CE6.4.3
  With some overhead the total amount of metadata per frame was 142 bytes
  For 60 Hz: < 70 kbps

## Slide 12
Results
Initially coding was done with HM-16.7
  Results of CE6.4.3 were cross-checked by Technicolor
  Results of CE6.4.6a were cross-checked by FastVDO
Next, coding was done again using “anchor HM” as used for the anchors in CE1
  Results were cross-checked by FastVDO
From our own observations we conclude:
  Original results from CE6.4.3 and CE6.4.6a were in general on par with the CE1 anchors, bit better in some areas, bit worse in other areas
  Coding results with “anchor HM” were clearly better than with HM-16.7 and better than the CE1 anchors in some areas (more detailed textures, wires)
Some examples are shown on the following slides

## Slide 13
Anchor rate3

## Slide 14
CE6.4.3 HM-16.7 rate3

## Slide 15
CE6.4.3 V2 (HM anchor) rate3
Much more detail in wall and parasol

## Slide 16
Anchor rate3

## Slide 17
CE6.4.3 HM-16.7 rate3

## Slide 18
CE6.4.3 V2 (HM anchor) rate3
Better reconstruction of powerlines

## Slide 19
Anchor rate3

## Slide 20
CE6.4.3 HM-16.7 rate3

## Slide 21
CE6.4.3 V2 (HM anchor) rate3
Much better reconstruction of rope

## Slide 22
Anchor rate3

## Slide 23
CE6.4.3 HM-16.7 rate3

## Slide 24
CE6.4.3 V2 (HM anchor) rate3
Much better reconstruction of details: rope, light poles and red line on track