## Slide 1
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University, Taiwan
Centralized Texture-Depth Packing
SEI Message for HEVC and AVC
(Revisions of JCTVC-Y0024 and Y0025)

## Slide 2: Contents
Revisions of Previous SEI Message Syntax
Centralized Texture-Depth Packing Formats
Revisions of Figures and Formulations
Conclusions
More Experimental Results
Progress of Adoption Plan

## Slide 3: Centralized Texture-Depth Packing SEI Message Syntax

## Slide 4: CTDP SEI Syntax (JCT3V-Y0024)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
centralized_texture_depth_packing_type | u(3)
quarter_depth_size | u(12)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_sample_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 5: CTDP SEI Syntax (JCT3V-AA0025)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
large_depth_type | u(1)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 6: ctdp_packing_type
CTDP-TB
CTDP-LR
Value | Interpretation
0 | Indicates the frame of the CTDP-TB type with an arrangement of subsample color depth top (SCDT), related texture (RT), and subsample color depth bottom (SCDB) regions from top to bottom, as illustrated in Figure D‑X1.
1 | Indicates the frame of the CTDP-LR type with an arrangement of subsample color depth left (SCDL), related texture (RT), and subsample color depth right (SCDR) regions from left to right, as illustrated in Figure D‑X2.
Removed 2-view & 2-depth CTDP formats

## Slide 7
large_depth_type equal to 1 indicates the depth information utilizes more color depth lines to carry depth map.
large_depth_type equal to 0 indicates the depth information utilizes less color depth lines to carry depth map.
When ctdp_packing_type is not equal to 0 or 1, large_depth_type is ignored and reserved for future use by ITU-T | ISO/IEC.
large_depth_type

## Slide 8: Centralized Texture-Depth Packing (CTDP) Formats
Simplify CTDP Formats:
  ctdp_packing_type (TB or LR)
  large_depth_type (large or small depth regions)

## Slide 9: CTDP- Top and Bottom (TB) Packing Procedure
Vertical Splitting
& Flipping
Spatial Subsample in
Vertical Direction
Vertical Subsample or
Original Texture Frame
Combination
H
H
Subsample
to Emulated YCbCr
HHD
HST
HRT
HHD
HHD
HHD
2HHD
6HHD
w
w
w
w
w
w
w
w

## Slide 10: CTDP Left and Right (LR) Packing Procedure
Horizontal Splitting
& Flipping
Spatial Subsample in
Horizontal Direction
Horizontal Subsample or
Original Texture Frame
Combination
W
W
Subsample to
Emulated YCbCr
2WHD
WHD
WRT
WHD
WRT
WHD
WHD
6WHD
H
H
H
H
H
H
H
H

## Slide 11: CTDP Formats for HD Video (1920x1080)
CTDP-TB, depth=1/6
CTDP-LR, depth=1/6
CTDP Formats (large depth):
CTDP Formats (small depth) :
CTDP-TB, depth=1/9
CTDP-LR, depth=1/12

## Slide 12
ctdp_packing_type =0
CTDP-TB

## Slide 13
CTDP-LR
Ctdp_packing_type =1

## Slide 14: Revisions of Figures and Formulations

## Slide 15: Positioning of YCbCr Components of Subsample Color Depth (SCD) ctdp_packing_type=0

## Slide 16: Emulated YCbCr to Depth Value Mapping ctdp_packing_type=0
D(3i, j) = (19078* ((Y(i, j) − 16) + 213) / 214, (D-X5)
D(3i+1, j+1) = (19078 * (Y(i, j+1) − 16) + 213) / 214, (D-X6)
D(3i+4, j) = (19078 * (Y(i+1, j) − 16) + 213) / 214, (D-X7)
D(3i+5, j+1) = (19078 * ((Y(i+1, j+1) − 16) + 213) / 214, (D-X8)
D(3i+2, j)= f(Cb(i, j), D(3i, j), D(3i+4,j)), (D-X9)
D(3i+3, j+1) = f(Cr(i, j), D(3i+1,j+1), D(3i+5, j+1))) (D-X10)
Linear Mapping for Y components in PCM Approach:
Piecewise Linear Mapping for Cb/Cr components in DPCM Approach:

## Slide 17: Linear Mapping of Y components
In PCM approach, four Y components are linearly mapped to four selected depth values.
0
Y
D
16
235
255
255
235
Slope=0.8588
Y= [16, 235]
D= [0, 255]
Y = 0.8588 * D + 16
D = 1.1644 (Y – 16)
D = (11644* (Y – 16) + 50000)/100000
D = (19078* (Y – 16) + 213)/214
New Revision:
in JCTVC-Y0024

## Slide 18: Cb/Cr to Depth Value Conversion
In DPCM approach, Cb/Cr component is mapped to the residual of the selected depth values with the prediction, which is the average of D and E.
Cb/Cr=[16, 240]
DD =[-255, 255]
Cb, Cr
DD
16
240
255
255
235
-255
0
128
5
-5
1/Slope’=2.3364
Slope’=1
133
123
1/Slope’=2.3364
New Revision:
in JCTVC-Y0024

## Slide 19: TB, Depth-1/9, Compatible CTDP Video
If need demo video, please inform:
jefyang@mail.ncku.edu.tw

## Slide 20: Positioning of YCbCr Components of Subsample Color Depth (SCD) ctdp_packing_type=1

## Slide 21: Emulated YCbCr to Depth Value Mapping ctdp_packing_type=1
D(i, 3j) = (19078* ((Y(i, j) − 16) + 213) / 214, (D-X12)
D(i+1, 3j+1) = (19078 * (Y(i+1, j) − 16) + 213) / 214, (D-X13)
D(i, 3j+4) = (19078 * (Y(i, j+1) − 16) + 213) / 214, (D-X14)
D(i+1, 3j+5) = (19078 * ((Y(i+1, j+1) − 16) + 213) / 214, (D-X15)
D(i, 3j+2) = f(Cb(i, j), D(i, 3j), D(i, 3j+4)), (D-X16)
D(i+1, 3j+3) = f(Cr(i, j), D(i+1, 3j+1), D(i+1, 3j+5))), (D-X17)
Linear Mapping for Y components in PCM Approach:
Piecewise Linear Mapping for Cb/Cr components in DPCM Approach:

## Slide 22: LR, Depth-1/12, Compatible CTDP Video
If need demo video, please inform:
jefyang@mail.ncku.edu.tw

## Slide 23: Depth Parameters Related to this CTDP SEI Syntax (Copied from 3D-HEVC)

## Slide 24: Depth Parameter Related Flags
baseline_dist_flag equal to 0 specifies that the syntax elements specifying the baseline distance are not present in the syntax structure. baseline_dist_flag equal to 1 specifies that the syntax elements specifying the baseline distance value are present in the syntax structure.
focal_length_flag equal to 0 specifies that the syntax elements specifying the focal length are not present in the syntax structure. focal_length_pixel_flag equal to 1 specifies that the syntax elements specifying the focal length value are present in the syntax structure.
z_near_flag equal to 0 specifies that the syntax elements specifying the nearest depth value are not present in the syntax structure. z_near_flag equal to 1 specifies that the syntax elements specifying the nearest depth value are present in the syntax structure.
z_far_flag equal to 0 specifies that the syntax elements specifying the farthest depth value are not present in the syntax structure. z_far_flag equal to 1 specifies that the syntax elements specifying the farthest depth value are present in the syntax structure.
d_min_flag equal to 0 specifies that the syntax elements specifying the minimum disparity value are not present in the syntax structure. d_min_flag equal to 1 specifies that the syntax elements specifying the minimum disparity value are present in the syntax structure.
d_max_flag equal to 0 specifies that the syntax elements specifying the maximum disparity value are not present in the syntax structure. d_max_flag equal to 1 specifies that the syntax elements specifying the maximum disparity value are present in the syntax structure.

## Slide 25: depth_representation_type
Value | Interpretation
0 | Each decoded luma sample value of an auxiliary picture represents an inverse of Z value that is uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 represents the inverse of ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents the inverse of ZNear (specified below).
1 | Each decoded luma sample value of an auxiliary picture represents disparity that is uniformly quantized into the range of 0 to maxVal, inclusive. When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
2 | Each decoded luma sample value of an auxiliary picture represents a Z value uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 corresponds to ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents ZNear (specified below).
3 | Each decoded luma sample value of an auxiliary picture represents a nonlinearly mapped disparity, normalized in range from 0 to maxVal, as specified by depth_nonlinear_representation_num_minus1 and depth_nonlinear_representation_model[i].When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
Other values | Reserved for future use
The variable maxVal is set equal to ( 1 << ( 8 + bit_depth_luma_minus8 ) ) − 1, where bit_depth_luma_minus8 is the value included in or inferred for the active SPS of the layer with nuh_layer_id equal to targetLayerId.
depth_representation_type specifies the representation definition of decoded luma samples of auxiliary pictures. In the table, disparity specifies the horizontal displacement between two texture views and Z value specifies the distance from a camera.

## Slide 26: View synthesis representation information element syntax
The syntax structure specifies the value of an element in the view synthesis representation information SEI message.
The syntax structure sets the values of the OutSign, OutExp, OutMantissa and OutManLen variables that represent a floating-point value. When the syntax structure is included in another syntax structure, the variable names OutSign, OutExp, OutMantissa and OutManLen are to be interpreted as being replaced by the variable names used when the syntax structure is included.
da_sign_flag equal to 0 indicates that the sign of the floating-point value is positive. da_sign_flag equal to 1 indicates that the sign is negative. The variable OutSign is set equal to da_sign_flag.
da_exponent specifies the exponent of the floating-point value. The value of da_exponent shall be in the range of 0 to 27 − 2, inclusive. The value 27 − 1 is reserved for future use by ITU-T | ISO/IEC. Decoders shall treat the value 27 − 1 as indicating an unspecified value. The variable OutExp is set equal to da_exponent.
da_mantissa_len_minus1 plus 1 specifies the number of bits in the da_mantissa syntax element. The value of da_mantissa_len_minus1 shall be in the range of 0 to 31, inclusive. The variable OutManLen is set equal to da_mantissa_len_minus1 + 1.
da_mantissa specifies the mantissa of the floating-point value. The variable OutMantissa is set equal to da_mantissa.
view_syn_rep_info_element( OutSign, OutExp, OutMantissa, OutManLen ) { | Descriptor
da_sign_flag | u(1)
da_exponent | u(7)
da_mantissa_len_minus1 | u(5)
da_mantissa | u(v)
} | 

## Slide 27: Association between depth parameter variables and syntax elements
x | s | e | n | v
Bdistance | BdistanceSign | BdistanceExp | BdistanceMantissa | BdistanceManLen
Flength | FlengthSign | FlengthExp | FlengthMantissa | FlengthManLen
ZNear | ZNearSign | ZNearExp | ZNearMantissa | ZNearManLen
ZFar | ZFarSign | ZFarExp | ZFarMantissa | ZFarManLen
DMax | DMaxSign | DMaxExp | DMaxMantissa | DMaxManLen
DMin | DMinSign | DMinExp | DMinMantissa | DMinManLen
The variables in the x column of table are derived from the respective variables in the s, e, n and v columns as follows:
– If the value of e is in the range of 0 to 127, exclusive, x is set equal to ( −1 )s* 2e - 31 * ( 1 + n ÷ 2v ).
– Otherwise (e is equal to 0), x is set equal to ( −1 )s * 2−( 30 + v ) * n.
The DMin and DMax values, when present, are specified in units of a luma sample width of the coded picture.
The units for the ZNear and ZFar, when present, are identical but unspecified.
When depth_representation_type is equal to 0 or 2, the disparity D can further be obtained from the value of Z, Bdistance, and Flength, where D = Bdistance × Flength ÷ Z

## Slide 28: Other Syntax Elements
depth_nonlinear_representation_num_minus1 plus 2 specifies the number of piecewise linear segments for mapping of depth values to a scale that is uniformly quantized in terms of disparity.
depth_nonlinear_representation_model[ i ] for i ranging from 0 to depth_nonlinear_representation_num_minus1 + 2, inclusive, specify the piecewise linear segments for mapping of decoded luma sample values of an auxiliary picture to a scale that is uniformly quantized in terms of disparity. The values of depth_nonlinear_representation_model[0] and depth_nonlinear_representation_model[ depth_nonlinear_representation_num_minus1 + 2 ] are both inferred to be equal to 0.
centralized_texture_depth_packing_persistence_flag specifies the persistence of the centralized texture-depth packing arrangement SEI message.
centralized_texture-depth_packing_persistence_flag equal to 0 specifies that the centralized texture-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_texture-depth_packing_persistence_flag equal to 1 specifies that the centralized texture-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
– A new CVS begins.
– The bitstream ends.
– A frame in an access unit containing a centralized texture-depth packing SEI message with the same

## Slide 29: Conclusions

## Slide 30: Conclusions
In this document, the variations of CTDP formats have been reduced to 8 formats, which will help to simplify realization of the system. (completed)
In this document, the figures and formulations have been revised to clearly explain the details. (completed)
In Taiwan, the CTDP formats starting from March 15, 2017 have been adopted by HYA Company to deliver the 3D television services in CATV systems. (completed)
In Taiwan, the CTDP formats will be adopted by Public Television Services (PTS) in Terrestrial TV broadcasting system for delivery of 3D 4K television services (In progress)

## Slide 31: Performance evaluations for some CTDP parameter: 1. Uncompressed CTDP Performance (Compare to Ground True Values) 2. HEVC-Coded CTDP Performance (Compare to 3D-HEVC Results)

## Slide 32
Sequences | Clipped Resolution | Frames | 1 View | Synthesized View
Undo Dancer | 1920×1080 | 250 | 3 | 4
Shark | 1920×1080 | 300 | 5 | 7
Computer Generated Test Sequences

## Slide 33: Experimental Settings
Uncoded and Coded HD Computer Generated Videos:
ratios of depth region :
CTDP TB: Depth-1/6 (large) and 1/9 (small)
CTDP LR: Depth-1/6 (large) and 1/12 (small)
HEVC-CTDP Coding Parameters:
encoding mode: All Intra, Low delay, Random access
QP: 27,32,37,42
ctdp_packing_type: CTDP-TB and CTDP-LR
Frame_compatible_type: compatible or incompatible
image resizing: Lancos 4
  depth resizing: bicubic
  depth spatial flipping: flipped/unflipped (syntax set to fipped)

## Slide 34
Uncoded CTDP Performances
CTDP depacked texture, depth, and synthesized view are compared to ground truth ones

## Slide 35
Objective Performances of Uncoded CTDP Formats
Performances | Depacked Texture and Depth |  |  |  | Synthesized Virtual View Generated by VSRS | 
 | DepackedTexture |  | Depacked Depth |  |  | 
 | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB
PSNR | 45.2634 | 46.1485 | 45.4699 | 44.1021 | 38.7427 | 38.8875
SSIM | 0.9922 | 0.9938 | 0.9939 | 0.9918 | 0.9846 | 0.9867
Performances | Depacked Texture and Depth |  |  |  | Synthesized Virtual View Generated by VSRS | 
 | Depacked Texture |  | Depacked Depth |  |  | 
 | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR
PSNR | 47.0243 | 49.2137 | 42.7756 | 39.8881 | 39.3348 | 38.2884
SSIM | 0.9932 | 0.9958 | 0.9929 | 0.9873 | 0.9878 | 0.9882
ctdp_packing_type = 0
ctdp_packing_type = 1

## Slide 36
HEVC-coded CTDP Performances
TB and LR Formats
CTDP-HEVC decoded and depacked texture, depth, and synthesized view are compared to 3D-HEVC decoded ones

## Slide 37
HEVC-coded CTDP-TB Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB
ra | 18.6241 | 13.6254 | -47.7598 | -30.6426 | 21.1467 | 25.7829
ldp | 13.8604 | 8.2266 | -62.3414 | -53.8872 | 11.8604 | 13.9024
ai | 9.7019 | 6.8931 | -39.1668 | -19.7578 | 23.9325 | 29.2954
ave | 14.0621 | 9.5817 | -49.7560 | -34.7625 | 18.9799 | 22.9936
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB | D-1/6 TB | D-1/9 TB
ra | -0.5694 | -0.4247 | 2.6245 | 1.3941 | -0.5769 | -0.6789
ldp | -0.4383 | -0.2707 | 4.7799 | 3.6932 | -0.3570 | -0.4051
ai | -0.3558 | -0.2557 | 2.2510 | 0.8799 | -0.7368 | -0.8694
ave | -0.4545 | -0.3170 | 3.2184 | 1.9902 | -0.5569 | -0.6511

## Slide 38
HEVC-coded CTDP-LR Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR
ra | 16.8323 | 11.7019 | -29.8353 | 26.5047 | 33.4633 | 67.8342
ldp | 12.6704 | 6.9614 | -56.4556 | -30.2637 | 18.8112 | 42.2946
ai | 7.3734 | 3.7328 | -23.1159 | 27.8123 | 35.3507 | 69.7477
ave | 12.2920 | 7.4653 | -36.4689 | 8.0178 | 29.2084 | 59.9588
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR | D-1/6 LR | D-1/12 LR
ra | -0.5064 | -0.3560 | 1.2864 | -1.0712 | -0.8184 | -1.3992
ldp | -0.3956 | -0.2231 | 3.7330 | 1.3046 | -0.5205 | -1.0077
ai | -0.2682 | -0.1370 | 0.9327 | -1.6007 | -0.9764 | -1.6165
ave | -0.3900 | -0.2387 | 1.9840 | -0.4558 | -0.7718 | -1.3411

## Slide 39
HEVC-coded CTDP Performances:
Depth Flipped and Unflipped
CTDP-HEVC decoded and depacked texture, depth, and synthesized view are compared to 3D-HEVC decoded ones

## Slide 40
Advantages of Flipped Depth Regions
Advantages of Flipped Depth Regions:
To achieve more comfortable visualization in 2D display.
To get better lineup for the subsample color depth and texture object
To avoid serious distortions in sensitive regions between texture and depth boundary.
With Flipped Depth Regions
Without Flipped Depth Regions

## Slide 41
HEVC-coded D-1/9 CTDP-TB Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | With Flipping | Without Flipping | With Flipping | Without Flipping | With Flipping | Without Flipping
ra | 13.6254 | 13.9349 | -30.6426 | -30.9876 | 25.7829 | 26.6110
ldp | 8.2266 | 8.5855 | -53.8872 | -54.0313 | 13.9024 | 14.3549
ai | 6.8931 | 7.0228 | -19.7578 | -19.7109 | 29.2954 | 30.1457
ave | 9.5817 | 9.8477 | -34.7625 | -34.9099 | 22.9936 | 23.7038
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | With Flipping | Without Flipping | With Flipping | Without Flipping | With Flipping | Without Flipping
ra | -0.4247 | -0.4340 | 1.3941 | 1.4114 | -0.6789 | -0.6964
ldp | -0.2707 | -0.2809 | 3.6932 | 3.7246 | -0.4051 | -0.4156
ai | -0.2557 | -0.2608 | 0.8799 | 0.8759 | -0.8694 | -0.8890
ave | -0.3170 | -0.3252 | 1.9902 | 2.0039 | -0.6511 | -0.6670

## Slide 42
HEVC-coded D-1/12 CTDP-LR Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | With Flipping | Without Flipping | With Flipping | Without Flipping | With Flipping | Without Flipping
ra | 11.7019 | 11.9281 | 26.5047 | 25.6331 | 67.8342 | 69.3347
ldp | 6.9614 | 7.2027 | -30.2637 | -30.0011 | 42.2946 | 42.3245
ai | 3.7328 | 3.7884 | 27.8123 | 28.0876 | 69.7477 | 69.0859
ave | 7.4653 | 7.6397 | 8.0178 | 7.9065 | 59.9588 | 60.2483
Coding Modes | Depacked Texture |  | Depacked Depth |  | Virtual View by VSRS | 
 | With Flipping | Without Flipping | With Flipping | Without Flipping | With Flipping | Without Flipping
ra | -0.3560 | -0.3629 | -1.0712 | -1.0792 | -1.3992 | -1.4227
ldp | -0.2231 | -0.2308 | 1.3046 | 1.2856 | -1.0077 | -1.0004
ai | -0.1370 | -0.1390 | -1.6007 | -1.6086 | -1.6165 | -1.6128
ave | -0.2387 | -0.2442 | -0.4558 | -0.4674 | -1.3411 | -1.3453

## Slide 43: Adoption Plan in Taiwan
Hsin Yeong An (HYA) Cable TV Company
Public Television Services

## Slide 44: Adoption Test Plan
The National Cheng Kung University and the Hsin Yeong An (HYA) Cable TV Company have signed Memorandum of Understanding (MOU) to adopt the CTDP formats to delivering 3D TV programs in HYA Broadcasting Systems. The test and adoption plan is divided into five stages and designed as:
1. Jan. 15, 2017: Complete MOU signing (completed)
2. Mar. 15, 2017: Propose and confirm the test and adoption detailed plans (completed)
3. Dec. 15, 2017: Test of downloaded 3D CTDP services with computer clients (in progress)
4. Aug. 15, 2018: Deliver 3D CATV services in a remote server and set-top-box with CTDP separate module.
5. Aug.15, 2019: Deliver 3D CATV services through Set-top-Boxes with Integrated CTDP depacking module (open to all users and charged 3D TV services)

## Slide 45: Simplified English MOE (signed)

## Slide 46: Test Plan for Headend

## Slide 47: Test Plan in STB Side

## Slide 48: Cooperated with Public Television Services
Public Television Service Foundation (PTS) visited the National Cheng Kung University on March 31, 2017 for discussion the future advanced broadcasting services. Both sides agreed with following conclusions as:
PTS should deliver advanced TV services such as 4K TV and 3D TV services.
PTS will provide the existing 2D and 3D television programs for the NCKU for testing the CTDP format 3D video services. The format conversion as well as the depth extraction will be performed by the NCKU team.
PTS will be interested in CTDP 3D formats, which can cover wide range of the audiences even they don’t have 3D displays.
PTS will sign the MOU with the NCKU as the HYA Cable Company to delivery of 3D 4K television in Terrestrial TV broadcasting systems in the near future.