## Slide 1: Support modification for parallel calculation of significant map contexts JCTVC-H0427
Vadim Seregin, Joel Sole and Marta Karczewicz

## Slide 2: Significance map context modeling in HM5.0
5-point neighborhood support (template) is used for TU > 8x8
Coefficient below current one is not used for coefficients (0, 0) and
(4, 3) in every 4x4 sub-block
  Achieves 2 contexts estimation in parallel

## Slide 3: Goal
In this contribution, throughput increase to 3 and 4 bins in parallel is studied
Three methods are analyzed
  Extending of skipping coefficients from the support
  Grouping the significance map, allowing inter-group reference
  Support modification, applied for all coefficients

## Slide 4: Extending of skipping coefficients from the support
Previous 3 (or 4) coefficients in the scan order are not used in significance map context calculation
  As a disadvantage, number of conditions to be checked to every coefficient are increased
  In general, a condition should be checked at every color point
  Support for 3 and 4 bins in parallel
Case 3 contexts in parallel:

## Slide 5: Grouping the significance map
Group significance map in groups of 3 (or 4) coefficients
Significance flags in each group might be processed in parallel
Inter-group reference for context modeling allowed
  Advantage: less number of conditions to be checked
3 contexts in parallel:

## Slide 6: Support modification applied to all positions
Support (template) is modified for significance map
  To incorporate most frequent conditions
New support applied to all coefficients
Number of conditions to be checked equal to HM5.0
3 contexts in :parallel

## Slide 7: Experimental results
 | AI-HE | AI-LC | RA-HE | RA-LC | RA-HE10 | HE-LB | LC-LB
Method 1 (3 bins) | 0.09 | 0.07 | 0.06 | 0.05 | 0.14 | 0.06 | 0.02
Method 1 (4 bins) | 0.11 | 0.09 | 0.08 | 0.07 | 0.16 | 0.05 | 0.05
Method 2 (3 bins) | 0.01 | 0.01 | 0.00 | 0.02 | 0.04 | 0.01 | 0.00
Method 2 (4 bins) | 0.12 | 0.09 | 0.09 | 0.08 | 0.16 | 0.07 | 0.02
Method 3 (3 bins) | 0.11 | 0.06 | 0.08 | 0.05 | 0.16 | 0.10 | 0.04
Method 3 (4 bins) | 0.21 | 0.12 | 0.17 | 0.11 | 0.25 | 0.22 | 0.07
Using common conditions (enc/dec times similar to anchor)
Cross-check: LGE (JCTVC-H0663)

## Slide 8: Conclusion
Throughput of significance map increased to 3 (and 4) bins in parallel
Methods 2 and 3 has less number of conditions to be checked
Recommend to adopt method 3 as more flexible with less number of conditions per coefficient

## Slide 9
Thank you!

## Slide 10: Extending of skipping coefficients from the support
4 coefficients in parallel:

## Slide 11: Grouping the significance map
Group of 4 coefficients:
4 contexts in parallel

## Slide 12: Support modification applied to all positions
4 parallel context calculation: