## Slide 1: Non-CE1: SAO syntax relocation for interleaving mode (JCTVC-I0292)
JCT-VC 9th Meeting in Geneva, CH, 27 April – 7 May 2012
Yukinobu Yasugi, Tomohiro Ikai
SHARP Corporation

## Slide 2: Overall summary
Motivation
  To make the order of SAO unit and coding tree in a bitstream the same as that of compression process
Proposal : relocate SAO unit syntax elements to the end of coding_tree
  improvement in encoder design
Experimental result
  BD-rate Performance was not changed
  Cross-checked results are provided by MediaTek (JCTVC-I0210)

## Slide 3: Proposal
SAO unit syntax in HM-6.0
  the order of compression process: compress CU  SAO process
  however, the order in the bitstream differ.
Proposal
  Relocate SAO unit syntax elements to the end of coding_tree (before end_of_slice_flag)
Advantages
  simplification of encoder process/design
SAOu 0
LCU 0
bitstream
SAOu 1
LCU 1
SAOu 2
LCU 2
SAOu 0
LCU 0
bitstream
SAOu 1
LCU 1
SAOu 2
LCU 2

## Slide 4: Original syntax (HM-6.0)
slice_data( ) {
...
do {
...
if( slice_sao_interleaving_flag ) {
if(slice_sample_adaptive_offset_flag)
sao_unit_cabac( xCtb, yCtb, 0 )
if(sao_cb_enable_flag)
sao_unit_cabac( xCtb, yCtb, 1 )
if(sao_cr_enable_flag)
sao_unit_cabac( xCtb, yCtb, 2 )
}
moreDataFlag = coding_tree( xCtb, yCtb, Log2CtbSize, 0 )
...
} while( moreDataFlag )
}
coding_tree( x0, y0, log2CbSize, cbDepth ) {
...
if( split_coding_unit_flag[ x0 ][ y0 ] ) {
...
} else {
if(adaptive_loop_filter_flag && alf_cu_control_flag )
AlfCuFlag[ x0 ][ y0 ] = alf_cu_flag[ AlfCuFlagIdx ]
if( NumPCMBlock = = 0 )
coding_unit( x0, y0, log2CbSize )
else
pcm_sample( x0, y0, log2CbSize )
if( !(( x0 + 1 << log2CbSize ) % ( 1 << SliceGranularity )) && !(( y0 + 1 << log2CbSize ) % ( 1 << SliceGranularity )) && NumPCMBlock = = 0 ) {
end_of_slice_flag
moreDataFlag = !end_of_slice_flag
} else
moreDataFlag = 1
}
return moreDataFlag
}
SAO units

## Slide 5: Proposed syntax
slice_data( ) {
...
do {
...
moreDataFlag = coding_tree( xCtb, yCtb, Log2CtbSize, 0 )
...
} while( moreDataFlag )
}
coding_tree( x0, y0, log2CbSize, cbDepth ) {
...
if( split_coding_unit_flag[ x0 ][ y0 ] ) {
...
} else {
if(adaptive_loop_filter_flag && alf_cu_control_flag )
AlfCuFlag[ x0 ][ y0 ] = alf_cu_flag[ AlfCuFlagIdx ]
if( NumPCMBlock = = 0 )
coding_unit( x0, y0, log2CbSize )
else
pcm_sample( x0, y0, log2CbSize )
if( !( ( x0 + 1 << log2CbSize ) % CtbSize ) && !( ( y0 + 1 << log2CbSize ) % CtbSize ) && NumPCMBlock = = 0 ) {
if( slice_sao_interleaving_flag ) {
if(slice_sample_adaptive_offset_flag)
sao_unit_cabac( xCtb, yCtb, 0 )
if(sao_cb_enable_flag)
sao_unit_cabac( xCtb, yCtb, 1 )
if(sao_cr_enable_flag)
sao_unit_cabac( xCtb, yCtb, 2 )
}
if( !(( x0 + 1 << log2CbSize ) % ( 1 << SliceGranularity )) && !(( y0 + 1 << log2CbSize ) % ( 1 << SliceGranularity )) && NumPCMBlock = = 0 ) {
end_of_slice_flag
moreDataFlag = !end_of_slice_flag
} else
moreDataFlag = 1
}
return moreDataFlag
}
SAO units

## Slide 6: Experimental result
BD-rate: 0.0 % for all tests
Runtime: no significant difference * This simulations were carried out on a PC cruster environment

## Slide 7: Conclusion
Motivation
  To make the order of SAO unit and coding tree in a bitstream the same as that of compression process
Proposal : relocate SAO unit syntax elements to the end of coding_tree
  improvement in encoder design
Experimental result
  BD-rate Performance was not changed
  Cross-checked results [JCTVC-I0210] are provided by MediaTek (Thanks to MediaTek)