## Slide 1: AHG6: Transform Dependent Deblocking Strength
Geert Van der Auwera, Rajan Joshi, Marta Karczewicz

## Slide 2: Summary
Certain video content suffers from severe blocking artifacts that are transform size dependent and are particularly visible for the maximum transform size.
The maximum TU size is encoder implementation dependent and, therefore, it is important that the HEVC deblocking filter process is flexible and general enough to reduce this type of blocking artifacts.
This contribution proposes to signal specific deblocking adjustment parameters to control the deblocking strength in case that at least one of two adjacent video blocks P and Q is included in a TU of maximum size.
The advantage of this method is not only applying stronger deblocking filtering to the edges of the TUs of maximum size, but more importantly, this method avoids oversmoothing in picture areas that are unaffected by these largest blocking artifacts.
This contribution also proposes a stronger β threshold curve with increased β values outside of the QP range of the common test conditions (>41), but within the QP range of the current HM7 curve.
The advantage is that the deblocking strength can be further increased beyond the HM7 strength without increasing the number of values to be stored in memory.
Visual quality examples illustrate the reduction of the blocking artifacts originating from the maximum TU sizes.

## Slide 3: Examples of 32x32 Blocking Artifacts
Frame 1 (cropped) of the “Riverbed” sequence demonstrating strong 32x32 blocking artifacts.

## Slide 4: Examples of 32x32 Blocking Artifacts
Frame 1 (cropped) of the “WestWindEasy” sequence demonstrating strong 32x32 blocking artifacts.

## Slide 5: Examples of 16x16 Blocking Artifacts
Frame 1 (cropped) of the “Riverbed” sequence demonstrating strong 16x16 blocking artifacts.

## Slide 6: Examples of 16x16 Blocking Artifacts
Frame 1 (cropped) of the “WestWindEasy” sequence demonstrating strong 16x16 blocking artifacts.

## Slide 7: Examples of 8x8 Blocking Artifacts
Frame 1 (cropped) of the “Riverbed” sequence demonstrating strong 8x8 blocking artifacts.

## Slide 8: Examples of 8x8 Blocking Artifacts
Frame 1 (cropped) of the “WestWindEasy” sequence demonstrating strong 8x8 blocking artifacts.

## Slide 9: Deblocking Strength Adjustment for Max TU Size Edges
It is proposed to signal specific deblocking adjustment parameters for offsetting tC and β deblocking thresholds to control the deblocking strength
  if at least one of two adjacent video blocks P and Q is included in a transform unit with the maximum transform size
    pps_beta_offset_max_tu / slice_header_beta_offset_max_tu
    pps_tc_offset_max_tu_div2 / slice_header_tc_offset_max_tu_div2
  otherwise, if neither video block P or Q is included in a maximum sized transform unit, then the current deblocking adjustment parameters apply.
    pps_beta_offset_div2 / slice_header_beta_offset_div2
    pps_tc_offset_div2 / slice_header_tc_offset_div2
Flag is signalled to enable the signalling of the additional offset parameters:
    deblocking_max_tu_offset_enabled_flag

## Slide 10: Beta Threshold Curve for Increased Deblocking Strength
Curves with various slopes (4, 8, 12, 16) to modify β-curve values beyond the QP value 41 (beyond HM test conditions)
Strongest curve with slope 16 (prop4) is employed for testing

## Slide 11: Test Conditions
Sequences:
  “Riverbed”
  “DucksTakeOff”
  “WestWindEasy”
  “ChinaSpeed” (class F)
LD-B-main @ QP 32 / 37 / 41
Reference: maximum HM7 deblocking strength for all edges
  Deblocking config parameters:
    LoopFilterBetaOffset_div2 : 13 # Range: -13 ~ 13
    LoopFilterTcOffset_div2 : 13 # Range: -13 ~ 13
Test: maximum deblocking strength for max TU edges (prop4 β-curve)
  Deblocking config parameters:
    LoopFilterBetaOffset_div2 : 0 # Range: -13 ~ 13
    LoopFilterTcOffset_div2 : 0 # Range: -13 ~ 13
    LoopFilterOffsetMaxTUEnabled : 1 # Enable max TU offsets
    LoopFilterBetaOffsetMaxTU : 26 # Range: -26 ~ 26
    LoopFilterTcOffsetMaxTUDiv2 : 13 # Range: -13 ~ 13
  Max TU size configuration
    QuadtreeTULog2MaxSize : 5 / 4 / 3

## Slide 12: Visual Quality Examples
“Riverbed” sequence (Max TU 32x32; QP 37): Reference (cropped frame 1)

## Slide 13: Visual Quality Examples
“Riverbed” sequence (Max TU 32x32; QP 37): Test

## Slide 14: Visual Quality Examples
    “Riverbed” sequence (Max TU 16x16; QP 37): Reference

## Slide 15: Visual Quality Examples
    “Riverbed” sequence (Max TU 16x16; QP 37): Test

## Slide 16: Visual Quality Examples
    “WestWindEasy” sequence (Max TU 32x32; QP 37): Reference

## Slide 17: Visual Quality Examples
    “WestWindEasy” sequence (Max TU 32x32; QP 37): Test

## Slide 18: Visual Quality Examples
    “WestWindEasy” sequence (Max TU 16x16; QP 37): Reference

## Slide 19: Visual Quality Examples
    “WestWindEasy” sequence (Max TU 16x16; QP 37): Test

## Slide 20: Conclusion
The advantage of the proposed technique is that the large blocking artifacts that occur in certain content types can be effectively reduced by specifically increasing deblocking filter strength for the edges of the maximum sized TUs, while avoiding oversmoothing of other picture areas.
It is suggested to adopt technique into the HEVC DIS.