## Slide 1: Fixed Upsampling Filters
JCTVC-L0199
Presented by Shan Liu
12th JCT Meeting in Geneva
14-23 January 2013
Zhenzhong Chen, Shan Liu, and Shawmin Lei

## Slide 2: Upsampling Filters
Inter/Intra
Prediction
Interlayer
Prediction
-
Prediction
T/Q
IT/IQ
Reconstruction
Entropy
Coding
T/Q Residues
Inter/intra
Prediction
-
Prediction
T/Q
IT/IQ
Reconstruction
Entropy
Coding
T/Q Residues
In-loop Filter
In-loop Filter
Mode Decision
Mode Decision
Multiplex
Scalable bitstream
Entropy
Coding
Up-sampling
Base layer information
Enhancement Layer
Spatial
decimation
Base Layer
Input

## Slide 3: Upsampling Filters
2D separable DCT based upsampling filters
  Sum of coefficients is 128, i.e., 7-bit precision.
  Coefficients derived according to the phase shift downsampling method.
  8-Tap filter for Luma
  4-Tap filter for Chroma
Phase | Filter coefficients
0 | { 0, 128, 0, 0},
1/4 | { -12, 111, 37, -8},
1/3 | { -12,100, 49, -9},
3/8 | { -12, 92, 56, -8},
1/2 | { -8, 72, 72, -8},
7/12 | { -11, 63, 91,-15},
2/3 | { -9, 49,100,-12},
7/8 | { -4, 20,116, -4},
11/12 | { -3, 11,124, -4}
Table 1 The 4-Tap up-sampling filter (7 Bits)
Phase | Filter coefficients
0 | { 0, 0, 0, 128, 0, 0, 0, 0},
1/3 | {-3, 9, -22, 105, 52, -18, 8, -3},
1/2 | { -2, 9,-23, 80, 80,-23, 9, -2},
2/3 | {-3, 8, -18, 52, 105, -22, 9, -3},
Table 2 The 8-Tap up-sampling filter (7 Bits)

## Slide 4: Results (Anchor: Simulcast)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -27.1% | -27.3% | -28.1% |  |  | 
Class B | -21.1% | -21.3% | -21.0% | -32.7% | -33.0% | -33.0%
Overall (EL+BL) | -22.8% | -23.0% | -23.1% | -32.7% | -33.0% | -33.0%
Overall (EL) | -34.8% | -35.3% | -35.5% | -58.3% | -58.3% | -58.4%
Enc Time[%] | 113.1% |  |  | 110.1% |  | 
Dec Time[%] | 104.7% |  |  | 105.4% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -18.5% | -7.9% | -9.3% |  |  | 
Class B | -15.5% | -9.2% | -7.8% | -26.2% | -20.4% | -18.8%
Overall (EL+BL) | -16.4% | -8.9% | -8.3% | -26.2% | -20.4% | -18.8%
Overall (EL) | -25.2% | -13.6% | -12.9% | -47.4% | -38.1% | -35.3%
Enc Time[%] | 108.0% |  |  | 109.8% |  | 
Dec Time[%] | 123.9% |  |  | 126.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -13.6% | -1.9% | -3.0% |  |  | 
Class B | -11.7% | -7.0% | -5.1% | -21.9% | -16.8% | -15.1%
Overall (EL+BL) | -12.3% | -5.5% | -4.5% | -21.9% | -16.8% | -15.1%
Overall (EL) | -19.6% | -8.6% | -7.2% | -40.7% | -31.9% | -28.8%
Enc Time[%] | 107.7% |  |  | 110.1% |  | 
Dec Time[%] | 128.8% |  |  | 135.6% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 5: TE1 Summary (Anchor: Simulcast)
Overall (EL+BL) | AI 2x |  |  | AI 1.5x |  |  | RA 2x |  |  | RA 1.5x |  |  | LDP 2x |  |  | LDP 1.5x |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 4.1 | -22.8% | -22.9% | -23.0% | -32.6% | -33.0% | -33.0% | -16.4% | -8.8% | -8.3% | -26.1% | -20.3% | -18.8% | -12.3% | -5.5% | -4.5% | -21.9% | -17.0% | -15.2%
Test 4.2 | -22.5% | -22.5% | -22.5% | -32.5% | -32.6% | -32.6% | -16.1% | -8.6% | -8.0% | -26.0% | -19.9% | -18.3% | -12.1% | -5.0% | -4.2% | -21.6% | -15.5% | -13.8%
Test 4.3 | -22.8% | -22.9% | -23.0% | -32.4% | -32.9% | -33.0% | -16.4% | -8.8% | -8.3% | -26.0% | -20.1% | -18.5% | -12.3% | -5.5% | -4.5% | -21.8% | -17.0% | -15.1%
TE4.3 (Chroma) | -22.8% | -22.9% | -23.0% | -32.6% | -33.0% | -33.0% | -16.4% | -8.8% | -8.3% | -26.1% | -20.3% | -18.7% | -12.3% | -5.5% | -4.5% | -21.9% | -17.1% | -15.2%
Test 4.4 | -22.7% | -22.8% | -22.9% | -32.6% | -33.0% | -33.1% | -16.3% | -8.7% | -8.2% | -26.1% | -20.3% | -18.8% | -12.2% | -5.4% | -4.4% | -21.9% | -17.0% | -15.3%
Test 4.5 | -22.8% | -22.9% | -23.0% | -32.4% | -32.7% | -32.7% | -16.4% | -8.8% | -8.3% | -25.9% | -20.1% | -18.6% | -12.3% | -5.5% | -4.5% | -21.7% | -16.5% | -14.7%
Test 4.2 (6 bit) | -22.7% | -22.7% | -22.8% | -32.6% | -32.7% | -32.7% | -16.3% | -8.6% | -8.0% | -26.1% | -20.0% | -18.4% | -12.2% | -5.1% | -4.1% | -21.7% | -15.7% | -13.9%
JCTVC-L0199 | -22.8% | -23.0% | -23.1% | -32.7% | -33.0% | -33.0% | -16.4% | -8.9% | -8.3% | -26.2% | -20.4% | -18.8% | -12.3% | -5.5% | -4.5% | -21.9% | -16.8% | -15.1%

## Slide 6: TE1 Summary (Anchor: SMuC0.1.1)
Based on Sumsung’s Crosscheck Results
Overall (EL+BL) | AI 2x |  |  | AI 1.5x |  |  | RA 2x |  |  | RA 1.5x |  |  | LDP 2x |  |  | LDP 1.5x |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Test 4.1 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Test 4.2 | 0.4% | 0.7% | 0.7% | 0.2% | 0.9% | 1.0% | 0.3% | 0.4% | 0.3% | 0.1% | 0.7% | 0.6% | 0.2% | 0.7% | 0.5% | 0.5% | 2.3% | 2.1%
Test 4.3 | 0.0% | 0.0% | 0.0% | 0.3% | 0.2% | 0.3% | 0.0% | 0.0% | 0.0% | 0.2% | 0.4% | 0.4% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1% | 0.2%
Test 4.4 | 0.1% | 0.2% | 0.2% | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | 0.2% | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | 0.3% | 0.0% | 0.0% | -0.1%
Test 4.5 | 0.1% | 0.2% | 0.2% | 0.3% | 0.5% | 0.5% | 0.0% | 0.1% | 0.2% | 0.5% | 0.2% | 0.1% | 0.0% | 0.1% | 0.3% | 0.4% | 0.7% | 0.7%
JCTVC-L0199 | 0.0% | -0.1% | -0.1% | -0.2% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.3% | 0.2%

## Slide 7: Conclusion
Results for DCT based upsampling filters with 7 bit precision are reported.
Results show that the proposed method out-performs other tools in TE.
Recommend to include the DCT based 7 bits precision upsampling filters in SHVC.

## Slide 8
www.mediatek.com