## Slide 1: AHG18: Modified scaling factor for transform-skip blocks to support higher bit depths greater than or equal to 14
Seung-Hwan Kim, Kiran Misra, Andrew Segall
(JCTVC-N0275)

## Slide 2: Organization
Background & Motivation
Problem Statement
Proposed Method
Results
Conclusions

## Slide 3: Background & Motivation
The current design is limited in supporting high fidelity coding for source bit depths greater than or equal to 14
Internal accuracy limitations in “transforms” was studied in JCTVC-M0178, where the following was noted:
  “From simulations, it has been observed that HEVC Range Extensions system is limited to about 90dB (for 14-bits source, 90dB is obtained when MSB is equal to 0.25)”
Here, we show that the fidelity achieved by the current “transform skip” design is similarly limited
Note, transform skip plays an important role at very low QP’s where it is used more frequently

## Slide 4: Problem Statement
Current Inverse transform skip process
  The output of the inverse transform skip process for dequantized coefficient values d[x][y] is determined based on the following equations
  r[ x ][ y ] = ( d[ x ][ y ] << 7 ) (8-267)
  bdShift = ( cIdx = = 0 ) ? 20 − BitDepthY : 20 − BitDepthC (8-268)
  r[ x ][ y ] = ( r[ x ][ y ] + ( 1 << ( bdShift − 1 ) ) ) >> bdShift (8-269)
If bdShift < 7, then precision loss occurs because LSB bits in r[ x ][ y ] are set to 0
Note, if source bit depth >= 14, then bdShift <=6 as a result a subset of LSB bits in r[ x ][ y ] are always set to 0

## Slide 5: Proposed Solution – Option 1
8.6.2 Scaling and transformation process
….
The (nTbS)x(nTbS) array of residual samples r is derived as follows:
If transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1, the residual sample array values r[ x ][ y ] with x = 0..nTbS − 1, y = 0..nTbS − 1 are derived as follows:
r[ x ][ y ] = ( d[ x ][ y ] << 7 ) (8‑267)
Otherwise (transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0), the transformation process for scaled transform coefficients as specified in subclause 8.6.4 is invoked with the transform block location ( xTbY, yTbY ), the size of the transform block nTbS, the colour component variable cIdx, and the (nTbS)x(nTbS) array of scaled transform coefficients d as inputs, and the output is an (nTbS)x(nTbS) array of residual samples r.
The variable bdShift is derived as follows:
bdShift = ( cIdx = = 0 ) ? 20 − BitDepthY : 20 − BitDepthC (8‑268)
When transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1, the value of bdShift is modified as follows:
bdShift = Max( 7, bdShift ) (8‑xxx)
The residual sample values r[ x ][ y ] with x = 0..nTbS − 1, y = 0..nTbS − 1 are modified as follows:
r[ x ][ y ] = ( r[ x ][ y ] + ( 1 << ( bdShift − 1 ) ) ) >> bdShift (8‑269)
…

## Slide 6: Proposed Solution – Option 2
8.6.2 Scaling and transformation process
...
The scaling process for transform coefficients as specified in subclause 8.6.3 is invoked with the transform block location ( xTbY, yTbY ), the size of the transform block nTbS, the colour component variable cIdx, and the quantization parameter qP as inputs, and the output is an (nTbS)x(nTbS) array of scaled transform coefficients d.
The variable bdShift is derived as follows:
bdShift = ( cIdx = = 0 ) ? 20 − BitDepthY : 20 − BitDepthC (8‑xxx)
The (nTbS)x(nTbS) array of residual samples r is derived as follows:
If transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1, the residual sample array values r[ x ][ y ] with x = 0..nTbS − 1, y = 0..nTbS − 1 are derived as follows:
r[ x ][ y ] = ( d[ x ][ y ] << Min( 7, bdShift ) ) (8‑xxx)
Otherwise (transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0), the transformation process for scaled transform coefficients as specified in subclause 8.6.4 is invoked with the transform block location ( xTbY, yTbY ), the size of the transform block nTbS, the colour component variable cIdx, and the (nTbS)x(nTbS) array of scaled transform coefficients d as inputs, and the output is an (nTbS)x(nTbS) array of residual samples r.
The residual sample values r[ x ][ y ] with x = 0..nTbS − 1, y = 0..nTbS − 1 are modified as follows:
r[ x ][ y ] = ( r[ x ][ y ] + ( 1 << ( bdShift − 1 ) ) ) >> bdShift (8‑269)
…

## Slide 7: Experimental condition & results
 | Y | U | V
All-intra | -8.5% | -8.3% | -3.5%
Random access | -7.1% | -33.0% | -61.8%
Proposed modifications implemented on Range Extension 3.1 software
Test Sequences (12-bit sequences extended to 14-bit)
  RGB (2560x1600) : Traffic
  YUV420 (1920x1080) : CrowdRun, DucksTakeOff, InToTree, OldTownCross, ParkScene
Source bit depth is extended to 14 bits by adding Gaussian LSB to 12 bit source sequence
QP= -36, -32, -28 -24
No change to transforms

## Slide 8: Results- RD plots (All Intra - ParkScene)
Chart: Y PSNR vs Bitrate
| 1594112.3304000001 | 1435694.2271999998 | 1275871.1947000001 | 1153644.3437000001
HM10.1_RExt3.1 | 88.9858 | 88.4624 | 88.254 | 84.1817
Proposed_TS_Shift | 147.512 | 102.502 | 89.811 | 86.6394
Source bit depth = 14 bits. Obtained by adding Gaussian LSB to 12-bit source sequence.

## Slide 9: Results- RD plots (RA- ParkScene)
Chart: Y PSNR vs Bitrate
| 1277889.8966000001 | 1125525.8381000001 | 993685.98289999936 | 871771.93629999994
HM10.1_RExt3.1 | 87.347 | 86.9353 | 83.429 | 79.642
Proposed_TS_Shift | 109.5341 | 90.2495 | 85.8782 | 81.8937
Source bit depth = 14 bits. Obtained by adding Gaussian LSB to 12-bit source sequence.

## Slide 10: Conclusions
Proposed modified transform skip scaling to support high fidelity coding of residuals for source bit depths 14 and higher
Simulations demonstrate that the base HEVC Range Extensions system that is limited to about 90dB has been improved to beyond 130dB.
The scaling factor is modified only for transform skip blocks and no change is made for transform blocks.