## Slide 1: JCTVC-S0040: Enhanced chroma QP signaling for adaptive cross-component transform in SCC extensions
Keiichi Chono
NEC Corp.

## Slide 2: Summary
Enhanced chroma QP signaling is proposed for Adaptive Cross-component Transform (ACT) in SCC extensions.
  Additional signaling of PPS/Slice-level chroma QP offset values;
  CU-level switching of chroma QP offset values.
It is recommended that the above elements are considered for SCC test model adoption or studied in AHG toward the next meeting.

## Slide 3: Background: Adaptive cross-component transform
Note: This figure is from JCTVC-R0147
G
B
R
Y
Co
Cr
Prediction residual is adaptively represented either in RGB color space or YCoCr color space.
G
B
R

## Slide 4: Problem statements
Note: This figure is from JCTVC-R0147
G
B
R
Y
Co
Cr
Same chroma QP offsets values are applied to RGB prediction residual and YCoCr prediction residual.
G
B
R
G
B
R
Y
Co
Cr
cb_qp_offset
cr_qp_offset
Visual quality optimization is not possible
when ACT is enabled.

## Slide 5: Proposal
Use different chroma QP offset values for different color-space prediction residues when ACT is enabled.
  Additional PPS/SPS-level QP offset signaling for ACT;
  CU-level QP offset switching based on ACT flag.
G
B
R
Y
Co
Cr
cb_qp_offset
cr_qp_offset
alt_cb_qp_offset
alt_cr_qp_offset
Visual quality optimization is achieved by using appropriate QP offset values.
cu_residual_act_flag=0
cu_residual_act_flag=1

## Slide 6: Detail of proposal (1/3)
PPS-level chroma QP signaling
pps_scc_extension ( ) { | Descriptor
… | 
if( residual_adaptive_colour_transform_enabled_flag ){ | 
alt_pps_cb_qp_offset | se(v)
alt_pps_cr_qp_offset | se(v)
} | 
… | 
} | 

## Slide 7: Detail of proposal (2/3)
Slice-level chroma QP signaling
slice_segment_header( ) { | Descriptor
first_slice_segment_in_pic_flag | u(1)
… | 
slice_qp_delta | se(v)
if( pps_slice_chroma_qp_offsets_present_flag ) { | 
slice_cb_qp_offset | se(v)
slice_cr_qp_offset | se(v)
if( residual_adaptive_colour_transform_enabled_flag ) { | 
alt_slice_cb_qp_offset | se(v)
alt_slice_cr_qp_offset | se(v)
} | 
} | 
… | 
byte_alignment( ) | 
} | 

## Slide 8: Detail of proposal (3/3)
QP derivation change for switching
8.6.1 Derivation process for quantization parameters
– If cu_residual_act_flag is equal to 0, the variables qPCb and qPCr are derived as follows:
qPiCb = Clip3( −QpBdOffsetC, 57, QpY + pps_cb_qp_offset + slice_cb_qp_offset + CuQpOffsetCb ) (8‑257)
qPiCr = Clip3( −QpBdOffsetC, 57, QpY + pps_cr_qp_offset + slice_cr_qp_offset + CuQpOffsetCr ) (8‑258)
– Otherwise (cu_residual_act_flag is equal to 1), the variables qPCb and qPCr are derived as follows:
qPiCb = Clip3( −QpBdOffsetC, 57, QpY + alt_pps_cb_qp_offset + alt_slice_cb_qp_offset + CuQpOffsetCb ) (8‑257)
qPiCr = Clip3( −QpBdOffsetC, 57, QpY + alt_pps_cr_qp_offset + alt_slice_cr_qp_offset + CuQpOffsetCr ) (8‑258)

## Slide 9: Summary of related contributions
 |  | S0040 | S0094 | S0144
Additional QP offset signaling for ACT | Co/Cr offset |  |  | 
 | Y offset |  |  | 
CU-level QP offset switching | QP derivation change (8.6.1) |  |  | 
 | Scaling process change (8.6.2) |  |  | 
Additional QP clipping |  |  |  | 
Document #
Item

## Slide 10: Conclusion and recommendation
Enhanced chroma QP signaling for ACT is proposed.
It is recommended that the following items are considered for SCC test model adoption or studied in AHG toward the next meeting:
  Additional signaling of PPS/Slice-level chroma QP offset values for ACT;
  CU-level switching of chroma QP offset values for ACT.