## Slide 1: High dynamic range compatibility SEI message JCTVC-U0033
Matteo Naccari, Andrew Cotton, Sebastian Schwarz, Manish Pindoria, Marta Mrak, Tim Borer

## Slide 2: Overview
Context and motivation
Proposed SEI message
Conclusions

## Slide 3: 1. Context and motivation

## Slide 4: Enabling HDR services in broadcasting
The Hybrid Log-Gamma Opto-Electronic Transfer Function (OETF) will be used to deliver HDR services in broadcasting
  It is backward compatible
  It does not require dynamic metadata
  It is display independent
By using the Hybrid Log-Gamma (HLG) OETF an HEVC bitstream will serve both Standard Dynamic Range (SDR) and HDR receivers:
  SDR receivers will use the OETF indicated in the VUI (e.g. BT.709 OETF)
  HDR receivers should be able to display the content using the full-dynamic range

## Slide 5: Design issue to be addressed in HDR broadcasting services
Version 1 decoders will be used in HDR services
Receivers should be notified about the colour primaries for SDR and HDR
  Even if SDR and HDR have the same primaries, HDR has a greater colour volume
  Different colour space conversions (e.g. via companding operations) should be also supported
The solution proposed here is an SEI message:
  Maintains compatibility with Version 1 receivers
  Allows a finer scale of adaptation of the post-processing operated at the receiver side

## Slide 6: 2. Proposed SEI message

## Slide 7: SEI message syntax
hdr_compatibility_info( payloadSize ) { | Descriptor
hdr_compatibility_cancel_flag | u(1)
if( !hdr_compatibility_cancel_flag ) { | 
hdr_compatibility_mode_flag | u(1)
hdr_transfer_characteristics_idc | u(2)
if( hdr_compatibility_mode_flag ) | 
hdr_colour_companding_idc | u(4)
} | 
} | 
Indicates when new HDR data are coming
Indicates that colour companding is applied
Indicates which EOTF/OETF is used
Indicates which colour companding is applied

## Slide 8: SEI message semantics
hdr_compatibility_mode_flag specifies whether the colour primaries associated with SDR and HDR need to be converted
hdr_transfer_characteristics_idc specifies which OETF should be used to display the decoded content
  0 = Use the VUI entry (for backwards compatibility)
  1 = HLG OETF
  > 1 = Reserved for future use
hdr_colour_companding_idc indicated which colour companding operation should be applied (8 companding operations are envisaged)

## Slide 9: 3. Conclusions

## Slide 10: To summarise
Backward compatibility with legacy receivers and delivery of HDR services in broadcasting is guaranteed by using the HLG OETF
HEVC Version 1 receivers can be used and HDR is enabled by using an SEI message
Issues such as different colour primaries are addressed by indicating the colour companding operation in the proposed SEI message