## Slide 1: [JCTVC-U0132] Target bits saturation to avoid CPB overflow and underflow under the constraint of HRD
Yong-Jo Ahn, Xiangjian Wu, Woong Lim, and Donggyu Sim
Kwangwoon University (KWU), Digital Insights Co.

## Slide 2: Introduction
In the recent HEVC reference model (HM), R-lambda model based rate control method was adopted
However, the rate control method doesn’t consider the constraint of hypothetical reference decoder (HRD)
Even though the rate control method achieves target bitrates, CPB overflow and underflow in a decoder side should be taken care for practical applications
To prevent CPB overflow and underflow, this contribution proposes a target bits saturation method under the constraint of HRD

## Slide 3: Additional parameters for CPB in RC
To consider CPB, rate control should have three parameters (R, B, F) with a leaky bucket model
  R: the peak transmission bit rate
  B: CPB size (capacity)
  F: buffer fullness (with 0 ≤ F ≤ B)
i: frame number, i=0,1,2,…
bi: i-th frame bits
Fi: buffer fullness after removing i-th frame
f: frame rate
D: initial delay
F0: initial buffer fullness (F=D x (R/f))
Initial delay (D)
CPB size (B)
Bitrate (R)
i-th frame bits (bi)
Initial buffer
fullness (F0)
time
bits
t0
t1
t2
t3
t0-D
b1
b2
b3
0

## Slide 4: Example of CPB overflow
When CPB occupancy is sufficiently full, but the amount of bits for a frame (bi) is relatively small, CPB overflow occurs in ti time
Condition: Fi – bi + R/f > B
B
R/f
bi
Fi
time
bits

## Slide 5: Example of CPB underflow
When the amount of bits for a frame (bi) is larger than current CPB fullness, CPB underflow occurs in ti time
Condition: Fi – bi < 0
B
bi
Fi
time
bits

## Slide 6: Proposed target bits saturation method
The proposed method controls the occupancy of CPB between 10% and 90% of the CPB size for lower and upper bounds
  Upper bound: Fi – tbi + R/f > B x 0.9
  Lower bound: Fi – tbi < B x 0.1
Upper bound
of CPB fullness(U)
Lower bound
of CPB fullness(L)
Initial delay (D)
CPB size (B)
Bitrate (R)
Frame bits (bi)
Initial buffer
fullness (F0)
time
bits
t0
t1
t2
t3
t0-D
b1
b2
b3
0

## Slide 7: Proposed preventing CPB overflow
Condition for overflow: Fi – tbi + R/f > B x 0.9
Target bits (tbi) is set to
tbi = Fi + R/f – B x 0.9
tbi: target bits for the i-th frame
CPB size (S)
Re-estimated
target bits(tbi)
Buffer fullness (Fi)
time
bits
Overflow bits
Upper bound
of CPB fullness (U)

## Slide 8: Proposed preventing CPB underflow
Lower bound: Fi – bi < B x 0.1
Target bits (tbi) is set to
tbi = max(200, Fi – B x 0.1)
Re-estimated
target bits(tbi)
Buffer fullness (Fi)
time
bits
Underflow bits
Lower bound
of CPB fullness (L)
CPB size (S)

## Slide 9: Performance evaluation
CPB fullness with respect to time index without target bits saturation (B=0.5R, F=0.9B)
CPB fullness with respect to time index with target bits saturation (B=0.5R, F=0.9B)

## Slide 10: Performance evaluation
CPB fullness with respect to time index without target bits saturation (B=R, F=0.5B)
CPB fullness with respect to time index with target bits saturation (B=R, F=0.5B)

## Slide 11: Conclusion
This contribution proposes a preventing method to avoid CPB overflow and underflow in rate control of HM
The proposed method prevents CPB overflow and underflow using saturation process for target bits