## Slide 1
MB skip flag coding in 3D-ATM optimized for 3D video compression
M. Mishurovskiy, A. Fartukov, I. Kovliga, JinYoung Lee
January’ 2013
Samsung R&D Russia Institute
and
Samsung Advanced Institute of Technology

## Slide 2
2
SAIT-Russia, SRR
Reasons for R&D
“SKIP” mode is widely used in AVC-based video coding providing high compression ratio due-to extremely low bitrate and reasonable reconstructed quality
In dependent views coding SKIP mode is used even more intensively due-to:
  Increased quantization factors adopted for dependent views
  Cascading quantization in B-slices
  Interview motion derivation implemented in the SKIP mode and proposed by Mediatek
Though mb_skip_flag is encoded by CABAC engine, due-to skewed probabilities and minimal probability of LPS symbol 0.0187, efficiency of mb_skip_flag coding is not optimal and might be improved

## Slide 3
3
SAIT-Russia, SRR
LPS probabilities estimation for mb_skip_flag
Results of LPS probability estimation for mb_skip_flag QP 26, 31, 36, 41; 25 frames, B-slices only, 7 sequences |  |  |  |  |  |  |  |  | 
ctxIdxInc | skip flag | Base view |  | Depended views |  | Base depths |  | Depended depths | 
 |  | Quantity of realizations | Prob.of LPS | Quantity of realizations | Prob.of LPS | Quantity of realizations | Prob.of LPS | Quantity of realizations | Prob.of LPS
2 | 0 | 75172 | 0.0185 | 87015 | 0.0099 | 8806 | 0.0081 | 18515 | 0.0084
 | 1 | 3981146 |  | 8700005 |  | 1075923 |  | 2174913 | 
1 | 0 | 260992 | 0.4794 | 186360 | 0.3988 | 39575 | 0.4550 | 66568 | 0.4926
 | 1 | 283457 |  | 280990 |  | 33042 |  | 64629 | 
0 | 0 | 139816 | 0.2914 | 87977 | 0.2459 | 33238 | 0.2118 | 61554 | 0.1728
 | 1 | 57498 |  | 28678 |  | 8933 |  | 12861 | 
Probabilities supported by CABAC engine: [0.01875…0.5] in 3D-ATM

## Slide 4
Example of slice-structure
MB Structure in AVC
4
Samsung Confidential
SAIT-Russia, SRR
MB structure and sequence of MBs in 3D-ATM
EOS
MB data
Mb_skip_flag
3 non-skipped MB
3 skipped MB
Can this sequence be encoded more efficiently?
Skipped MB
EOS
Mb_skip_flag

## Slide 5
5
Samsung Confidential
SAIT-Russia, SRR
Proposed Approach: Run of skipped MB
Skipped MB with Run Length
EOS
Signal of Run
Len
1
2
3
Combining
Possible inserting of run’s length
Excluding repeated MB
……….
! There is no mb_skip_flag here due-to its already known that mb_skip_flag=0 for the next MB

## Slide 6
6
Samsung Confidential
SAIT-Russia, SRR
Signaling & types of skipped MB runs
1
Modifications are introduced only if ctxIdxInc = 2 ( MB to the top and MB to the left are both skipped)
2
mb_skip_run_type is introduced instead of mb_skip_flag
3
Run’s length is defined either implicitly or explicitly
Skipped MB Run with explicit length
EOS
mb_skip_run_type=0
Len
Skipped MB Run with implicit length
EOS
mb_skip_run_type=1

## Slide 7
7
Samsung Confidential
SAIT-Russia, SRR
Explicitly defined run’s length: 2 possible cases
Skipped MB Run with Length
EOS
mb_skip_run_type=0
Len
0
0
0
0
0
0
0
0
0
6
0
0
0
0
1
0
1
0
1
1
0
1
0
1
0
1
0
0
0
0
0
For each MB where ctxIdxInc =2
! There is no mb_skip_flag here due-to its already known that mb_skip_flag=0 for the next MB
and slice contains another MB
0
0
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
0
0
Slice header
0
0
0
0
0
1
6
0
0
Slice header
For each MB where ctxIdxInc =2
End of slice AND not end of picture
1
2

## Slide 8
8
Samsung Confidential
SAIT-Russia, SRR
Implicitly defined run’s length
Skipped MB Run without Length
EOS
mb_skip_run_type=1
MB where ctxIdxInc =2
MB where ctxIdxInc becomes not 2
1
2
Number of MB in run less than 16
3
Picture has at least one more MB
While ctxIdxInc =2
Criteria to continue current run

## Slide 9
9
Samsung Confidential
SAIT-Russia, SRR
Run Length (Len) coding approach
Len value statistic for
Poznan_hall2 QP26
Explicit Len Value | Probability (p) | Log2(p)
0 | 0.186384 | 2.423648
1 | 0.114345 | 3.128539
2 | 0.091239 | 3.454203
3 | 0.078834 | 3.665043
… | … | …
10 | 0.038179 | 4.711074
11 | 0.038482 | 4.699686
12 | 0.036144 | 4.790117
13 | 0.033613 | 4.894838
14 | 0.031715 | 4.978689
15 | 0.031935 | 4.968714
 | Entropy: | 3.77bits
Uncompressed: |  | 4 bits
Total N of Runs: |  | 36355
Saved Bits: |  | 8231.65
Total Bits: |  | 12167680
Theoretical Gain: |  | 0.07%
We calculated theoretical gain for each QP for each sequence in the same way as for poznan_hall2@QP26 case (at the left).
We averaged gains for each sequence:
Sequence |  | Average Gain
balloons |  | 0.05%
gt_fly |  | 0.10%
kendo |  | 0.11%
newspaper1 |  | 0.04%
Poznan_hall2 |  | 0.03%
Poznan_street |  | 0.06%
undo_dancer |  | 0.06%
total average: |  | 0.07%
We decided to use fixed length code for binarization and bypass coding mode for all bits of Len. It allow us to simplify and speed up encoding and decoding processes. It also is confirmed through theoretical estimations of possible coding gains in case of more complicated coding of Len.

## Slide 10
10
Samsung Confidential
SAIT-Russia, SRR
Influence of Max Length onto compression gain
Which max length to be used? ( based on experiments)
Length code type | Max Length | Texture Coding |  | Depth Coding |  | Total (Coded PSNR) | 
Fixed length codes are used |  | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB | dBR, % | dPSNR,dB
 | 2 | -0.58 | 0.02 | -1.80 | 0.10 | -0.75 | 0.03
 | 4 | -0.83 | 0.03 | -2.42 | 0.13 | -1.08 | 0.04
 | 8 | -0.92 | 0.03 | -2.54 | 0.14 | -1.19 | 0.04
 | 16 | -0.91 | 0.03 | -2.51 | 0.13 | -1.21 | 0.04
 | 32 | -0.86 | 0.03 | -2.16 | 0.11 | -1.17 | 0.04

## Slide 11
11
Samsung Confidential
SAIT-Russia, SRR
Syntax: Changes at the Sequence Parameter Set 3DVC
seq_parameter_set_3dvc_extension( ) { | C | Descriptor
… |  | 
if( profile_idc = = 139 && depth_info_present_flag ) { |  | 
reduced_resolution_flag | 0 | u(1)
slice_header_prediction_flag | 0 | u(1)
inside_view_mvp_flag | 0 | u(1)
disp_flag | 0 | u(1)
psip_flag | 0 | u(1)
nonlinear_depth_representation_num | 0 | ue(v)
for( i = 1; i <= nonlinear_depth_representation_num; i++ ) |  | 
nonlinear_depth_representation_model[ i ] | 0 | ue(v)
seq_view_synthesis_flag | 0 | u(1)
} |  | 
if( profile_idc = = 139 && !depth_info_present_flag ) |  | 
enable_alc_encoder_flag | 0 | u(1)
if( profile_idc = = 139 ) |  | 
enable_rle_skip_flag | 0 | u(1)
} |  | 

## Slide 12
12
Samsung Confidential
SAIT-Russia, SRR
Changes at slice data syntax
slice_data( ) { | C | Descriptor
if( entropy_coding_mode_flag ) |  | 
while( !byte_aligned( ) ) |  | 
cabac_alignment_one_bit | 2 | f(1)
CurrMbAddr = first_mb_in_slice * ( 1 + MbaffFrameFlag ) |  | 
moreDataFlag = 1 |  | 
prevMbSkipped = 0 |  | 
RunLength = 0 |  | 
do { |  | 
if( slice_type != I && slice_type != SI ) |  | 
if( !entropy_coding_mode_flag ) { |  | 

## Slide 13
13
Samsung Confidential
SAIT-Russia, SRR
Changes at slice data syntax
if( !mb_vsskip_flag ) { |  | 
mb_skip_flag | 2 | u(1) ¦ ae(v)
moreDataFlag = !mb_skip_flag |  | 
} |  | 
} else { |  | 
RLECtx = RLE_skip_context( ) |  | 
if( RLECtx && RunLength == 0) { |  | 
mb_skip_run_type | 2 | u(1) ¦ ae(v)
if (mb_skip_run_type = = 1) |  | 
RunLength = 16 |  | 
else { |  | 
number_of_skipped_macroblocks | 2 | u(4) ¦ ae(v)
RunLength= number_of_skipped_macroblocks+1 |  | 
} |  | 
} else |  | 
if( !RLECtx && RunLength != 0) |  | 
RunLength = 0 |  | 
if( RLECtx) { |  | 
if(!mb_skip_run_type && RunLength == 1) |  | 
mb_skip_flag = 0 |  | 
else |  | 
mb_skip_flag = 1 |  | 
RunLength = RunLength - 1 |  | 
} else |  | 
mb_skip_flag | 2 | u(1) ¦ ae(v)
moreDataFlag = !mb_skip_flag |  | 

## Slide 14
14
Samsung Confidential
SAIT-Russia, SRR
Changes at slice data syntax
if( !entropy_coding_mode_flag ) |  | 
moreDataFlag = more_rbsp_data( ) |  | 
else { |  | 
if( slice_type != I && slice_type != SI ) |  | 
prevMbSkipped = mb_skip_flag ¦ ¦ mb_vsskip_flag |  | 
if( MbaffFrameFlag && CurrMbAddr % 2 = = 0 ) |  | 
moreDataFlag = 1 |  | 
else { |  | 
if (RunLength == 0 ¦¦ CurrMbAddr == (PicSizeInMbs-1) ¦¦ !mb_skip_run_type && RunLength == 1 ¦¦ mb_skip_run_type && NonSkipNextUpMb()) |  | 
end_of_slice_flag | 2 | ae(v)
else |  | 
end_of_slice_flag = 0 |  | 
moreDataFlag = !end_of_slice_flag |  | 
} |  | 
} |  | 
CurrMbAddr = NextMbAddress( CurrMbAddr ) |  | 
} while( moreDataFlag ) |  | 
If run is finished at this MB, end_of_slice should be read
Check that we still in the current picture

## Slide 15
15
Samsung Confidential
SAIT-Russia, SRR
Results: 3D-ATM 6.1 vs. 3D-ATM 6.1 + 3D-SRC
Compression Gain |  |  |  |  |  |  |  | 
Seq. | Texture Coding |  | Depth Coding |  | Total Coding ( coded PSNR) |  | Total Coding ( synthesized PSNR) | 
 | DBR, % | dPSNR, dB | DBR, % | dPSNR, dB | DBR, % | dPSNR, dB | DBR, % | dPSNR, dB
S01 | -2.60 | 0.08 | -8.45 | 0.45 | -3.37 | 0.10 | -3.38 | 0.11
S02 | -1.56 | 0.05 | -5.28 | 0.23 | -1.96 | 0.06 | -1.98 | 0.06
S03 | -0.29 | 0.01 | -1.81 | 0.14 | -0.44 | 0.01 | -0.47 | 0.01
S04 | -0.25 | 0.01 | -2.98 | 0.15 | -0.55 | 0.02 | -0.53 | 0.02
S05 | -0.22 | 0.01 | 1.85 | -0.09 | -0.37 | 0.02 | -0.33 | 0.01
S06 | -0.70 | 0.03 | -0.41 | 0.02 | -0.92 | 0.04 | -0.98 | 0.04
S08 | -0.77 | 0.03 | -0.45 | 0.02 | -0.86 | 0.04 | -0.91 | 0.03
Average | -0.91 | 0.03 | -2.51 | 0.13 | -1.21 | 0.04 | -1.23 | 0.04

## Slide 16
16
Samsung Confidential
SAIT-Russia, SRR
Results: 3D-ATM 6.1 vs. 3D-ATM 6.1 + 3D-SRC
Seq. | Complexity | 
 | Encoder, % | Decoder, %
S01 | 100.00 | 99.59
S02 | 100.00 | 99.66
S03 | 100.05 | 99.73
S04 | 99.94 | 99.67
S05 | 100.00 | 99.50
S06 | 100.00 | 99.61
S08 | 100.00 | 99.56
Average | 100.00 | 99.62

## Slide 17
17
Samsung Confidential
SAIT-Russia, SRR
Conclusions
Current 3D-ATM reference model uses so-called SKIP mode extensively especially for dependent views of texture and all views of depth due-to specific quantization politics and additional 3D-based tools which increase SKIP mode usage;
CABAC engine supports finite probabilities range of LPS, namely [0.01875…0.5] which means that symbols with LPS lower than 0.01875 might be encoded sub-optimally;
It has been proved that mb_skip_flag has ~ twice lower probability than lowest boundary of LPS supported by CABAC; based on this 3D-Skip Run Coding (3D-SRC) has been proposed to improve coding efficiency of mb_skip_flag in B-Slices.
3D-SRC tool being integrated into 3D-ATM 6.1 shows the following:
  Compression gain for texture coding: -0.91% BD-Rate
  Total compression gain based on coded texture: -1.21% BD-Rate
  Total compression gain based on synthetic texture : -1.23% BD-Rate
  Compression gain for dependent views : -4.16% BD-Rate
  Compression gain for depths : -2.51% BD-Rate
  Complexity of Encoder is estimated as 100%; Complexity of Decoder is estimated as 99.6%
5. No parsing dependency between base and supplementary views has been introduced;
6. Its believed that syntax changes and new semantic fits well text of the standard;
Based on this we kindly recommend adopting 3D Skip Run Coding into subsequent release of 3D-ATM reference model.