## Slide 1: 3D-HEVC: Report on Reduced Resolution Depth Map Coding in 3D-HEVC
Shiori Sugimoto
Shinya Shimizu
Hideaki Kimata
JCT3V-D0215

## Slide 2: Motivation
#1 Limitation of depth-sensing devices
  Depth data generally can be captured only at lower resolution than texture data
  E.g. Kinect : Texture - 1280x1024 Depth - 640x480
#2 System requirement
  Data volume is required to be 4x of single view video for keeping throughput of the decoder

## Slide 3: Affected tools
Texture coding tools
  VSP
  DoNBDV
Depth coding tools
  DMM
  MPI
  VSO
  QTLPC

## Slide 4: Modification : Adjustment of Inter-component correspondence
#1 : Scaling a position of corresponding inter-component (VSP, DoNBDV, MPI and QTLPC)
#2 : Scaling an obtained motion vector (MPI)
#3 : Allowing 1 LCU to correspond multiple LCUs (QTLPC)
#4 : Resampling of inter-component reference picture (DMM mode 3 & 4 )
LCU on Texture
LCUs on Depth

## Slide 5: Modification : VSO reference
  Reference synthesized view can be generated based on what kind of depth map
  If encoder has full resolution depth map, both of the original depth map and the upsampled reduced resolution depth map are acceptable for VSO reference
    Only requirement #2 allows the former.

## Slide 6: Experimental condition
Input data is full resolution , downsampled before slice encoding and upsampled after slice decoding
Both resampling on the outside of coding loop are excluded in coding times

## Slide 7: Experimental condition
  VSO reference is the synthesized view based on the original full resolution depth map
Resampling filters
 | target | Filter
Downsampling | Input depth map | Nearest neighbor
 | inter-component reference picture | 12 tap sinc filter
Upsampling | Reconstructed depth map on VSO | Nearest neighbor
 | Output depth map | Nearest neighbor

## Slide 8: Experimental Results
 | video 0 | video 1 | video 2 | Video /video | Synth /total | enc time | dec time
Balloons | 0.0% | 0.0% | 0.1% | 0.0% | 1.9% | 95.6% | 75.2%
Kendo | 0.0% | 0.1% | 0.2% | 0.0% | -0.3% | 93.9% | 74.7%
Newspapercc | 0.0% | 0.2% | 0.2% | 0.1% | 4.1% | 94.1% | 72.9%
GhostTownFly | 0.0% | 1.6% | 1.8% | 0.3% | 0.5% | 93.9% | 73.6%
PoznanHall2 | 0.0% | -0.2% | 0.5% | 0.0% | 1.7% | 97.5% | 73.5%
PoznanStreet | 0.0% | -0.1% | 0.0% | 0.0% | 1.2% | 96.3% | 72.7%
UndoDancer | 0.0% | -0.5% | 0.4% | -0.1% | 8.6% | 97.8% | 74.0%
1024x768 | 0.0% | 0.1% | 0.2% | 0.0% | 1.9% | 94.5% | 74.3%
1920x1088 | 0.0% | 0.2% | 0.7% | 0.0% | 3.0% | 96.4% | 73.4%
average | 0.0% | 0.2% | 0.4% | 0.0% | 2.5% | 95.6% | 73.8%
Table1. Full resolution vs 1/4 resolution w/ affected tools

## Slide 9: Experimental Results
RD curve of synthesized view in the best case, Kendo
Chart: 
| 1822.7991999999999 | 878.77440000000013 | 480.84639999999996 | 283.27760000000001
Full resolution | 43.1115 | 40.8532 | 38.4485 | 35.9088
Quarter resolution | 42.7504 | 40.7036 | 38.4087 | 35.9087

## Slide 10: Experimental Results
Chart: 
| 6800.7063000000007 | 2856.5135999999998 | 1326.8560000000002 | 637.83600000000001
Full resolution | 38.6507 | 35.8378 | 33.3219 | 31.0052
Quarter resolution | 37.8954 | 35.4976 | 33.1746 | 30.9573
RD curve of synthesized view in the worst case, Undo Dancer

## Slide 11: Conclusion
Reduced resolution depth coding in HTM can be achieved by simple modification
It provides loss on coding performance compared with full resolution coding, but it does not make much of a difference at low bit rate
Decoding time is effectively reduced
The data volume is vastly reduced to 15/4 of single view and the requirement is satisfied

## Slide 12: Experimental Results
Table2. w/o affected tools vs w/ affected tools at 1/4 resolution
 | video 0 | video 1 | video 2 | Video /video | Synth /total | enc time | dec time
Balloons | 0.0% | -24.5% | -24.1% | -11.8% | -10.8% | -21.0% | 115.5%
Kendo | 0.0% | -23.4% | -24.1% | -11.5% | -12.5% | -26.5% | 121.9%
Newspapercc | 0.0% | -14.7% | -13.6% | -6.3% | -1.9% | -34.3% | 115.8%
GhostTownFly | 0.0% | -9.5% | -9.2% | -3.5% | -0.9% | -30.4% | 114.6%
PoznanHall2 | 0.0% | -14.1% | -15.1% | -7.2% | -4.3% | -30.1% | 120.4%
PoznanStreet | 0.0% | -8.3% | -9.5% | -3.5% | -0.7% | -17.5% | 119.1%
UndoDancer | 0.0% | -15.4% | -15.2% | -5.4% | -1.5% | -57.9% | 116.3%
1024x768 | 0.0% | -20.8% | -20.6% | -9.8% | -8.4% | -27.3% | 117.7%
1920x1088 | 0.0% | -11.8% | -12.3% | -4.9% | -1.9% | -34.0% | 117.6%
average | 0.0% | -15.7% | -15.8% | -7.0% | -4.7% | -31.1% | 117.6%