## Slide 1: CE6: Simplified DC calculation for SDC (JCT3V-E0117)
Hyunho Jo, Woong Lim, Jonghoon Yoo, and Donggyu Sim
Kwangwoon University (KWU)

## Slide 2: Summary
Motivation
  Reduce the number of computing operations for the calculation of the DC value for simplified depth coding (SDC)
  Accumulation, branch, and division operations are used in HTM 7.0r1
Proposed method
  Calculate DC value using the partial samples of the predicted block based on the characteristics of three types of prediction modes (DC, Planar, and DMM Mode-1)
  Remove accumulation, branch, and division operations
Experimental results
  CTC: 0.1% coding gain on synthesized view
Cross-check
  JCT3V-E0194 by LGE

## Slide 3: Problem statements
Calculation of mean value for the predicting depth value in SDC
  SDC coding mode consists of the three prediction mode (DC, Planar, and DMM Mode-1)
  For the complexity reduction, sub-sampling method was adopted for DMM and SDC
  However, accumulation with varying number of samples, branch, and division operations are still utilized
    Higher computational complexity
    Inappropriate for hardware implementation (accumulation and division)

## Slide 4: Proposed simplified DC calculation for SDC
Proposed method
  It calculates DC value using the partial samples of the predicted block based on the characteristics of three types of prediction modes (DC, Planar, and DMM Mode-1) of SDC coded block
  Remove accumulation, branch, and division operations

## Slide 5: DC calculation for DC mode in SDC coded block
For DC prediction mode, the right-bottom sample in a predicted block is used as the DC value
  Inner boundary filtering is employed for 8x8 and 16x16 blocks
  The right-bottom sample is the same as the ‘dcVal’ in DC prediction mode
HTM 7.0r1
Proposed
Constant value
Constant value
(dcVal)
Inner-boundary filtered
region
Inner-boundary filtered
region

## Slide 6: DC calculation for DMM Mode-1 mode in SDC coded block
For DMM Mode-1 prediction mode, the left-top, right-top, left-bottom, and right-bottom sample in a predicted block is used to find the DC values of segment-1 and segment-2, respectively
HTM 7.0r1
Proposed

## Slide 7: A problem of sub-sampling method for DMM Mode-1 mode
The sub-sampling method (HTM 7.0r1) cannot consider all the partitioning case of DMM Mode-1 for the 32x32 and 64x64 blocks
Segment-1
Segment-2
Sub-sampling points
( red samples)

## Slide 8: DC calculation for Planar mode in SDC coded block
For Planar prediction mode, the left-top, right-top, left-bottom, and right-bottom samples in a predicted block is used to get the DC value
HTM 7.0r1
Proposed

## Slide 9: Comparison of number of involved pixels for DC calculation
The sub-sampling method in HTM-7.0r1 is used for the 32x32 and 64x64 block
Prediction Mode | Block Size | Number of pixels involved |  | Ratio
 |  | HTM 7.0r1 | Proposed | 
DC | 8x8 | 64 | 1 | 1.56%
 | 16x16 | 256 | 1 | 0.39%
 | 32x32 | 256 | 1 | 0.39%
 | 64x64 | 1024 | 1 | 0.10%
Planar | 8x8 | 64 | 4 | 6.25%
 | 16x16 | 256 | 4 | 1.56%
 | 32x32 | 256 | 4 | 1.56%
 | 64x64 | 1024 | 4 | 0.39%
DMM Mode-1 | 8x8 | 64 | 4 | 6.25%
 | 16x16 | 256 | 4 | 1.56%
 | 32x32 | 256 | 4 | 1.56%
 | 64x64 | n/a | n/a | n/a

## Slide 10: Comparison of involved operation types and number of that operations
Prediction Mode | Block Size | Operation types and number of that operations |  |  |  |  | 
 |  | HTM 7.0r1 |  |  | Proposed |  | 
 |  | Addition1 | Division | Branch | Addition2 | Shift | Branch
DC | 8x8 | 126 | 1 | 64 | - | - | -
 | 16x16 | 510 | 1 | 256 | - | - | -
 | 32x32 | 510 | 1 | 256 | - | - | -
 | 64x64 | 2046 | 1 | 1024 | - | - | -
Planar | 8x8 | 126 | 1 | 64 | 4 | 1 | -
 | 16x16 | 510 | 1 | 256 | 4 | 1 | -
 | 32x32 | 510 | 1 | 256 | 4 | 1 | -
 | 64x64 | 2046 | 1 | 1024 | 4 | 1 | -
DMM Mode-1 | 8x8 | 126 | 2 | 64 | - | - | -
 | 16x16 | 510 | 2 | 256 | - | - | -
 | 32x32 | 510 | 2 | 256 | - | - | -
 | 64x64 | n/a | n/a | n/a | n/a | n/a | n/a
Count the number of addition for ‘sumPred’ and ‘numPred’
Left-top, right-top, left-bottom, right-bottom, and round offset

## Slide 11: Experimental results (1)
BD rate results for 3-view case under CTC
Sequences | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 100.8%
Kendo | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 99.6% | 100.4%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 100.2% | 101.9%
GT_Fly | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 101.0%
Poznan_Hall2 | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 100.8% | 101.0%
Poznan_Street | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 101.2%
Undo_Dancer | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | -0.1% | 100.0% | 100.9%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 99.8% | 101.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 101.0%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 100.1% | 101.0%

## Slide 12: Experimental results (2)
BD rate results for 3-view case under All Intra
Sequences | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons |  |  |  |  |  |  |  | 
Kendo |  |  |  |  |  |  |  | 
Newspaper_CC |  |  |  |  |  |  |  | 
GT_Fly |  |  |  |  |  |  |  | 
Poznan_Hall2 |  |  |  |  |  |  |  | 
Poznan_Street |  |  |  |  |  |  |  | 
Undo_Dancer |  |  |  |  |  |  |  | 
1024x768 |  |  |  |  |  |  |  | 
1920x1088 |  |  |  |  |  |  |  | 
average |  |  |  |  |  |  |  | 

## Slide 13: Conclusions
Simplified DC calculation for SDC is proposed to reduce the computational complexity
  The proposed method can replace the accumulation and division operation
  The proposed method can significantly reduce the number of computing operation
The proposed method achieves 0.1% coding gain for synthesized views in CTC
It is recommended to adopt proposed method into 3D-HEVC