## Slide 1: JCT3V-E0175 An adaptive disparity vector derivation method for ARP in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  In ARP, the estimated DV derived by NBDV is not accurate enough.
Proposed
  An adaptive disparity vector derivation (ADVD) method is proposed
  Three DV candidates are derived from neighbouring blocks to be selected by the encoder.
Results
  Achieve 0.33% BD-rate saving for the synthesized views

## Slide 3: The problem
Advanced residual prediction (ARP) is adopted to replace the simple inter-view residual prediction
In ARP, the estimated DV is derived by a neighbouring block disparity vector (NBDV) procedure.
  The first encountered DV from a temporal or spatial neighbouring block is utilized by ARP as the estimated DV for the current block.
  Since such an estimated DV is not accurate enough, pseudo residual prediction may be inefficient in some cases.

## Slide 4: Proposed
  An adaptive disparity vector derivation (ADVD) method is proposed.
    3 DV candidates are derived from neighbouring blocks.
      The first three unique DVs in the NBDV procedure are treated as DV candidates in ADVD
    The encoder can find the best DV candidate in ARP according to RDO criterion and signal the index to the decoder.
    Since the accuracy of the estimated DV is improved, the ½ weighting option is removed.

## Slide 5: Results
Achieve 0.33% BD-rate saving for the synthesized views
Cross-checked by JCT3V-Exxxx (Thank LG)
CTC

## Slide 6: Conclusion
An adaptive disparity vector derivation (ADVD) method is proposed to improve ARP coding efficiency.
  Improves the accuracy of the estimated DV.
0.33% BD-rate saving for the synthesized views
Suggest to be adopted

## Slide 7: Thank you for your attention!