## Slide 1: JCT3V-E0178 3D-CE2.h related: A simplified DV derivation method in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  DV derivation is quite complex in the current 3D-HEVC.
  A derived DV (DDV) is proposed to simplify DV derivation by removing the DV-MCP procedure.
    Troubles may arise due to such a global updating variable
Proposed
  Simplify the DV-MCP procedure in two aspects
    The checking on DV-MCP block is omitted
    Only two neighboring blocks may be accessed instead of five
  Reduce the complexity while keeping neighboring-based feature
Results
  Cause no BD-rate loss in the common test condition

## Slide 3: The problem
DV-MCP method is applied in the DV derivation process when no DV can be found from any neighboring blocks.
  Five spatial neighboring blocks are checked to identify if a neighboring block is a DV-MCP block.
  DV-MCP block is defined as a block which is coded in merge mode using inter-view motion vector prediction.
    a flag to indicate whether a block is a DV-MCP block and its derived DV must be stored

## Slide 4: The problem (Cont.)
DDV is proposed to simplify DV derivation by removing the DV-MCP procedure
  DDV is output when no DV can be found from any neighboring blocks, and is updated after coding/decoding each CU.
DDV is the only global updating variable in reconstruction
  Break the traditional neighboring-based reconstruction rule
  May cause troubles in some applications

## Slide 5: Proposed
  Simplify DV-MCP while keeping its neighboring-based feature
    The DV-MCP checking is omitted
      The derived DV is stored for a CU without identifying whether it is a DV-MCP block.
      The DV-MCP flag is required no more.
      A neighboring block is available when it is inter-coded and in the current LCU-row
    Only two neighboring blocks L and A, may be accessed

## Slide 6: Results
The simplification does not cause a BD-rate loss.
Cross-checked by JCT3V-Exxxx (Thank Samsung)

## Slide 7: Conclusion
A simplified DV derivation method in 3D-HEVC is proposed.
Reduce the complexity of DV-MCP significantly while keeping its neighboring-based feature.
No BD-rate loss in the common test condition
Suggest to be adopted

## Slide 8: Thank you for your attention!