## Slide 1
JCT3V-F0088 2D Backward Compatible Centralized 2-View Packing
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University

## Slide 2: Contents
Introduction
Backward Frame Compatible C2V Packing
Experimental Results
Conclusions

## Slide 3: Introduction

## Slide 4: Why Stereo Packing?
To deliver 3D contents, one simple and direct way is to combine both left and right view frames into single frame by a stereo packing format such that the traditional transmission and video coding system can treat them as the normal 2D videos.
Simplest Stereo 3D and Deliverable in 2D DTV Systems:
2D Video
Encoder
2D Video
Decoder
Stereo
Packing
Right view
Left view
Right view
Left view
(Interpolation)
Hole Filing
H.264/AVC, HEVC ….
2D DTV Systems

## Slide 5: Stereo Packing 3D Videos
Left
view
Right
view
Side
by
Side
Top
and
Bottom
Why New Stereo Packing?
Current Stereo Packing Formats:
Notes: If the pixel from one view is always surrounded by pixels from the other view, the format is called a blending format, e.g. the checkerboard format.
Otherwise, it is called a non-blending format, e.g. the side-by-side format
[ref] Tao Zhang, “3D image identification by image difference,” Proceedings of IEEE International Conference on Multimedia and Expo, pp. 1415-1420, 2010.

## Slide 6: Problems & Goal
Top and Bottom Stereo Packing
Visually Discomfort for 2D Displays

## Slide 7: Problems & Goal
The popular 3D frame compatible formats for transmitting stereoscopic views are side-by-side and top-and-bottom.
Visual discomfort is the common problem when the audiences view the packed stereoscopic 3D video through their 2D TVs.
The proposed backward compatible centralized 2-view packing format shows more comfort visualization in the ordinary 2D TV
without extra pre-processing
and more comfortably visualization
in 2D TV receivers
Notes: In recent year, 3DTV displays have become more popular in the consumer market.
Frame Packing refers to the combination of two frames, one for the left eye and the other for the right eye, into a single “packed” frame that consists of these two individual sub-frames. The most 3D frame compatible formats for transmitting stereoscopic views are side-by-side and top-and-bottom.
But the significant problem is Visual discomfort when the audience views the stereoscopic 3D video through traditional TV.
In order to eliminate Visual discomfort problem,we proposed a novel packing format: Two-View Centralized Packing

## Slide 8: 2D Backwards Compatible Centralized 2-View Packing

## Slide 9: 3D Video Transmission Framework
Storage and/or
Transmission
View 0
View 1
Centralized 2-View Packing
Encoding
Decoding
3D TV
2D TV
Centralized 2-View De-packing

## Slide 10: The Proposed Centralized 2-View Packing
2D backwards compatible centralized 2-view packing includes two parts
  Checkerboard down-sampling & alignment
  Rearrangement & centralized packing
L
R
Down-sampling
Rearrangement &
Centralized Packing

## Slide 11: The Proposed Centralized 2-View Packing
To utilize the advantage of the checkerboard format while improving its compression efficiency simultaneously, we propose checkerboard-based side-by-side format and checkerboard-based top-and-bottom format as
Checkerboard
Checkerboard down-sampling & alignment :
L
L
L
L
L
L
L
L
R
R
R
R
R
R
R
R
L
L
L
L
L
L
L
L
R
R
R
R
R
R
R
R

## Slide 12: The Proposed Centralized 2-View Packing
To utilize the advantage of the checkerboard format while improving its compression efficiency simultaneously, we propose checkerboard-based side-by-side format and checkerboard-based top-and-bottom format as
L
L
L
L
L
R
R
R
R
L
R
L
L
R
R
R
Checkerboard
Checkerboard bottom-up
Checkerboard down-sampling & alignment :
R
L
L
L
L
L
L
L
R
R
R
L
R
R
R
R
Checkerboard
Checkerboard side-by-side

## Slide 13: The Proposed Centralized 2-View Packing
Spilt the top or left view and reverse
Set the bottom or right view as center
Place it at top and bottom
Rearrangement & centralized packing:
B
L1
L2
T1-Reverse
T2-Reverse
R
L2
L1
L2-Reverse
T1-Reverse
Notes: The Top view is divided into two parts called T1 and T2.
Then, the T1 and T2 parts are reversed by the vertical direction called T1-reverse and t2-reverse.
We place it at top and bottom location of packed frame, respectively.
Centrailzed packing is adapted by using L1-reverse, R view, and L2-reverse packing orders.

## Slide 14: The Proposed Centralized 2-View Packing
Frame after C2V Packing

## Slide 15
The Proposed Centralized 2-View De-Packing
Checkerboard Up-sampling :
The hole pixel can be interpolated from either vertical or horizontal direction, which can be chosen from the following formula:
Hole
V1
V2
H1
H2
The direction which contains smaller difference will be chosen
For each hole pixel, we use non-hole pixels with the weighted matrix [1, -5, 20, 20, -5, 1]/32 to estimate its pixel value.

## Slide 16: Simulations

## Slide 17
Simulations
The anchor software is HTM-8.0 with 2 view + 2 depth configuration.
The PSNR is calculated by averaging the PSNR in view 1 and view 2
The bit rate is obtained by summing all the related bits that are needed to recover the reconstructed frames.
Anchor Reconstruction – view1 & depth1
Anchor Reconstruction – view2 & depth2
Reconstruction – view1 & depth1
Reconstruction – view2 &depth2
De-Packing
Up-Sampling
PSNR
Calculation
PSNR
Calculation
Y1
U1
V1
Y2
U2
V2
Proposed Reconstruction – packed view & depth
D1
D2
Notes: the the bit rate comparison uses the sum of original_view1, original_view2, original_depth1, original_depth2 versus the sum of packed-view and packed-depth to evaluate the coding efficiency.
The de-packed frame can get form decoding, de-packing and up-sampling. The PSNR is calculated by averaging the PSNR in view 1 and view 2

## Slide 18
Simulations

## Slide 19
Side-by-Side 2-View 3D Video

## Slide 20
The Proposed C2V 3D Video

## Slide 21: Conclusions

## Slide 22
Conclusions
This contribution develops a new C2V stereo 3D video packing format that provides a more unrestricted and comfortable vision experience for two-view videos.
For traditional TV receiving 3D video contents, the proposed C2V format can provide more comfortably visualization without un-packing process.
For 3D stereo TV, the proposed C2V with similar complexity can exhibit comparable 3D quality .

## Slide 23
Thank you for your attention
Q&A