## Slide 1
On camera parameter transmission for 3D-HEVC
(JCT3V-J0044)
Sunmi Yoo, Junghak Nam and Sehoon Yea
LG Electronics
October 2014

## Slide 2: Summary
Problem statement
  Redundant camera parameter(CP) transmission in slice segment header (SH)
    Time-varying camera parameters but not frequently changed
Proposed method
  Inherit CPs from the previous SH
    Method 1 : SH change only
    Method 2 : Use VPS CPs as default

## Slide 3: Introduction
2 ways for camera parameter transmission in 3D-HEVC
  Send in VPS : No CP change for ViewX
  Send in SH : Time-variant CPs
cpA0
V0
POC0
cpB0
V0
POC1
cpC0
V0
POC2
cpA1
V1
POC0
cpB1
V1
POC1
cpC1
V1
POC2
cpA2
V2
POC0
cpB2
V2
POC1
cpC2
V2
POC2
time
view
…
…
…
cpV0
cpV1
cpV2
V0
POC0
V0
POC1
V0
POC2
V1
POC0
V1
POC1
V1
POC2
V2
POC0
V2
POC1
V2
POC2
view
…
…
…
time
Figure 1 Camera parameters transmitted in VPS
Figure 2 Camera parameters transmitted in SH

## Slide 4: Problem Statement
Time-varying but not frequently changed CPs
  Identical CPs repeatedly sent in a period
  Unnecessary transmission
cpA
ViewX
POC0
cpA
ViewX
POC1
cpA
ViewX
POC2
cpA
ViewX
POC3
cpA
ViewX
POC N
cpB
ViewX
POC N+1
…
…
Redundant camera parameters
Time
Figure 3 Redundant camera parameter transmission in the current 3D-HEVC

## Slide 5: Proposed Method
Prevention of duplicated camera parameters
  Reuse CPs in the previous SH
  Additional flag for copy indication
cpA
cpB
…
…
Time
Copy the previous slice camera parameters
New camera parameters
parsing
Figure 4 Proposed camera parameter transmission method
ViewX
POC0
ViewX
POC1
ViewX
POC2
ViewX
POC3
ViewX
POC N
ViewX
POC N+1

## Slide 6: Method #1 – SH change only
prev_cp_in_slice_segment_header_flag[ ViewIdx ] equal to 0 specifies that the syntax elements cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] are present in the slice segment header. prev_cp_in_slice_segment_header_flag[ j ] equal to 1 specifies that the syntax element cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] are derived from the corresponding syntax element of the previous slice segment header having a view index equal to ViewIdx. When not present, prev_cp_in_slice_segment_header_flag[ j ] is inferred to be equal to 1. It is a requirement of bitstream conformance, that the value prev_cp_in_slice_segment_header_flag[ ViewIdx ] in a slice segment header shall be equal to 0 when the picture in an access unit with nuh_layer_id equal to 0 is an IRAP picture.
cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] specify conversion parameters for converting a depth value to a disparity value. When not present and cp_in_slice_segment_header_flag[ ViewIdx ] is equal to 0, the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ], are inferred to be equal to vps_cp_scale[ ViewIdx ][ j ], vps_cp_off[ ViewIdx ][ j ], vps_cp_inv_scale_plus_scale[ ViewIdx ][ j ], and vps_cp_inv_off_plus_off[ ViewIdx ][ j ], respectively. It is a requirement of bitstream conformance, that the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxA and the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxB shall be the same, when viewIdxA is equal to viewIdxB.
I.7.3.6.1 General slice segment header syntax
I.7.4.7.1 General slice segment header semantics
slice_segment_header( ) { | Descriptor
... | 
if( cp_in_slice_segment_header_flag[ ViewIdx ] ) | 
prev_cp_in_slice_segment_header_flag[ ViewIdx ] | u(1)
if( nuh_layer_id > 0 && cp_in_slice_segment_header_flag[ ViewIdx ]!prev_cp_in_slice_segment_header_flag[ ViewIdx ] ) | 
for ( j = 0; j < ViewIdx; j++ ) { | 
cp_scale[ j ] | se(v)
cp_off[ j ] | se(v)
cp_inv_scale_plus_scale[ j ] | se(v)
cp_inv_off_plus_off[ j ] | se(v)
} | 
... | 
} | 
prev_cp_in_slice_segment_header_flag[ ViewIdx ] equal to 0 specifies that the syntax elements cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] are present in the slice segment header. prev_cp_in_slice_segment_header_flag[ j ] equal to 1 specifies that the syntax element cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] are derived from the corresponding syntax element of the previous slice segment header having a view index equal to ViewIdx. When not present, prev_cp_in_slice_segment_header_flag[ j ] is inferred to be equal to 1. It is a requirement of bitstream conformance, that the value prev_cp_in_slice_segment_header_flag[ ViewIdx ] in a slice segment header shall be equal to 0 when the picture in an access unit with nuh_layer_id equal to 0 is an IRAP picture.
cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] specify conversion parameters for converting a depth value to a disparity value. When not present and cp_in_slice_segment_header_flag[ ViewIdx ] is equal to 0, the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ], are inferred to be equal to vps_cp_scale[ ViewIdx ][ j ], vps_cp_off[ ViewIdx ][ j ], vps_cp_inv_scale_plus_scale[ ViewIdx ][ j ], and vps_cp_inv_off_plus_off[ ViewIdx ][ j ], respectively. It is a requirement of bitstream conformance, that the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxA and the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxB shall be the same, when viewIdxA is equal to viewIdxB.

## Slide 7: Method #2 – Use VPS CP as default CP
I.7.3.2.1.2 Video parameter set extension 2 syntax
I.7.4.3.1.2 Video parameter set extension 2 semantics
vps_extension2( ) { | Descriptor
... | 
cp_precision | ue(v)
for( i = 1; i < NumViews; i++ ) { | 
cp_present_flag[ i ] | u(1)
if( cp_present_flag[ i ] ) { | 
cp_in_slice_segment_header_flag[ i ] | u(1)
if( !cp_in_slice_segment_header_flag[ i ] ) | 
for( j = 0; j < i; j++ ) { | 
vps_cp_scale[ i ][ j ] | se(v)
vps_cp_off[ i ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ i ][ j ] | se(v)
vps_cp_inv_off_plus_off[ i ][ j ] | se(v)
} | 
} | 
} | 
} | 
vps_cp_scale[ i ][ j ], vps_cp_off[ i ][ j ], vps_cp_inv_scale_plus_scale[ i ][ j ], and vps_cp_inv_off_plus_off[ i ][ j ] specify conversion parameters for converting a depth value to a disparity value and might be used to infer the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] for the i-th view specified in VPS. When the i-th view contains both a texture view and a depth view, the conversion parameters are associated with the texture view.
The variables CpScale[ i ][ j ], CpOff[ i ][ j ], CpInvScalePlusScale[ i ][ j ], and CpInvOffPlusOff[ i ][ j] are defined as follows :
CpScale[ i ][ j ] = vps_cp_scale[ i ][ j ]
CpOff[ i ][ j ] = vps_cp_off[ i ][ j ]
CpInvScalePlusScale[ i ][ j ] = vps_cp_inv_scale_plus_scale[ i ][ j ]
CpInvOffPlusOff[ i ][ j] = vps_cp_inv_off_plus_off[ i ][ j ]

## Slide 8: Method #2
I.7.3.2.1.2 General slice segment header syntax
I.7.4.7.1 General slice segment header semantics
cp_update_flag[ ViewIdx ] equal to 1 specifies that the syntax elements cp_scale[ ViewIdx ], cp_off[ ViewIdx ], cp_inv_scale_plus_scale[ ViewIdx ], and cp_inv_off_plus_off[ ViewIdx ] are present in the slice segment header. cp_update_flag[ ViewIdx ] equal to 0 specifies that the syntax element cp_scale[ ViewIdx ], cp_off[ ViewIdx ], cp_inv_scale_plus_scale[ ViewIdx ], and cp_inv_off_plus_off[ ViewIdx ] are derived from the corresponding syntax element of the previous slice segment header. When not present, cp_update_flag[ ViewIdx ] is inferred to be equal to 0. It is a requirement of bitstream conformance, that the value prev_cp_in_slice_segment_header_flag[ ViewIdx ] in a slice segment header shall be equal to 1 when the picture in an access unit with nuh_layer_id equal to 0 is an IRAP picture.
cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] specify conversion parameters for converting a depth value to a disparity value. When not present, the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ], are inferred to be equal to vps_cp_scale[ ViewIdx ][ j ], vps_cp_off[ ViewIdx ][ j ], vps_cp_inv_scale_plus_scale[ ViewIdx ][ j ], and vps_cp_inv_off_plus_off[ ViewIdx ][ j ], respectively. It is a requirement of bitstream conformance, that the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxA and the values of cp_scale[ j ], cp_off[ j ], cp_inv_scale_plus_scale[ j ], and cp_inv_off_plus_off[ j ] in a slice segment header having a ViewIdx equal to viewIdxB shall be the same, when viewIdxA is equal to viewIdxB.
slice_segment_header( ) { | Descriptor
... | 
if( nuh_layer_id > 0 && cp_in_slice_segment_header_flag[ ViewIdx ] ) | 
cp_update_flag [ ViewIdx ] | u(1)
if ( cp_update_flag [ViewIdx ] ) | 
for ( j = 0; j < ViewIdx; j++ ) { | 
cp_scale[ j ] | se(v)
cp_off[ j ] | se(v)
cp_inv_scale_plus_scale[ j ] | se(v)
cp_inv_off_plus_off[ j ] | se(v)
} | 
... | 
} | 

## Slide 9: Conclusion
Problem statement
  Duplicated CPs might be transmitted when CP change is occasionally
Proposed method
  New flag in SH – indication inherit CPs from the previous SH
It is recommended to adopt J0044.
  Prevent redundant information transmission
  Beneficial for multiple slices in a picture