## Slide 1: JCTVC-J0199: Comments on DPB size
Thomas Davies
Arild Fuldseth (Cisco Systems)

## Slide 2: Summary
In the HEVC draft DPB size is specified in units of pictures, unlike AVC, allowing:
  6 pictures for all levels, including current picture
  More references than AVC at the highest level resolution
  Fewer references than AVC at lower resolutions in a level
This limit prevents the extensive use of long-term references for error resilience
  Widely used in video conferencing today
  Up to 16 reference frames in shipping products
We propose modifying the draft to allow significantly more references to be used, preferably 16 as in AVC

## Slide 3: Flexible DPB size in AVC
In AVC systems with a capability exchange, it is possible to indicate (IETF RFC 3984):
  Support for decoding e.g. level 4 resolutions
  Support for a larger DPB size than level 4 supports
Then an encoder may use a sufficiently high level value to capture the DPB size but otherwise stick to level 4 limits
This method allows up to 16 reference pictures to be supported

## Slide 4: LTRs and error recovery in AVC
Sent but not received
Received but no ACK/NACK yet
ACKed/NACKed
Current
good recovery
frame
Earlier
Later

## Slide 5: LTRs and error recovery in AVC
Sent but not received
Received but no ACK/NACK yet
ACKed/NACKed
Current
good recovery
frame
Earlier
Later
Next candidate
recovery frame

## Slide 6: Distribution of recovery frames
Recovery frames must be distributed over the effective RTT i.e. incorporating all delays:
  Feedback can also be lost
  Feedback can be required from multiple participants
  The worst-case ERTT can be very significant
The number of reference frames affects the age of the recovery reference frame.
  ERTT + Δ = (1 + 1/(N-1)) * ERTT
6 pictures = current + 3*STR + 2*LTR, which is insufficient

## Slide 7: Conclusions
Analysis of DPB size so far has not included LTRs
We believe that HEVC should offer at least the same reference capabilities as AVC
Use of multiple LTRs in AVC has proved extremely valuable in video conferencing
We have shipping products making use of 16 reference pictures
We are agnostic about the method by which an increased DPB size is achieved (AVC method or other)

## Slide 8: Some options
MaxDpbSize = 16 for all levels
AVC method: DPB memory equivalent to N largest pictures including current, N=5, 6
“Layered” solution: DPB memory may be split into N full-size, 2*N half-size, 4*N quarter size, N=5, 6
  Extends J0111, J0210, J0283, J0367, J0496 to 4*N
As 3, but add 3*N/2, 4*N/3 (J0496)
As 2, 3, or 4, but with N=5 for level > 4 (as per J0163)