## Slide 1
Non-RCE2: On sample adaptive intra prediction
for oblique modes in lossy coding
JCTVC-N0177
Ankur Saxena, Haoming Chen and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation and Prior Work
Sample Adaptive Prediction (SAP) from JCTVC-M0056 for horizontal and vertical modes was adopted in HEVC Range Extensions Working Draft in JCTVC April 2013 meeting.
SAP for lossy Horizontal and Vertical modes presented in JCTVC M-0351/N-0052
SAP for diagonal (lossless) modes in our contribution JCTVC-N0176.

## Slide 3: Overview of SAP in HM10.1+RExt3.0
Current SAP for Horizontal and Vertical modes
Proposal: Propose SAP for 3 strictly diagonal modes for lossy scenario
  Fully parallel at the encoder and decoder.

## Slide 4: Proposed SAP for 3 diagonal modes
  Proposed for 4x4 blocks when transform is skipped.
  Fully parallel at both the encoder and decoder.
  Additional number of operations even less than Horizontal and Vertical SAP in HM.

## Slide 5: Experiments
  Anchor : HM10.1 + RExt 3.0 in Lossy settings according to stipulated test conditions in RCE 2
  Proposed method is to use SAP for lossy H+V+ 3 Diagonal modes at size 4x4.
  Thanks to Qualcomm for cross-checking the results in JCTVC-N0363.

## Slide 6: Results for SAP for H+V+3 Diagonal Modes Anchor: HM 10.1+RExt3.0 Lossy

## Slide 7: Comparison with JCTVC-N0052
Proposal : SAP for H+V+3 Diagonal Modes; Anchor: HM 10.1+RExt3.0 Lossy
SAP for H+V Modes (N-0052); Anchor: HM10.1+RExt3.0 Lossy

## Slide 8: Discussion and Complexity Considerations
Gains on top of N-0052
Roughly 0.5 % gain for Screen Content YUV; 0.3 % for RGB; and 0.1 % for Class B as compared to N-0052 (DPCM for lossy H+V Modes).
 | 4×4 | 
 | Additional Complexity | Additions/Sample
Strictly Diagonal Modes | 14 adds | 0.875
H or V mode already in HEVC-Range Extensions software | 24 adds | 1.5
Additional complexity for SAP for diagonal modes is even less than complexity of SAP for horizontal and vertical modes in HM.

## Slide 9: Conclusions
Proposed SAP for diagonal modes for lossy coding.
SAP for these diagonal modes is fully parallel at both the encoder and decoder
Recommend to adopt proposed SAP for diagonal modes in HEVC-Range Extensions WD/CD.