## Slide 1: AHG 5 and 18: Internal Precision for High Bit Depths
JCTVC-N0188
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Introduction
Range Extensions has been mandated to support higher bit depths.
  Currently 14 bit is specified, but from the outset, 16-bit was seen as a possibility.
At the previous meeting, the capabilities of HEVC at higher bit depths were presented.
  Settings were recommended regarding a high-accuracy system, suitable for rate control and high bit depths and high operating points.

## Slide 3: Required Operating Range
When considering operation at higher bit depths the target PSNR must also be higher.
  There is no point in a 16-bit system producing a maximum PSNR of 94.6 (ignoring compression efficiency).
    This equates to an MSE of 1.5, which can be achieved by rounding the coefficients to 14-bits and using an almost-lossless 14-bit system.
      i.e. the two least-significant bits in the output are effectively random noise.
  Note that at these high-bit depth operating points, numerical behaviour is paramount, since subjective behaviour is not observable to the human eye.

## Slide 4: HM / RExt3.0 Transform Response
RDOQ off, Transform Skip off, MTDR=ETDR=15, TransformPrecision=6, PCM&Lossless disabled
16-bit degrades in HM due to non-standard clipping on the output to 15-bit (otherwise follows the 14-bit curve).

## Slide 5: Proposed Transform Response
RDOQ off, Transform Skip off, MTDR=ETDR=max(15,bitDepth+6), TransformPrecision=14, PCM&Lossless disabled

## Slide 6: Lambda
Lambda has been analysed for the low QP intra operating points
  On average, the current settings in HM are correct.
    Some sequences indicated a slightly lower lambda, some slightly higher, with only negligible deviation in the resulting performance.
  However, the C Model in TComRdCost used parameters describing lambda as UInts, and for 16-bit input data at high QPs (eg 37), this overflowed.
    Those parameters have been changed to Doubles.

## Slide 7: Mixed Coding
Mixed lossy / lossless coding has been studied
        (lossless = transquant bypass, IPCM and transform skip)
Additional bug-fixes required in the HM / RExt3.0 code.
  Current RExt3.0 does not decode due to illegal QPs being used by the encoder for transquant-bypass CUs
    Errors generated due to the deltaQP mechanism.
  The current cost function is:
      cost=lambda * costbits + costdistortion
    modified to
      cost= costbits + costdistortion / lambda
    Similarly, the estimated cost in intra searching now uses a fixed QP’ of 4 (q of 1).
    These changes makes the lossless costs QP independent (in the mixed system).
      (the initialisation of context variables is still QP dependent)
  The sequence PSNR is formed from the average MSEs, not the average PSNRs
    You can’t average a PSNR=99.99dB (=∞dB) with a PSNR of 40dB.

## Slide 8: Mixed Coding (continued)
Sequence 1 – Hard to compress – 14 bit

## Slide 9: Mixed Coding (continued)
Sequence 2 – Easier to compress – 14 bit

## Slide 10: Mixed Coding (continued)
For some difficult-to-compress sequences, there is little difference between the high accuracy and lower accuracy systems.
  Both systems are effectively coded with 100% lossless encoding, and (for 14-bit), there is less differentiation for 4x4 TU coding at higher (less negative) QPs.
However, for simpler systems, there is 10dB difference between the two cases, and the high bit depth system is easier to rate control over the high end.
16-bit scenarios demonstrate more extreme behaviour
  These can be seen in JCTVC-N0189
    High Bit Depth Golomb-Rice Parameter Offset and Adaptive Fixed Bits Results.xlsm

## Slide 11: Applications
For applications, such as professional, it is important that all blocks have a similar level of noise.
  It is important that the frame-average SNR is not raised with QP as a result of a mixture of quite noisy blocks and an increasing number of lossless blocks.
  Lossless blocks would be used only when the block is practically lossless and when the saving in bits would allow all the other lossy blocks to use a lower QP and thereby reduce their level of noise.
  The transform is important as it allows rate-control, scaling lists, and has benefits in noisy management.
However, for other applications the transform is not required.
  e.g. lossless applications.
  e.g. high-bit-depth input data but rely on non-transform coding to maintain the required quality.
  It is proposed that these applications be kept in different profiles where there is an absence of transforms.

## Slide 12: Conclusion
The base RExt lossy (rate-controllable) coding has been extended from ~80dB to ~120dB.
The various sources of error in the current RExt system have been analysed, and the following recommendations are made:
  To provide better support for higher bit depths, internal accuracies should be increased:
    MAX_TR_DYNAMIC_RANGE = max(15, bitDepth + 6)
    ENTROPY_CODING_DYNAMIC_RANGE = max(15, bitDepth + 6)
    Transform matrix precision >= bitDepth - 2