## Slide 1: AHG5: Unifying DPCM
JCTVC-O0066
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
In the Vienna meeting, the following was adopted:
  Rotation/scan-reversal of transform-skipped (TS) TUs
  DPCM of residuals (RDPCM) for lossy intra TUs
  DPCM of coefficients (CDPCM) for lossy inter TUs
  DPCM of residuals (RDPCM) for lossless inter TUs, noting that RDPCM for lossless intra TUs had been previously adopted (SAIP).
This has led to the following flow of data through the system:

## Slide 3: RExt4 System Flowchart

## Slide 4: Proposal
DPCM process ordering is proposed to be updated.
These changes take into account a number of aspects:
  Unification of designs
  RDOQ
  Numerical limits
  Parallelisation
  Feedback path length

## Slide 5: Aspect 1: Unification
Having the process ordering be different between intra and inter is not conducive to compact implementation.
  Currently
    Intra is using RDPCM.
    Inter & intra-block-copy are using CDPCM.
    Forward RDCPM is before any rotation is applied.
    Forward CDPCM is after any rotation is applied.

## Slide 6: Aspect 2: RDOQ
    If rotation occurs before DPCM, an encoder will struggle to apply any form of RDOQ: adjusting a value will require all previously encoded values to be adjusted.
If rotation occurs after DPCM, RDOQ can be applied more easily.
It would therefore be useful if rotation could be applied to any transform-skip TU, including those larger than 4x4.

## Slide 7: Aspect 3: Numerical Limits
The bit stream is constrained to contain encoded 16-bit signed values (for extended_precision_flag=0).
The inverse quantiser also clips the coefficients to the same range.
There is currently no further clipping on the non-transform paths until the recombination with the prediction.
  Therefore, RDPCM will need to use accumulators that are 21-bit signed (since they will need to accumulate up to 32 16-bit values), although it only usefully needs (bitDepth + 1) bits (signed).
  CDPCM will also require 21-bit signed accumulators, although it only usefully needs 16 bits.
A clipping stage in DPCM would therefore be useful to reduce accumulator sizes in the decoder.

## Slide 8: Aspect 4: Parallelisation
In SAIP, parallelisation in encoder and decoder was trivial.
  However, because there was no rotation, inverse RDPCM could not occur until the top-left coefficient was decoded, and therefore a temporary buffer would be required.
If rotation could be applied, then no 2D temporary buffer would be required.
  For Horizontal DPCM, intra uses a vertical scan order, and therefore only a 1D (32-element) array of accumulators would be required.
    Similarly for Vertical DPCM.
  For inter, the scan order is always diagonal.
    It would be useful for DPCM decoding if the inter scan order was governed by the DPCM mode.

## Slide 9: Aspect 5: Feedback Length
The encoder requires a feedback path in order to apply DPCM when using lossy coding.
  For RDPCM:
    A sample must be DPCM’d, transformed, quantised, inverse-quantised, inverse-transformed and then inverse-DPCM’d before the next sample can be considered.
  For CDPCM
    A coefficient must be DPCM’d, quantised, inverse-quantised and then inverse-DPCM’d before the next sample can be considered.

## Slide 10: Proposed System #1: Unified RDPCM
Intra behaves as in RExt4, except:
  Clipping is added in IRDPCM.
  Rotation can be applied to all TU sizes, and is always applied when DPCM is used.

## Slide 11: Proposed System #2: CDPCM
Inter behaves as in RExt4, except:
  Clipping is added in ICDPCM.
  Rotation is applied before ICDPCM, to all TU sizes, and is always applied when DPCM is used.
  Scan order in entropy coding is governed by inter DPCM mode.

## Slide 12: Results – AHG8 Lossy
RDPCM
CDPCM
In both cases, RDOQ is now used for DPCM TUs.

## Slide 13: Results – AHG8 Lossy (without inter scan order modification)
RDPCM
CDPCM
In both cases, RDOQ is now used for DPCM TUs.

## Slide 14: Results – AHG8 Lossless
RDPCM & CDPCM (they are identical for lossless).
  Results do not include the additional modification to always apply rotation where DPCM is used.
Without inter-scan order modification, the results are identical to anchor (nothing has changed apart from clipping, which does not affect these results).

## Slide 15: Conclusion
The following changes are proposed:
  Unification of inter and intra DPCM modes, preferring CDPCM because the feedback loop is shorter.
  Addition of clipping to inverse DPCM.
  Addition of inter-scan orders controlled by inter DPCM direction to reduce decoder buffering.
  Rotation always applied prior to inverse-DPCM wherever DPCM is used, permitting RDOQ in encoder and reducing buffering in decoder.
  The software has been restructured to remove the previously-added two pairs of quantisers used by inter and intra lossy DPCM, using instead the standard xQuant and xDeQuant functions.