## Slide 1
Non-RCE4:
Palette prediction for palette coding
JCTVC-P0160
Guoxin Jin, Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation
Screen content video has similar colors in local areas
It will be good to re-use previous coded palettes to prevent transmitting colors in current palettes
y
x
For example, CU x can re-use palette in y

## Slide 3: Motivation
However, there may exist ‘gap’ between two palette coded CUs.
y: Previous palette coded CU
z: Not palette coded
x: Current CU
Can benefit by using palette from the last CU on left coded using palette coding.
y
x
z

## Slide 4: Proposed Palette Prediction Schemes
Two schemes for palette prediction proposed:
Scheme A.1 : Search palette from CU’s located to the left of current CU. Search range constrained in current LCU
Scheme A.2 : Search palette from CU’s located to the left of current CU. Search range is constrained in one left LCU and current LCU

## Slide 5: Scheme A.1 Search Left within current LCU
Search to the left until it finds the first palette coded CU
If no palette until the left of LCU, terminate search.
Rate-Distortion:
  Palette of x
  Choose palette of y for x (prediction)
y
x

## Slide 6: Scheme A.2 Search Left in LCU+Left LCU
Search to the left until it finds the first palette coded CU
If no palette until the left of LCU, terminate search.
Rate-Distortion:
  Palette of x
  Choose palette of y for x (prediction)
y
x

## Slide 7: Proposal highlights
Part 1: Anchor : RExt5.1 + JCTVC-O0218
  Bit-rate savings of:
  2.5 % for Lossy coding SC YUV 444
  3 % Lossless coding SC YUV 444
Part 2 : Anchor: RExt5.1 + JCTVC-P0198 (RCE 4 test 2)
  0.8 % for Lossy coding SC YUV 444
  0.8 % Lossless coding SC YUV 444

## Slide 8: Scheme A.1 Lossless Results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current LCU only)

## Slide 9: Scheme A.1 : Lossy results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current LCU only)

## Slide 10: Scheme A.2 Lossless Results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 11: Scheme A.2 : Lossy results on O-0218
Anchor: HM 12.1+RExt5.1 + O-0218
Proposal : HM 12.1+RExt5.1 + O-0218 + Scheme A.1 (Palette prediction in current + one left LCU only)

## Slide 12: Scheme A.2 Lossless Results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal : HM 12.1+RExt5.1 + P-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 13: Scheme A.2 : Lossy results on P-0198
Anchor: HM 12.1+RExt5.1 + P-0218
Proposal : HM 12.1+RExt5.1 + P-0218 + Scheme A.2 (Palette prediction in current + one left LCU only)

## Slide 14: Conclusions
Proposed two palette prediction schemes.
  Scheme A.1 :Search palette from CUs located in current LCU
  Scheme A.2: Search palette from all CUs in current+one left LCU
2.5 % gain for Lossy; and 3 % gain for lossless over
O-0218 in Rext 5.1.
0.8 % gain for Lossy and Lossless over P-0198.
Recommend to adopt the technique or test in a CE.