## Slide 1: Additional Definitions of Frame Packing Arrangement SEI Message Syntax for CCDP Extensions
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University

## Slide 2: Outlooks of CCDPs (color 3/4, 7/8, 15/16)
1H
3/4H
1/8H
1/8H
1H
Color-3/4 CCDP
1H
15/16H
1/32H
1/32H
Color-15/16 CCDP
1H
7/8H
1/16H
1/16H
Color-7/8 CCDP
Original Color
Original Depth

## Slide 3: Modified Frame Packing Arrangement Syntax
frame_packing_arrangement( payloadSize ) { | Descriptor
frame_packing_arrangement_id | ue(v)
frame_packing_arrangement_cancel_flag | u(1)
if( !frame_packing_arrangement_cancel_flag ) { | 
frame_packing_arrangement_type | u(7)
quincunx_sampling_flag | u(1)
content_interpretation_type | u(6)
spatial_flipping_flag | u(1)
frame0_flipped_flag | u(1)
field_views_flag | u(1)
current_frame_is_frame0_flag | u(1)
frame0_self_contained_flag | u(1)
frame1_self_contained_flag | u(1)
if( !quincunx_sampling_flag && frame_packing_arrangement_type != 5 ) { | 
frame0_grid_position_x | u(4)
frame0_grid_position_y | u(4)
frame1_grid_position_x | u(4)
frame1_grid_position_y | u(4)
} | 
frame_packing_arrangement_reserved_byte | u(8)
frame_packing_arrangement_persistence_flag | u(1)
} | 
upsampled_aspect_ratio_flag | u(1)
} | 
frame_packing_arrangement( payloadSize ) { | Descriptor
frame_packing_arrangement_id | ue(v)
frame_packing_arrangement_cancel_flag | u(1)
if( !frame_packing_arrangement_cancel_flag ) { | 
frame_packing_arrangement_type | u(7)
quincunx_sampling_flag | u(1)
content_interpretation_type | u(6)
spatial_flipping_flag | u(1)
frame0_flipped_flag | u(1)
field_views_flag | u(1)
current_frame_is_frame0_flag | u(1)
frame0_self_contained_flag | u(1)
frame1_self_contained_flag | u(1)
if( !quincunx_sampling_flag && frame_packing_arrangement_type != 5) { | 
frame0_grid_position_x | u(4)
frame0_grid_position_y | u(4)
frame1_grid_position_x | u(4)
frame1_grid_position_y | u(4)
} | 
if(frame_packing_arrangement_type == 65 ¦¦ frame_packing_arrangement_type == 66 ¦¦ frame_packing_arrangement_type == 67) { | 
depth_subpixel_arrangement_type | u(1)
color_sampling_type | u(3)
if(content_interpretation_type == 33 ¦¦ content_interpretation_type ==34) | 
depth_sampling_type | u(4)
} | 
else{ | 
frame_packing_arrangement_reserved_byte | u(8)
} | 
frame_packing_arrangement_persistence_flag | u(1)
} | 
upsampled_aspect_ratio_flag | u(1)
} | 
Original FPA
Modified FPA

## Slide 4: frame_packing_arrangement_type
Value | Interpretation
3 | Each component plane of the decoded frames contains a side-by-side packing arrangement of corresponding planes of two constituent frames as illustrated in Figure D‑4, Figure D‑5, and Figure D‑8.
4 | Each component plane of the decoded frames contains a top-bottom packing arrangement of corresponding planes of two constituent frames as illustrated in Figure D‑6 and Figure D‑7.
5 | The component planes of the decoded frames in output order form a temporal interleaving of alternating first and second constituent frames as illustrated in Figure D‑9.
65 | Color and depth planes of the decoded frames contains a color-3/4 CCDP arrangement of corresponding planes of 2D color and depth frames as illustrated in Figure D 10.
66 | Color and depth planes of the decoded frames contains a color-7/8 CCDP arrangement of corresponding planes of 2D color and depth frames as illustrated in Figure D 11.
67 | Color and depth planes of the decoded frames contains a color-15/16 CCDP arrangement of corresponding planes of 2D color and depth frames as illustrated in Figure D 12.

## Slide 5: content_interpretation_type
Value | Interpretation
0 | Unspecified relationship between the frame packed constituent frames
1 | Indicates that the two constituent frames form the left and right views of a stereo view scene, with frame 0 being associated with the left view and frame 1 being associated with the right view
2 | Indicates that the two constituent frames form the right and left views of a stereo view scene, with frame 0 being associated with the right view and frame 1 being associated with the left view
33 | Indicates that the packed frame is arranged in order of reduced_depth_1, resized_color, and reduced_depth_2 from top to bottom
34 | Indicates that the packed frame is arranged in order of reduced_depth_1, resized_color, and reduced_depth_2 from left to right
NOTE X: When value is 1 or 2 in content_interpretation_type, and frame_packing_arrangement_type should be equal to 3 or 4 should be equal 0. When value is 33 or 34 for content_interpretation_type, frame_packing_arrangement_type should be equal to 6, 7, or 8.
1H
1W
content_interpretation_type =63
content_interpretation_type =64

## Slide 6: spatial_flipping_flag
spatial_flipping_flag equal to 1, when frame_packing_arrangement_type is equal to 65, 66 or 67 and content_interpretation_type equal 33 or 34, indicates that depth frame is spatially flipped relative to its intended orientation for display or other such purposes.
When frame_packing_arrangement_type is equal to 65, 66 or 67, content_interpretation_type equal 33 or 34, and spatial_flipping_flag is equal to 1, the type of spatial flipping that is indicated is as follows:
  If content_interpretation_type is equal to 33, the indicated spatial flipping is vertical flipping.
  If content_interpretation_type is equal to 34, the indicated spatial flipping is horizontal flipping.
  Otherwise (spatial_flipping_flag is equal to 0), the indicated spatial flipping is not necessary.
1H
1H
spatial_flipping_flag=1
spatial_flipping_flag=0

## Slide 7: depth_subpixel_rotation_flag
depth_subpixel_rotation_flag equal to 1 indicates that embedding the Y values into Cb and Cr channels in the depth frame is used the line-offset rotation method. depth_subpixel_arrangement_flag equal to 0 indicates that embedding the Y values into Cb and Cr channels in the depth frame is used by Y, Cb, Cr sequence order.
YCbCr YCbCr YCbCr…
CrYCb CrYCb CrYCb…
CbCrY CbCrY CbCrY …
depth_subpixel_rotation_flag=1
YCbCr YCbCr Y…
YCbCr YCbCr Y…
YCbCr YCbCr Y …
depth_subpixel_rotation_flag=0

## Slide 8: color_sampling_type
color_sampling_type indicates that the method of the color sampling is used by an encoder to indicate to a decoder as specified in Table D‑13.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical or horizontal resolution of color frame
Values of color_sampling_type that do not appear in Table D.13 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignoreframe packing arrangement SEI messages that contain reserved values of content_interpretation_type.
NOTE 7–When content_interpretation_type equal to 33, the value 0 for color_sampling_type, the color frame is down scale the vertical resolution by using bilinear method. When content_interpretation_type equal to 34, the value 0 for color_sampling_type, the color frame is down scale the horizontal resolution by using bilinear method.

## Slide 9: depth_sampling_type
depth_sampling_type indicates that the method of the depth sampling is used by an encoder to indicate to a decoder as specified in Table D‑14.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical or horizontal resolution of depth frame
Values of depth_sampling_type that do not appear in Table D.14 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignoreframe packing arrangement SEI messages that contain reserved values of content_interpretation_type.
NOTE 8–When content_interpretation_type equal to 34, the value 0 for depth_sampling_type, the depth frame is down scale the vertical resolution by using bilinear method. When content_interpretation_type equal to 64, the value 0 for depth_sampling_type, the depth frame is down scale the horizontal resolution by using bilinear method.