## Slide 1: [JCTVC-V078] Improvement of coding efficiency for rate control under the constraint of HRD
Yong-Jo Ahn, Xiangjian Wu, Donggyu Sim, and Hochan Ryu
KWU (Kwangwoon University), Digital Insights Co.

## Slide 2: Introduction
To prevent CPB from overflow and underflow, JCTVC-U0132 proposed a target bits saturation method under the constraint of HRD
  It was adopted in HM at 21st JCT-VC meeting
The proposed method controls the occupancy of CPB between 10% and 90% of the CPB size for lower and upper bounds
(a) without target bits saturation
CPB fullness with respect to time index (B=0.5R, F=0.9B)
(b) without target bits saturation
CPB overflow
CPB underflow

## Slide 3: Introduction
It performed target bits saturation with 0.82% BD-BR loss and 0.04% rate control accuracy decrement
  Compared to rate control of HM-16.5 without consideration for the constraint of HRD
Table 1. RD performance of the proposed target bits saturation method (Random access)
Table 2. RD performance of the proposed target bits saturation method (Low-delay B)

## Slide 4: Motivation
In JCTVC-U0132, the proposed target bit saturation method can successfully prevent the CPB from overflow and underflow
However, some degradations of coding efficiency were observed in particular sequences
  Traffic, ParkScene, BQSquare
 |  | QPISlice | kbps | Y psnr | U psnr | V psnr | Enc T [s] | Dec T [s] | Enc T [h] |  | kbps | Y psnr | U psnr | V psnr | Enc T [s] | Dec T [s] | Enc T [h] |  | Y | U | V
Class A | Traffic | 22 | 13259.80 | 41.60 | 41.55 | 44.20 | 12947.81 | 18.75 | 3.60 |  | 13259.74 | 41.59 | 41.55 | 44.20 | 12620.82 | 18.77 | 3.51 |  | 8.0% | 18.0% | 20.4%
4K |  | 27 | 5405.91 | 39.12 | 39.90 | 42.42 | 10682.09 | 24.14 | 2.97 |  | 5405.93 | 38.90 | 39.61 | 42.03 | 10665.64 | 24.27 | 2.96 |  |  |  | 
 |  | 32 | 2562.02 | 36.50 | 38.50 | 40.87 | 9392.37 | 15.82 | 2.61 |  | 2562.45 | 36.12 | 38.00 | 40.31 | 9891.38 | 15.87 | 2.75 |  |  |  | 
 |  | 37 | 1342.88 | 33.86 | 37.43 | 39.76 | 8757.29 | 14.00 | 2.43 |  | 1300.24 | 33.11 | 36.62 | 38.97 | 9338.26 | 14.01 | 2.59 |  |  |  | 
 | PeopleOnStreet | 22 | 33590.43 | 40.15 | 45.06 | 44.79 | 19074.26 | 37.65 | 5.30 |  | 33590.73 | 40.14 | 45.06 | 44.79 | 19050.51 | 37.48 | 5.29 |  | -0.4% | 0.6% | 0.7%
 |  | 27 | 16180.57 | 37.18 | 43.22 | 43.52 | 15621.04 | 29.21 | 4.34 |  | 16179.80 | 37.18 | 43.21 | 43.51 | 15808.51 | 29.23 | 4.39 |  |  |  | 
 |  | 32 | 8452.64 | 34.11 | 41.49 | 42.17 | 13387.73 | 23.30 | 3.72 |  | 8452.72 | 34.12 | 41.48 | 42.16 | 13476.01 | 23.62 | 3.74 |  |  |  | 
 |  | 37 | 4683.17 | 31.13 | 40.05 | 40.92 | 11935.72 | 19.88 | 3.32 |  | 4683.23 | 31.26 | 39.97 | 40.86 | 12213.31 | 20.04 | 3.39 |  |  |  | 
 | Nebuta | 22 | 220617.04 | 39.01 | 39.43 | 38.04 | 59462.36 | 99.44 | 16.52 |  | 220617.00 | 39.01 | 39.44 | 38.04 | 59093.15 | 99.02 | 16.41 |  | -0.1% | 3.1% | 2.7%
 |  | 27 | 96189.48 | 33.61 | 38.06 | 36.60 | 46707.49 | 85.02 | 12.97 |  | 96189.53 | 33.61 | 38.06 | 36.60 | 47980.09 | 85.18 | 13.33 |  |  |  | 
 |  | 32 | 30064.06 | 29.55 | 36.90 | 35.52 | 31382.96 | 62.49 | 8.72 |  | 30063.96 | 29.54 | 36.90 | 35.53 | 30244.27 | 62.53 | 8.40 |  |  |  | 
 |  | 37 | 7065.17 | 27.88 | 35.79 | 34.51 | 21189.83 | 40.08 | 5.89 |  | 7064.52 | 27.89 | 35.55 | 34.30 | 23007.15 | 40.17 | 6.39 |  |  |  | 
 | SteamLocomotive | 22 | 23551.96 | 41.24 | 46.09 | 45.76 | 32423.57 | 49.02 | 9.01 |  | 23551.98 | 41.24 | 46.09 | 45.76 | 30620.15 | 49.02 | 8.51 |  | 2.3% | 0.3% | 0.5%
 |  | 27 | 6169.28 | 39.81 | 45.47 | 45.25 | 24415.93 | 37.48 | 6.78 |  | 6169.17 | 39.81 | 45.47 | 45.25 | 24127.91 | 37.66 | 6.70 |  |  |  | 
 |  | 32 | 2547.90 | 38.55 | 45.02 | 44.96 | 21958.05 | 32.75 | 6.10 |  | 2547.93 | 38.47 | 45.01 | 44.95 | 21198.35 | 32.82 | 5.89 |  |  |  | 
 |  | 37 | 1207.71 | 36.89 | 44.56 | 44.63 | 19219.58 | 29.14 | 5.34 |  | 1207.55 | 36.77 | 44.60 | 44.65 | 20544.52 | 29.33 | 5.71 |  |  |  | 

## Slide 5: Target bit saturation in key pictures
It was observed that conventional rate control algorithm without target bit saturation allocate the target bit for I-pictures (key pictures) as extremely high
Coded bits for I-pictures were observed as extremely high without consideration for the constraint of HRD
1115928 bits
(37.12dB for Y)
518664 bits
(33.21dB for Y)

## Slide 6: The proposed adaptive lower bound
To improve the coding efficiency of rate control under the constraint of HRD
This contribution proposes a target bit saturation for each picture using adaptive lower bound instead of a fixed lower bound
Re-estimated target bits(tb'i):
Buffer fullness (Fi)
time
bits
Underflow bits
Fixed lower bound
of CPB fullness (Bx0.1)
CPB size (B)
The fixed lower bound for target bit saturation in JCTVC-U0132

## Slide 7: The proposed adaptive lower bound
To determine the adaptive lower bound (Li) for preventing CPB from underflow, target bit for the next coded picture is used
  If the target bit for next coded picture is expected large, lower bound is set to relatively high
  Otherwise, lower bound is set to relatively low
Target bit for the next coded picture is calculated by the conventional R-lambda rate control algorithm
tbi: target bit for i-th picture
TBGOP: target bit for current GOP
CBGOP: coded bit of current GOP
ωi: weighted parameter for i-th picture
N: number of pictures in GOP

## Slide 8: The proposed adaptive lower bound
Condition for underflow:
Re-estimated target bits (tb'i) is set to
Re-estimated
target bits(tb'i)
Buffer fullness (Fi)
time
bits
Underflow bits
Adaptive lower bound
of CPB fullness (Li)
CPB size (B)
The proposed adaptive lower bound for target bit saturation

## Slide 9: Performance evaluation (scenario 1)
CPB fullness with respect to time index without the target bit saturation (B=0.5R, F=0.9B)
CPB fullness with respect to time index with the proposed adaptive lower bound(B=0.5R, F=0.9B)

## Slide 10: Performance evaluation (scenario 1)
CPB fullness with respect to time index with the fixed lower bound (B=0.5R, F=0.9B)
CPB fullness with respect to time index with the proposed adaptive lower bound(B=0.5R, F=0.9B)

## Slide 11: Performance evaluation (scenario 1)
The proposed method improves the coding efficiency with 0.15% Y BD-BR gain compared to JCTVC-U0132
  0.58% Y BD-BR loss compared to rate control of HM-16.6 without consideration for the constraint of HRD
Table 1. RD performance of the proposed target bit saturation method compared to rate control of HM without any target bit saturation method (Scenario 1: B=0.5R, F=0.9B)
Table 2. RD performance of the proposed target bit saturation method compared to rate control of HM with the target bit saturation using the fixed lower bound (Scenario 1: B=0.5R, F=0.9B)
 | Random access |  |  |  | Low-delay B |  |  | 
 | Y | U | V | ΔE | Y | U | V | ΔE
Class A | 2.05 | 5.01 | 5.27 | -0.00 |  |  |  | 
Class B | 1.71 | 5.18 | 5.13 | -0.01 | -0.22 | 2.49 | 3.18 | -0.02
Class C | 0.01 | 0.73 | 0.44 | 0.01 | 0.03 | 0.94 | 1.01 | 0.00
Class D | 0.28 | 1.39 | 1.44 | 0.10 | 0.17 | 1.48 | 1.79 | 0.05
Class E |  |  |  |  | 0.65 | 2.30 | 2.76 | 0.01
Overall | 1.05 | 3.20 | 3.19 | 0.02 | 0.10 | 1.82 | 2.21 | 0.00
 | Random access |  |  |  | Low-delay B |  |  | 
 | Y | U | V | ΔE | Y | U | V | ΔE
Class A | -0.43 | -0.70 | -0.57 | -0.00 |  |  |  | 
Class B | 0.11 | 0.86 | 0.79 | 0.08 | -0.08 | -0.29 | -0.35 | 0.00
Class C | -0.09 | -0.29 | -0.30 | 0.00 | -0.01 | -0.01 | -0.03 | -0.01
Class D | -0.35 | -0.49 | -0.82 | -0.06 | 0.02 | 0.41 | -0.31 | -0.00
Class E |  |  |  |  | -0.52 | -1.24 | -1.74 | -0.00
Overall | -0.17 | -0.09 | -0.16 | 0.01 | -0.12 | -0.22 | -0.52 | -0.00

## Slide 12: Performance evaluation (scenario 2)
CPB fullness with respect to time index without the target bit saturation (B=R, F=0.75B)
CPB fullness with respect to time index with the proposed adaptive lower bound(B=R, F=0.75B)

## Slide 13: Performance evaluation (scenario 2)
CPB fullness with respect to time index with the fixed lower bound (B=R, F=0.75B)
CPB fullness with respect to time index with the proposed adaptive lower bound(B=R, F=0.75B)

## Slide 14: Performance evaluation (scenario 2)
The proposed method improves the coding efficiency with 0.02% Y BD-BR gain compared to JCTVC-U0132
  0.01% Y BD-BR gain compared to rate control of HM-16.6 without consideration for the constraint of HRD
Table 1. RD performance of the proposed target bit saturation method compared to rate control of HM without any target bit saturation method (Scenario 2: B=R, F=0.75B)
Table 2. RD performance of the proposed target bit saturation method compared to rate control of HM with the target bit saturation using the fixed lower bound (Scenario 2: B=R, F=0.75B)
 | Random access |  |  |  | Low-delay B |  |  | 
 | Y | U | V | ΔE | Y | U | V | ΔE
Class A | -0.18 | -0.44 | -0.42 | 0.00 |  |  |  | 
Class B | 0.06 | 0.60 | 0.35 | -0.12 | -0.07 | 0.18 | 0.31 | 0.00
Class C | -0.03 | -0.21 | -0.13 | -0.01 | 0.01 | -0.06 | 0.07 | 0.00
Class D | 0.05 | 0.37 | 0.50 | 0.03 | 0.02 | 0.41 | 0.61 | 0.00
Class E |  |  |  |  | 0.00 | 0.00 | 0.00 | 0.00
Overall | -0.02 | 0.11 | 0.09 | -0.03 | -0.02 | -0.15 | -0.27 | -0.00
 | Random access |  |  |  | Low-delay B |  |  | 
 | Y | U | V | ΔE | Y | U | V | ΔE
Class A | 0.00 | 0.85 | 0.95 | 0.00 |  |  |  | 
Class B | 0.06 | 0.60 | 0.35 | -0.12 | -0.07 | 0.18 | 0.31 | -0.00
Class C | -0.03 | -0.21 | -0.13 | -0.01 | 0.01 | -0.06 | 0.07 | 0.00
Class D | 0.05 | 0.37 | 0.50 | 0.03 | 0.02 | 0.41 | 0.61 | 0.00
Class E |  |  |  |  | -0.08 | -0.30 | 0.23 | 0.00
Overall | 0.02 | 0.41 | 0.41 | -0.03 | -0.03 | 0.09 | 0.31 | 0.00

## Slide 15: Conclusion
In this contribution, a way to improve usage of CPB and coding efficiency of the target bits saturation method is proposed
  To improve coding efficiency, this contribution proposes a target bit saturation for each picture using the adaptive lower bound instead of the fixed one
The proposed method performs target bit saturation under the constraint of HRD with 0.15% BD-BR gain compared to JCTVC-U0132