## Slide 1: AHG12: Signaling of decoded motion constrained tile set hash
J. Taquet, N. Ouedraogo, F. Denoual, F. Mazé
28/03/2017

## Slide 2: Context
Requirement:
  Tool to verify that a temporal motion constrained tile set (MCTS) is properly decoded
Target:
  Validation of bitstreams’ decoding in various scenarios
1/5

## Slide 3: Example of scenarios where we want to check that MCTS are properly decoded
mcts_00
Video 0
extraction
encoding
mcts_00
mcts_01
mcts_02
mcts_03
decoding
Video 0
combination
mcts_00
mcts_11
mcts_12
mcts_03
mcts_00
mcts_01
mcts_02
mcts_03
mcts_10
mcts_11
mcts_12
mcts_13
Quality 0
encoding
Quality 1
encoding
decoding
combination
Video 0
Video 1
mcts_00
mcts_01
mcts_02
mcts_03
mcts_10
mcts_11
mcts_12
mcts_13
encoding
encoding
decoding
Scenario 1: Validate decoding of extracted tiles
Scenario 2: Validate decoding of combined tiles
Scenario 3: Validate decoding of combined and shuffled tiles
mcts_01
mcts_10
mcts_03
mcts_12
decoding conform to hash
+mcts_hash
+mcts_hash
+mcts_hash
2/5

## Slide 4
Additional requirements:
  Tool should also allow verifying if only a sub-part (i.e. cropped area) of a temporal motion constrained tile set is properly decoded
Targets:
  Streams for which in-loop filters are applied on the tile boundaries
  Streams for which only a sub part of the tile-set should be reliably decoded
Video 0
combination
mcts_00
mcts_11
mcts_12
mcts_03
mcts_00
mcts_01
mcts_02
mcts_03
mcts_10
mcts_11
mcts_12
mcts_13
Quality 0
encoding
Quality 1
encoding
decoding
Loop-filters-on
decoding conform to hash
Areas not checked with hash
+mcts-partial hash
3/5

## Slide 5: Proposal: decoded_mcts_hash SEI message
Proposal:
  New SEI message
    Refers to temporal motion constrained tile set (MCTS) SEI
    Allow computing the hash on a subpart (crop) of a MCTS region
    Reuse/adapt hash functions already defined for decoded picture hash SEI message
Discussions about regional nesting SEI message with decoded picture hash SEI message
  Decoded picture hash SEI message is not included in listOfRegionNestableMessageTypes
  About hash functions
    With our proposal, the hash functions are well defined for motion constrained tile set rectangular region of tiles
    Decoded picture hash SEI message only defines hash functions at a picture level
  About extraction of hash SEI simultaneously with MCTS extraction
    With our proposal, a parser can easily retrieve the hash information related to a MCTS by checking MCTS identifiers
    Regional nesting SEI do not directly refer to MCTS identifiers
      To extract a MCTS and associated hash(es), a parser would have to check all the rectangular regions (defined in pixels) in regional nesting SEI to see if they are included into one of the MCTS rectangular region of tiles (defined in tile indexes)
      To provide hash(es) for extracted MCTS, there is potential issues with spatial locations of the rectangular regions that may differ between the original stream and the extracted stream
4/5

## Slide 6: decoded_mcts_hash SEI message syntax
decoded_mcts_hash( payloadSize ) { | Descriptor
num_mcts_hash_minus1 | ue(v)
for( n = 0; n <= num_mcts_hash_minus1; n++ ) { | 
mcts_hash_id[ n ] | ue(v)
mcts_hash_tile_rect_idx[ n ] | ue(v)
crop_mcts_hash[ n ] | u(1)
if( crop_mcts_hash[ n ] ) { | 
crop_mcts_hash_with_same_margins[ n ] | u(1)
if( crop_mcts_hash_with_same_margins[ n ] ) | 
crop_mcts_hash_margin[ n ] | ue(v)
else { | 
crop_mcts_hash_top_margin[ n ] | ue(v)
crop_mcts_hash_bottom_margin[ n ] | ue(v)
crop_mcts_hash_left_margin[ n ] | ue(v)
crop_mcts_hash_right_margin[ n ] | ue(v)
} | 
} | 
mcts_hash_type[ n ] | u(8)
for( cIdx = 0; cIdx < ( chroma_format_idc = = 0 ? 1 : 3 ); cIdx++ ) { | 
if( mcts_hash_type = = 0 ) | 
for( i = 0; i < 16; i++) | 
mcts_md5[ n ][ cIdx ][ i ] | b(8)
else if( mcts_hash_type = = 1 ) | 
mcts_crc[ n ] [ cIdx ] | u(16)
else if( mcts_hash_type = = 2 ) | 
mcts_checksum[ n ] [ cIdx ] | u(32)
} | 
} | 
} | 
5/5

## Slide 7: Thank you for your attention.