## Slide 1: JVET-AE0027: Object Tracking SEI
Jill Boyce
Palanivel Guruva reddiar

## Slide 2: Motivation: Object detection and tracking is common workload for end-to-end video systems
Typical steps in intermediate processing stage:
Decode compressed video
Perform analytics on the video to identify object locations using a rectangular bounding box for each picture
Composite video with a graphical outline of the bounding box(es)
Re-encode the video containing bounding box(es)
Smart Cameras
Video Gateway
Data center / Cloud

## Slide 3: Proposal: New object tracking SEI for HEVC and AVC
SEI metadata to indicate rectangular bounding box for multiple objects
Use of SEI metadata has significant advantages over compositing graphical bounding box within video frame
      Un-modified video is available at later stages
      SEI message data can be added to compressed bitstream at intermediate stages without re-encoding, saving significant computational complexity and reducing latency
      Refinement of object tracking parameters is possible at intermediate stages

## Slide 4: Features of proposed syntax & semantics
  List of text labels, each can be used by multiple objects
  Track multiple objects, indicating
    Rectangular bounding box parameters (location and size)
    Text label (optional)
    Detection confidence (optional), with signaled level of precision
  Update bounding box locations of individual objects only as needed, using persistence within persistence scope
  Sequence level indications
    Indicate if coded bitstream is not intended for user viewing
    Indicate if motion information (MVs, modes) were selected to accurately track objection motion, rather than optimizing coding efficiency

## Slide 5: Object tracking SEI message syntax (1 of 2)
object_tracking( payloadSize ) { | Descriptor
object_tracking_seq_parameter_set_id | ue(v)
object_tracking_not_intended_for_viewing_flag | u(1)
object_tracking_true_motion_flag | u(1)
object_tracking_item_label_present_flag | u(1)
object_tracking_item_detection_confidence_info_present_flag | u(1)
if (object_tracking_item_detection_confidence_info_present_flag ) | 
object_tracking_item_detection_confidence_precision_num_bits | u(4)
if ( object_tracking_item_label_ present_flag ) { | 
object_tracking_label_language_present_flag | u(1)
if ( object_tracking_label_language_ present_flag ) { | 
while( !byte_aligned( ) ) | 
object_tracking_zero_bit /* equal to 0 */ | f(1)
object_tracking_label_language | st(v)
} | 
object_tracking_num_new_labels | ue(v)
for( i = 0; i < object_tracking_num_new_labels; i++ ) | 
object_tracking_label_idx[[ i ] | ue(v)
for( i = 0; i < object_tracking_num_new_labels; i++ ) { | 
while( !byte_aligned( ) ) | 
object_tracking_zero_bit /* equal to 0 */ | f(1)
object_tracking_label[[ object_tracking_label_idx[[ i ] ] | st(v)
} | 
} | 

## Slide 6: Object tracking SEI message syntax (2 of 2)
object_tracking_num_items_minus1 | ue(v)
for( i = 0; i <= object_tracking_num_items_minus1; i++ ) { | 
object_tracking_item_idx[[ i ] | ue(v)
object_tracking_new_item_flag[[ object_tracking_item_idx[ i ] ] | u(1)
if ( !object_tracking_new_item_flag[ object_tracking_item_idx[ i ] ] ) | 
object_tracking_item_bounding_box_update_flag[ object_tracking_item_idx[ i ] ] | u(1)
if( object_tracking_new_item_flag[ object_tracking_item_idx[ i ] && object_tracking_item_label_ present_flag ) { | 
object_tracking_item_label_idc[ object_tracking_item_idx[ i ] ] | ue(v)
if( object_tracking_item_bounding_box_update_flag[ object_tracking_item_idx[ i ] ] ¦ ¦ object_tracking_new_item_flag[ object_tracking_item_idx[ i ] ]) { | 
object_tracking_item_top[ object_tracking_item_idx[ i ] ] | u(16)
object_tracking_item_left[ object_tracking_item_idx[ i ] ] | u(16)
object_tracking_item_width[ object_tracking_item_idx[ i ] ] | u(16)
object_tracking_item_height[ object_tracking_item_idx[ i ] ] | u(16)
if ( object_tracking_item_detection_confidence_info_present_flag ) | 
object_tracking_item_detection_confidence[ object_tracking_item_idx[ i ] ] | u(v)
} | 
} | 
} | 

## Slide 7: Example Scenario : Picture 0
BB_B
BB_A
Two objects in the picture
Car: Bounding box A (BB_A)
Person: Bounding box B (BB_B)
object_tracking_item_label_present_flag | 1
object_tracking_num_new_labels | 2
object_tracking_label_idx[ 0 ] | 0
object_tracking_label_idx[ 1 ] | 1
object_tracking_label[ 0 ] | car
object_tracking_label[ 1 ] | person
object_tracking_num_items_minus1 | 1
object_tracking_item_idx[ 0 ] | 0
object_tracking_new_item_flag[ 0 ] | 1
object_tracking_item_idx[ 1 ] | 1
object_tracking_new_item_flag[ 1 ] | 1
object_tracking_item_label_idc[ 0 ] | 0
object_tracking_item_label_idc[ 1 ] | 1
object_tracking_item_top, left, width, height[ 0 ] | BB_A
object_tracking_item_top, left, width, height[ 1 ] | BB_B

## Slide 8: Example Scenario : Picture 1
Two objects in the picture
Same objects as in previous picture. Car stays in same position and person moves.
Car: Bounding box A (BB_A)
(Persists from previous picture, all object details will be re-used)
Person: Bounding box C (BB_C)
(new location in the picture, label details will be reused)
BB_C
BB_A
object_tracking_item_label_present_flag | 1
object_tracking_num_new_labels | 0
object_tracking_num_items_minus1 | 1
object_tracking_item_idx[ 0 ] | 0
object_tracking_new_item_flag[ 0 ] | 0
object_tracking_item_bounding_box_update_flag[ 0 ] | 0
object_tracking_item_idx[ 1 ] | 1
object_tracking_new_item_flag[ 1 ] | 0
object_tracking_item_bounding_box_update_flag[ 1 ] | 1
object_tracking_item_top, left, width, height[ 1 ] | BB_C

## Slide 9: Example Scenario : Picture 2
Three objects in the picture
Previous car no longer in picture. Person moved, different car entered, dog entered picture.
Car: Bounding box D (BB_D)
(new object in the picture, previous labels will be reused)
Person: Bounding box E (BB_E)
(new location in the picture, previous labels will be reused )
Dog: Bounding box (BB_F)
(new object in the picture)
BB_D
BB_F
BB_E
object_tracking_item_label_present_flag | 1
object_tracking_num_new_labels | 1
object_tracking_label_idx[ 0 ] | 2
object_tracking_label[ 2 ] | dog
object_tracking_num_items_minus1 | 2
object_tracking_item_idx[ 0 ] | 1
object_tracking_new_item_flag[ 1 ] | 0
object_tracking_item_bounding_box_update_flag[ 1 ] | 1
object_tracking_item_idx[ 1 ] | 2
object_tracking_new_item_flag[ 2 ] | 1
object_tracking_item_label_idc[ 2 ] | 0
object_tracking_item_idx[ 2 ] | 3
object_tracking_new_item_flag[ 3 ] | 1
object_tracking_item_label_idc[ 3 ] | 2
object_tracking_item_top, left, width, height[ 1 ] | BB_D
object_tracking_item_top, left, width, height[ 2 ] | BB_E
object_tracking_item_top, left, width, height[ 3 ] | BB_F

## Slide 10: Object tracking SEI message – Salient Features
  Ability to associate video analytics data with the frame resolution (object_tracking_seq_parameter_set_id)
  Ability to associate video analytics data : For human visual perception (or) for machine consumption (object_tracking_not_intended_for_viewing_flag)
  Ability to communicate the accuracy of the represented motion : True motion (or) approximated motion (object_tracking_true_motion_flag)
  Ability to transmit label and confidence information associated with the detected objects (object_tracking_item_label_present_flag & object_tracking_label_language_present_flag)
  Ability to configure the precision of the object detection confidence (object_tracking_item_detection_confidence_precision_num_bits)
  Ability to support different label languages (object_tracking_label_language)
  Ability to persist existing object information and signal only the new and obsolete objects

## Slide 11: Summary
New SEI message proposed for HEVC and AVC
Addresses key shortcomings of existing practices in surveillance applications
Proposed syntax is flexible and efficient