## Slide 1: Non-SCE4: Inter-layer switchable upsampling filters for spatial scalability
JCTVC-M0233
Presented by Shan Liu
13th JCT Meeting in Incheon
18-26 April 2013
Zhenzhong Chen, PoLin Lai, Ximin Zhang, Shan Liu, Shawmin Lei

## Slide 2: CU Level Switchable Up-sampling
Current approach in SHM1.0
  8 tap Luma upsampling filter and 4 tap Chroma upsampling filter.
However, a long-tap filter may include outliers from the adjacent object
Fig. 1. Illustration of interpolation of pixel close to the object boundary.

## Slide 3: CU Level Switchable Up-sampling
Switch between long- and short-tap filters
  Additional Luma filter
    Reuse the existing 4-tap Chroma filters
  Additional Chroma filter
    2-Tap DCT up-sampling filters
  CU-level Switch with On/Off flag on INTRA_BL framework.
  A 3-tap Gaussian filter {7, 50, 7} applied for the zero-phase position pixel when CU is upsampled by the shorter tap filter (flag = On).
    Not introduce additional filtering step.
Phase | Filter coefficients
1/4 | { 49, 15},
1/3 | { 44, 20},
3/8 | { 41, 23},
1/2 | { 32, 32},
7/12 | { 26, 38},
2/3 | { 20, 44},
7/8 | { 7, 57},
11/12 | { 4, 60}

## Slide 4: Results (Anchor: SHM1.0)
INTRA_BL framework
switchable upsampling filter |  |  |  |  | 
 | EL + BL |  |  | Enc | Dec
 | Y | U | V |  | 
AI-2x | -0.2% | 0.0% | -0.1% | 113.9% | 94.5%
AI-1.5x | 0.0% | 0.0% | 0.1% | 112.1% | 94.8%
RA-2x | -0.2% | 0.0% | 0.0% | 103.9% | 83.0%
RA-1.5x | 0.1% | 0.1% | 0.1% | 103.2% | 84.0%
LDP-2x | -0.8% | -0.6% | -0.6% | 104.2% | 82.4%
LDP-1.5x | -0.3% | -0.4% | -0.3% | 103.4% | 83.7%
LDP-2x | -0.3% | -0.3% | -0.4% | 103.0% | 81.6%
LDP-1.5x | 0.1% | -0.2% | -0.2% | 102.8% | 82.6%

## Slide 5: Results (Anchor: SHM1.0)

## Slide 6: Complexity Assessment
Summary
Worst case: same as Anchor.
 | AI HEVC 2x |  |  |  |  | AI HEVC 1.5x |  |  |  | 
 | 8b/8b | 64b/256b | 64b/512b | Mults | Adds | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
Class A | 92% | 96% | 97% | 91% | 90% |  |  |  |  | 
Class B | 87% | 96% | 97% | 83% | 80% | 93% | 92% | 92% | 90% | 89%
Overall | 88% | 96% | 97% | 85% | 83% | 93% | 92% | 92% | 90% | 89%
 | RA HEVC 2x |  |  |  |  | RA HEVC 1.5x |  |  |  | 
 | 8b/8b | 64b/256b | 64b/512b | Mults | Adds | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
Class A | 99% | 100% | 100% | 98% | 97% |  |  |  |  | 
Class B | 99% | 100% | 100% | 97% | 96% | 99% | 99% | 98% | 97% | 97%
Overall | 99% | 100% | 100% | 97% | 96% | 99% | 99% | 98% | 97% | 97%
 | LD-P HEVC 2x |  |  |  |  | LD-P HEVC 1.5x |  |  |  | 
 | 8b/8b | 64b/256b | 64b/512b | Mults | Adds | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
Class A | 98% | 99% | 99% | 95% | 95% |  |  |  |  | 
Class B | 97% | 99% | 99% | 93% | 92% | 97% | 96% | 96% | 92% | 91%
Overall | 98% | 99% | 99% | 94% | 93% | 97% | 96% | 96% | 92% | 91%
 | LD_B HEVC 2x |  |  |  |  | LD-B HEVC 1.5x |  |  |  | 
 | 8b/8b | 64b/256b | 64b/512b | Mults | Adds | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
Class A | 99% | 99% | 99% | 97% | 97% |  |  |  |  | 
Class B | 98% | 99% | 99% | 96% | 95% | 98% | 98% | 98% | 96% | 95%
Overall | 98% | 99% | 99% | 96% | 96% | 98% | 98% | 98% | 96% | 95%

## Slide 7: Conclusion
Inter-layer switchable up-sampling filters for spatial scalability.
Results are reported compared with SHM1.0 anchor.
  BD rate reduction
    -0.2% (AI 2x), -0.0% (AI 1.5x), -0.2% (RA 2x), +0.1% (RA 1.5x), -0.8% (LD-P 2x), -0.3% (LD-P 1.5x).
  Enc time
    113.9% (AI 2x), 112.1% (AI 1.5x), 103.9% (RA 2x), 103.2% (RA 1.5x), 104.2% (LD-P 2x), 103.4% (LD-P 1.5x).
  Dec time
    94.5% (AI 2x), 94.8%(AI 1.5x), 83.0% (RA 2x), 84.0% (RA 1.5x), 82.4% (LD-P 2x), 83.7% (LD-P 1.5x).
    Performing upsampling on INTRA_BL block only.
    Shorter tap upsampling results in lower dec time.
Thank Sony for Crosscheck (JCTVC-M0400).

## Slide 8
www.mediatek.com