## Slide 1: JCTVC-Q0074 SEI message for Colour Mapping Information
P. Andrivon, P. Bordes, E. François
17th JCT-VC Meeting: Valencia, 27 March - 4 April 2014

## Slide 2: Colour Mapping Info SEI
  Context
    Migrating to WCG vs legacy
    Different services, different grades
    Preserve colour fidelity from studios
  Issues previously adressed
    Scope: clarified
    Complexity: low + using existing resources from targeted devices
    Persistence: same as Tone Mapping SEI…

## Slide 3: Colour Mapping Info SEI: Visually…
Colour graded BT.709
Colour graded BT.2020 converted to BT.709
BT.2020 colour mapped to BT.709 using proposal
Colour graded BT.2020 displayed as is on BT.709 display
JCTVC-P0126

## Slide 4: Colour Mapping Info SEI: Applications
    Example: backward compatibility
      Aid mapping if Rec. 2020 signal rendering is optional for UHD-1 phase 1 devices
Production
Rec.709 grade
WCG grade
WCG to Rec.709
gamut mapped
WCG to Rec.709
colour mapping SEI
colour
metadata
Displays
WCG display
Rec.709 legacy
display
HEVC STB
WCG to Rec.709
Colour mapping SEI
Rec.709 display
Wide CG display
Legacy
display
HEVC
distribution
WCG + metadata
Home
Distribution

## Slide 5: Colour Mapping Info SEI: Proposition
    Syntax/semantics inspired from:
      Targeted color space: VUI
      Model:
        Tone Mapping SEI + Film Grain SEI
        Leveraging existing CE resources
    Editorial: identified issues addressed
    Synchronization:
      One SEI per long sequence gives visually coherent results
      Optimal is one per shot/sequence
    Softwares provided:
      SEI implementation in encoder and decoder (HM13.0/RExt6.0)
      Model parameters identification

## Slide 6: Colour Mapping Info SEI: Syntax proposition
Target colour space characteristics
Piece-wise linear model per component
Piece-wise linear model per component
3x3 matrix

## Slide 7: Colour Mapping Info SEI: Conclusion
    Aid colour mapping
      Preserving content creator intent
      Keeping TV sets manufacturers differentiation
      Benefits already shown in demo
    Low-complexity model
      use limited resources from CE devices
      softwares supplied
        on top of HM13.0-RExt6.0
        parameters identification provided for the model