## Slide 1: Summary report for Core Experiment 2 on Intra block copy memory access
JCTVC-U0022

## Slide 2: CE2 Tests and cross-checks
Doc No. | Title | Participants | Type
JCTVC-U0034 | CE2: Test 3 on intra block copy constraints on filtering (single-pass encoding decisions) | J. Lainema, M. M. Hannuksela (Nokia) | Proposal
JCTVC-U0053 | CE2 Test 2: Intra block copy constraints on filtering | G. Laroche, G. Malard, C. Gisquet, P. Onno (Canon) | Proposal
JCTVC-U0078 | CE2 : Test 5 on intra block copy constraints on prediction | K. Rapaka, V. Seregin, R. Joshi, T. Hsieh, M. Karczewicz (Qualcomm) | Proposal
JCTVC-U0035 | CE2: Crosscheck of Test 2 on intra block copy constraints on filtering (frame level encoding decisions) | Nokia | Crosscheck
JCTVC-U0060 | CE2: Cross check of Test 5 on Intra block copy constraints on Bi-prediction samples with use of local cache | Canon | Crosscheck
JCTVC-U0082 | CE2: cross check of CE2 Test 1: Intra block copy constraints on filtering | Qualcomm | Crosscheck

## Slide 3: Motivation of CE2
To maintain the worst case memory accesses within HEVC v1 limits
To reduce the average case memory accesses
Report objective coding efficiency of the tested methods
Report Average/worst memory access analysis
Report subjective analysis of the tested methods (not done).

## Slide 4: Test 2: Intra block copy constraints on filtering (Picture level decision process)
Decoding process
A flag is signaled at CTU to specify
  De-blocking and SAO on/off control and
  Availability for IBC referencing
Current CTU and previous CTU are always considered available
Filtering process is modified to allow filtering across the CTU
boundaries and disable for edges only within the CTU boundary
Encoding Process
Encoder decides after analysing BV distribution whole frame (assumes out of loop deblocking and SAO design)
Incorporates encoding optimization proposed in JCTVC-I0184 to SCM (not adopted into HM)

## Slide 5: Test 3: Intra block copy constraints on filtering (single–pass decision process)
Decoding process
A flag is signaled at CTU to specify
  De-blocking and SAO on/off control
  Availability for IBC referencing
Current CTU and previous CTU are always considered available
Filtering process is modified to allow filtering across the CTU
boundaries and disable for edges only within the CTU boundary
Encoding Process
After encoding a CTU, decision is made if the CTU is to be used as a reference for future IBC blocks based on some statistics.

## Slide 6: CE2 : Test 5 on intra block copy constraints on prediction
Test 5.1
Decoding process
CTU is marked as unavailable for IBC reference if it has at least one 8x8 Bi-predicted block
Current CTU and previous CTU are always considered available
Encoding Process
After encoding a CTU, decision is made if the CTU is to be used as a reference for future IBC blocks based on existence of 8x8 Bi-prediction blocks.
Test 5.2
Decoding process
when IBC is enabled, bi-prediction for 8x8 block is disallowed.

## Slide 7: CE2 : Test 5 on intra block copy constraints on prediction
Test 5.3
Decoding process
when IBC is enabled and use_integer_mv_flag = 0, bi-prediction for 8x8 block is disallowed.
Test 5.4
Decoding process
CTU is marked as unavailable for IBC reference if it has at least one 8x8 Bi-predicted block and use_integer_mv_flag = 0
Current CTU and previous CTU are always considered available
Encoding Process
After encoding a CTU, decision is made if the CTU is to be used as a reference for future IBC blocks based on existence of 8x8 Bi-prediction blocks.

## Slide 8: 444 Lossy AI configuration comparisons –Full frame CTC
 | 444 Lossy All Intra |  |  |  |  | 
Tests | Test 3 | Test 2 | Test 5.1 | Test 5.2 | Test 5.3 | Test 5.4
RGB, TGM | 1.3% | 0.6% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, MC | 2.1% | 1.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Ani. | 0.5% | 0.3% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, CC | 0.1% | 0.3% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM | 1.7% | 1.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, MC | 2.3% | 1.3% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Ani. | 1.0% | 0.7% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, CC | 0.1% | 0.5% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 9: 444 Lossy RA configuration comparisons - Full frame CTC
 | 444 Lossy Random Access |  |  |  |  | 
Tests | Test 3 | Test 2 | Test 5.1 | Test 5.2 | Test 5.3 | Test 5.4
RGB, TGM | 2.6% | 0.7% | 3.2% | 0.4% | 0.4% | 2.1%
RGB, MC | 1.2% | 0.5% | 2.0% | 0.6% | 0.6% | 2.0%
RGB, Ani. | 0.1% | 0.1% | 0.0% | 1.1% | 1.1% | 0.0%
RGB, CC | 0.1% | 0.1% | 0.0% | 0.8% | 0.8% | 0.0%
YUV, TGM | 3.0% | 1.1% | 2.8% | 0.3% | 0.3% | 1.8%
YUV, MC | 1.4% | 0.8% | 2.0% | 0.4% | 0.4% | 2.0%
YUV, Ani. | 0.4% | 0.2% | 0.0% | 0.7% | 0.7% | 0.0%
YUV, CC | 0.1% | 0.2% | 0.0% | 0.8% | 0.8% | 0.0%

## Slide 10: 444 Lossy LD configuration comparisons - Full frame CTC
 | 444 Lossy Low-delay B |  |  |  |  | 
Tests | Test 3 | Test 2 | Test 5.1 | Test 5.2 | Test 5.3 | Test 5.4
RGB, TGM | 3.8% | 0.9% | 4.8% | 0.4% | 0.3% | 2.5%
RGB, MC | 1.7% | 0.4% | 2.8% | 1.1% | 1.0% | 2.6%
RGB, Ani. | 0.0% | 0.0% | -0.1% | 1.0% | 1.0% | -0.1%
RGB, CC | 0.0% | 0.0% | 0.0% | 0.8% | 0.8% | 0.0%
YUV, TGM | 3.8% | 1.2% | 4.5% | 0.4% | 0.3% | 2.3%
YUV, MC | 2.0% | 0.8% | 2.7% | 0.7% | 0.7% | 2.6%
YUV, Ani. | 0.2% | 0.1% | -0.1% | 0.6% | 0.6% | -0.1%
YUV, CC | 0.0% | 0.0% | 0.0% | 0.4% | 0.4% | 0.0%

## Slide 11: Related CE proposals
Doc No. | Title | Proponents | Type
JCTVC-U0065 | CE2-related: Intra block copy searching constraints for reducing worst case bandwidth | T.-D. Chuang, C.-Y. Chen, Y.-W. Huang, S. Lei (MediaTek) | Proposal
JCTVC-U0077 | On chroma motion vector derivation for intra block copy | X. Xu, S. Liu, S. Lei (MediaTek) | Proposal
JCTVC-U0079 | HLS : On Intra block copy signaling control | K. Rapaka, V. Seregin, R. Joshi, M. Karczewicz, Y.-K. Wang (Qualcomm), A. Tourapis, Y. Su, D. Singer (Apple) | Proposal
JCTVC-U0080 | Intra block copy chroma interpolation for Non-444 | K. Rapaka, V. Seregin, R. Joshi, M. Karczewicz (Qualcomm) | Proposal
JCTVC-U0103 | On chroma derivation of intra block copy for non-444 video | X. Xiu, Y. Ye, Y. He (InterDigital) | Proposal

## Slide 12: Worst case Memory BW Analysis
 | With outputting filtered pixels (bandwidth in HEVC) |  | With outputting filtered and unfiltered pixels (bandwidth in HEVC-SCC) | 
Memory configuration and burst | 8×8 bi-pred. | 4×8 uni-pred. | 8×8 bi-pred. | 4×8 uni-pred.
4×1, burst 1 | 10.375(Y) + 6.5*2 (C) = 23.2375 | 8.5(Y) + 5.125*2(C) = 18.75 | 24.2375 | 19.75
4×2, burst 1 | 11(Y) + 7*2(C) = 25 | 9(Y) + 5.5*2(C) = 20 | 26 | 21
8×1, burst 1 | 12.25(Y) + 9.25*2(C) = 30.75 | 12.25(Y)+6.5*2(C) = 25.25 | 31.75 | 26.25
8×2, burst 1 | 13 (Y) + 10*2(C) = 33 | 13(Y)+7*2(C) = 27 | 34 | 28
 | Test 2 | Test 3 | Test 5.1 | Test 5.2 | Test 5.3 | Test 5.4
Memory configuration and burst | 8×8 bi-pred. | 8×8 bi-pred. | 8×8 bi-pred. | 8×8 bi-pred. | 8×8 bi-pred. | 8×8 bi-pred.
4×1, burst 1 | 23.2375 | 23.2375 | 23.2375 | 19.75 | 19.75 | 23.2375
4×2, burst 1 | 25 | 25 | 25 | 21 | 21 | 25
8×1, burst 1 | 30.75 | 30.75 | 30.75 | 26.25 | 26.25 | 30.75
8×2, burst 1 | 33 | 33 | 33 | 28 | 28 | 33