## Slide 1: On bi-prediction restriction when intra block copy is enabled
JCTVC-V0048
K. Rapaka, V. Seregin, R. Joshi, M. Karczewicz (Qualcomm)

## Slide 2: Introduction
In the current WD, an 8x8 bi-prediction restriction is applied
  when IBC is enabled (i.e curr_pic_as_ref_enabled_flag is equal to 1) or
  adaptive motion vector resolution is enabled (i.e use_integer_mv equal to 1)
This restriction reduces worst-case memory accesses by 7-9% when IBC is used.
This proposal, proposes to relax existing 8x8 bi-prediction restriction based on the characteristic of the motion vector.

## Slide 3: Proposal
In this contribution, it is proposed to improve the current bi-prediction restriction for intra block copy as follows:
  The 8x8 bi-prediction is restricted when all of the following conditions are true:
    IBC is enabled for the current block based on slice, picture or sequence level IBC control
    use_integer_mv is equal to zero for the current slice
    Both MVs of an 8x8 bi-predicted block are
      not integer-pel (fractional-pel accuracy)
      not equal
      not from the same reference picture

## Slide 4: Experimental Results – 444 CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | -0.5% | -0.6% | -0.6%
RGB, camera captured, 1080p | -0.2% | -0.3% | -0.2%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.2% | -0.3% | -0.2%
YUV, Animation, 720p | -0.3% | -0.3% | -0.4%
YUV, camera captured, 1080p | -0.2% | -0.1% | -0.2%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.6% | -0.5% | -0.5%
RGB, Animation, 720p | -0.6% | -0.7% | -0.7%
RGB, camera captured, 1080p | -0.3% | -0.3% | -0.3%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.2% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.4% | -0.6%
YUV, Animation, 720p | -0.4% | -0.5% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.1% | -0.2%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
444 Lossy Full frame IBC CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | -0.5% | -0.6% | -0.6%
RGB, camera captured, 1080p | -0.2% | -0.2% | -0.2%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.1%
YUV, Animation, 720p | -0.3% | -0.3% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.1% | -0.2%
Enc Time[%] | 83% |  | 
Dec Time[%] | 84% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.3% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.6% | -0.5% | -0.4%
RGB, Animation, 720p | -0.6% | -0.8% | -0.8%
RGB, camera captured, 1080p | -0.2% | -0.3% | -0.3%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.2% | -0.3%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.3% | -0.4%
YUV, Animation, 720p | -0.3% | -0.4% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.2% | -0.2%
Enc Time[%] | 95% |  | 
Dec Time[%] | 92% |  | 
444 Lossy local search IBC CTC

## Slide 5: Experimental Results – 420 CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.2% | -0.1%
YUV, Animation, 720p | -0.2% | -0.4% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 102% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV, text & graphics with motion, 1080p & 720p | -0.2% | -0.1% | -0.3%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.1% | -0.1%
YUV, Animation, 720p | -0.2% | 0.1% | 0.0%
Enc Time[%] | 102% |  | 
Dec Time[%] | 103% |  | 
420 Lossy full frame IBC CTC

## Slide 6: Conclusion
It is reported that the proposed approach provides objective bit rate reductions of 0.5 % and 0.3% for Random access 720p Animation RGB and YUV categories, respectively over SCM-5.0 anchor. It is reported that the proposed approach provides objective bit rate reductions of 0.6 % and 0.4% for Low delay B 720p Animation RGB and YUV categories, respectively over SCM-5.2 anchor.
The worst case memory accesses of the proposed method based on JCTVC-U0175 are not increased over the current WD.
We would like to Thank MediaTek for cross-checking the proposal