## Slide 1: Best practices for HDR/WCG
JCTVC-V0053 / MPEG m36998

## Slide 2: Summary
Workflow precision
Grading: managing color volume
  Esp. P3 within BT.2020
Video conversion steps towards encoder input
  Overall goal: try to align with CE1 recommendations
  Linear to non-linear signal conversion precision
  Color space conversion from primaries to YCbCr
  Chroma resampling from 4:4:4 to 4:2:0
  Pixel-wise micro re-grading color volume adjustment
HEVC encoder parameters
  CE1 common conditions translated to x265.

## Slide 3: Workflow precision
As explained in U0047, at least 24 bits of linear light precision is needed to maintain JND on content that has a final ODT target 10-bit PQ (ODT) output.
It is recommended to use 64-bit (double float) for the color space conversion steps, esp. for iterative system (RGB->4:2:0 YCbCr->RGB) encoding loops.

## Slide 4: Color Volume
BT.2020 is almost a pure superset of P3 -- Almost all colors of P3 contained within BT.2020.
Some adjustment needed when converting P3 content to BT.2020 due to P3 red that is slightly outside BT.2020 gamut.
Clipping less desirable than color remapping.

## Slide 5: Grading: managing color volume
D65 white point
P3 magenta
Green BT.2020 Primary
Blue BT.2020 Primary
Red BT.2020 primary
2020 cyan
BT.2020 color gamut
P3 gamut
Note that P3 red is slightly outside BT.2020 gamut

## Slide 6: Out of gamut content
Pixels may be out of gamut when converted from a large source color space (XYZ) to a smaller space.
Pixels may also stray out of gamut due to processing (filter overshoot, ringing…)
Some workflow stages force pixels inside range after clipping, but may go out of range when pixels are converted to another temporary color work space.
Tone mapping / re-shaper operations in RRT or ODT may undo range set by earlier workflow stages.

## Slide 7: Common core conversion stages
OETF
Color Space Conversion (RGB to YCbCr NCL)
Grading, color timing, tone mapping, noise filtering, etc.
Chroma resample 4:4:4 to 4:2:0
Main10 HEVC or High10 AVC Encode
Y
10
Cb
10
Cr
10
Y’
10+
Cb
10+
Cr
10+
R’
12+
G’
12+
B’
12+
R
24+
G
24+
B
24+
Conversion of signal from linear light to (perceptually uniform) non-linear brightness
Conversion of non-linear primaries to non-constant luminance color difference space
Format conversion from 4:4:4 YCbCr-NCL to 4:2:0 YCbCr-NCL
SMPTE ST 2084
ITU-R BT.2020
(user-defined)
(user-defined)
(Encoder)

## Slide 8: OETF
Many products will approximate linear to PQ conversion via hardware LUT of piece-wise linear or spline segments along pivots (e.g. 16 or 32).
Transcoding accuracy more critical: same results after iterations of linear  PQ followed by full ST 2084 spec. PQ  linear via 10-bit (1024 entry) LUT
  Quantization noise from in-between steps of color conversion and resampling could also be factored.

## Slide 9: Color conversion
Small gains by using double-precision (64-bit) float precision in the BT.2020 R’G’B’ to Y’Cb’Cr’ NCL conversion step
BT2020RGBtoYCbCrNCL matrix:
  [0.262699236013774 0.678001738734420 0.059299025251807
  -0.139629656645994 -0.360370861451270 0.500000518097265
  0.500000518097265 -0.459786883720616 -0.040213634376649]
Use exact inverse of matrix in iterative system coding loops

## Slide 10: Chroma resampling filters
Small energy past 0.5 (half-band)
4:2:0 -> 4:4:4 Lanczos serves as a sharp upsampling filter (from JCTVC-U0041)
Recommended windowed-sync 4:4:4 to 4:2:0 filter from JCTVC-U0041 derived from JVT-I0018 has less ringing and energy past half-band than traditional FIR 4:4:4 to 4:2:0 filters.

## Slide 11: Coefficients (from HDRTools)
In HDRTools, the following parameters are recommended:
ChromaDownSamplerFilter=6 (4:4:4 to 4:2:0) [18-taps, 12 non-zero multiplies], FilterUsingFloats=1
  Co-sited: 15.0, -0.01716352771649 * 512, 0.0, +0.04066666714886 * 512, 0.0, -0.09154810319329 * 512, 0.0, 0.31577823859943 * 512, 0.50453345032298 * 512, 0.31577823859943 * 512, 0.0, -0.09154810319329 * 512, 0.0, 0.04066666714886 * 512, 0.0, -0.01716352771649 * 512, +256.0, 9.0
  Non-cosited: 16.0, -0.00945406160902 * 512, -0.01539537217249 * 512, 0.02360533018213 * 512, 0.03519540819902 * 512, -0.05254456550808 * 512, -0.08189331229717 * 512, 0.14630826357715 * 512, 0.45417830962846 * 512, 0.45417830962846 * 512, 0.14630826357715 * 512, -0.08189331229717 * 512, -0.05254456550808 * 512, 0.03519540819902 * 512, 0.02360533018213 * 512, -0.01539537217249 * 512, -0.00945406160902 * 512 , +256.0, 9.0
ChromaUpsampler=4 (4:2:0 to 4:4:4), UseAdaptiveFiltering=1, FilterUsingFloats=1
  Co-sited phase 0: 2.0, 0.0, +256.0, +128.0, 8.0
  Non-cosited phase 0: 6.0, +2.0, -18.0, +70.0, +228.0, -34.0, +8.0, +128.0, 8.0
  Co-sited phase 1: 6.0, +6.0, -34.0, +156.0, +156.0, -34.0, +6.0, +128.0, 8.0
  Non-co-sited phase 1: 6.0, +8.0, -34.0, +228.0, +70.0, -18.0, +2.0, +128.0, 8.0
Note that BT.2020 requires co-sited horizontal and vertical 4:2:0 samples chroma_loc_type* = 2 (HEVC , AVC bitstream defaults to horizontal co-sited, vertically interstitial sub-pel locations, i.e. Chroma_loc_type* = 0)

## Slide 12: Luma adjustment (micro re-grading)
RGB
To
XYZ
Compare
RGB to XYZ
Y’CbCr
to
R’G’B’
TF-1
TF-1
TF-1
R’
G’
B’
R
G
B
Original pixel
R
G
B
Adjust Y’
EOTF
See next slide for example adjustment algorithm

## Slide 13: Adjustment operation (binary search example)
RGB to CIE 1931 XYZ
RGB to 4:2:0 Y’Cb’Cr’
Yref
4:2:0 to 4:4:4
Y’low= 64
Y’mid=512
Y’high=940
Y’mid
Y’Cb’Cr’
to XYZ
Y > Yref
?
Y’mid= (Y’high + Y’low)/2
Y’high =Y’mid
Y’low =Y’mid
Yes
No
Y’high > Y’low
?
4:4:4
Cb’Cr’
Init Y’mid
Y’mid
Initial settings (for 10-bit legal range)
Y
Yes
No
Exit
Input RGB
Output 4:2:0 Y’Cb’Cr’
final Y’mid
Cb’Cr’
Y’ binary tree branch adjustment loop
Iterations=BitDepth_Y
choose lower interval
choose upper interval
Cb,Cr are not altered (~preserve hue)

## Slide 14: HDRTools activation of micro re-grading
ClosedLoopConversion=6
ClosedLoopIterations=10
original
decoded
Micro re-graded & decoded

## Slide 15: Micro re-grading through luma adjustment
Ideally, colorist would (macro) re-grade content (scene by scene or across program span for consistency) that has gone through RGB->4:2:0 YCbCr + compression chain in order to stay within monitor (ST 2086) and/or signal container (video_full_range_flag=0 VUI) limits.
This process however would potentially entail unlimited re-grade-to-encode iterations.
As a last step, micro re-grading alters Y’ on a pixel-basis, but leaves Cb’,Cr’ intact in an attempt to maintain hue (avoid clipping of RGB to wrong color).

## Slide 16: Encoding parameters
Essential:
  Chroma Qp offset: -6 for Cb and Cr. [likely update to Ericsson Qp formula: m37179 and m37439]
  VUI and SEI
  CU-level quantization (64x64 to 8x8)
Recommended:
  Use x265 (HM reference encoder does not have adaptive quantizer… can make 50% difference in bitrate)
  aq_mode = 3 (AQ enabled with auto-variance and bias to dark scenes) for best results in dark, flat picture regions most susceptible to noise and posterization in PQ/HLG signals.
  Will consider HEVC HM reference encoder in future as new adaptive quantizers (local Qp) are incorporated.