## Slide 1: Simplification of the common test condition for fast simulation
Author/ Email: Xiang Ma, Huanbang Chen, Haitao Yang
maxiang6@huawei.com

## Slide 2: Background
Many new coding tools
  Efficiency
    RA:-20.01%
    AI:-13.99%
  Simulation time
    different job, different time
    decided by longest job
      RA: about 10days(Nebuta,QP22)
      AI: about 7days(Nebuta,QP22)
    4K sequences
  ClassA:2560x1600; 4K:4096x2160, 3840x2160
  Time: 30days?
  Simplified simulation method
Chart: RA, QP22(h)
| Traffic | Nebuta | SteamLocomotive | Kimono | BQTerrace | BasketballDrill | RaceHorses | ChinaSpeed
 | 27.5809 | 233.1055 | 85.2204 | 30.855 | 97.9356 | 13.7085 | 2.8955 | 30.1916

## Slide 3: Prediction structure in RA configuration
Prediction structure in RA configuration
  Open GOP
  Leading pictures
Segment1
Segment0
Segment2
Leading pictures
Leading pictures

## Slide 4: Parallel encoding for RA configuration
Parallel encoding
  Parallel in RAS level
  Log file analysis
    VPS,SPS,PPS

## Slide 5: Simulation results via different methods(RA)
JEM1.0 VS HM16.6
  Full sequence
  RAS in parallel
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A | -20.81% | -29.93% | -23.77% | 551% | 585%
Class B | -21.27% | -13.17% | -9.24% | 523% | 660%
Class C | -20.65% | -14.78% | -18.20% | 602% | 777%
Class D | -20.55% | -9.84% | -12.06% | 609% | 933%
Class E |  |  |  |  | 
Class F | -16.45% | -14.81% | -14.54% | 450% | 390%
Overall (Ref) | -20.01% | -16.35% | -15.26% | 543% | 643%
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A | -20.80% | -29.93% | -23.81% | 594% | 680%
Class B | -21.28% | -13.17% | -9.34% | 544% | 681%
Class C | -20.64% | -14.84% | -18.26% | 604% | 794%
Class D | -20.55% | -9.90% | -12.10% | 664% | 879%
Class E |  |  |  |  | 
Class F | -16.38% | -15.00% | -14.68% | 476% | 385%
Overall (Ref) | -20.00% | -16.41% | -15.34% | 572% | 660%
Mismatch factors
  CABAC context initialization
    CABAC_INIT_PRESENT_FLAG
    VCEG_AZ07_INIT_PREVFRAME
  ALF
    COM16_C806_ALF_TEMPPRED_NUM
  SAO
    Only in last RAS(short)

## Slide 6: AI simulation using snapshot of full-length sequence
Snapshot method
  RAP pictures in RA configuration
  Form smaller sequences

## Slide 7: Simulation results via different methods(AI)
JEM1.0 VS HM16.6
  Full sequence
  Snapshot method
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A | -15.38% | -23.49% | -20.05% | 2138% | 215%
Class B | -13.82% | -8.76% | -6.20% | 1965% | 180%
Class C | -14.84% | -11.77% | -14.91% | 1911% | 209%
Class D | -11.79% | -7.95% | -9.36% | 1928% | 163%
Class E | -15.75% | -11.97% | -14.40% | 1480% | 208%
Class F | -12.85% | -11.56% | -11.59% | 1588% | 226%
Overall (Ref) | -13.99% | -12.45% | -12.41% | 1842% | 198%
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A | -15.34% | -23.57% | -20.70% | 1340% | 90%
Class B | -13.77% | -8.87% | -6.19% | 2177% | 172%
Class C | -14.69% | -11.53% | -14.56% | 2757% | 216%
Class D | -11.71% | -8.12% | -9.06% | 3798% | 417%
Class E | -15.70% | -11.82% | -14.30% | 1798% | 202%
Class F | -12.74% | -11.51% | -11.76% | 1792% | 146%
Overall (Ref) | -13.91% | -12.45% | -12.42% | 2166% | 184%

## Slide 8: Conclusion
Proposed method
  RA
    Performance:
      Could be equal to original sequential encoding results
    Time:
      Only about 1/T of original, (T: sequence duration in second)
  AI
    Performance:
      Very close to original full-length encoding results
    Time:
      Only about 1/IP of original, (IP: intra period in RA)
Suggest to adopt proposed method