## Slide 1: Dequantization and scaling for next generation containers
Jie Zhao, Andrew Segall, Seung-Hwan Kim and Kiran Misra

## Slide 2
Overview
Proposes a change in the de-quantization and scaling process in JEM 1.0
Proposal is motivated by recent work in MPEG/JCT-VC HDR activity
Gains of 2.0% for both AI and RA when re-creating HDR test simulations with JEM 1.0

## Slide 3: Motivation
Motivation
  In last meeting, a study was presented suggesting that QP should vary relative to luma value when coding content in a ST-2084 container
  Tested and confirmed by MPEG/JCT-VC CE1 to provide (significant) benefit
  Incorporated into the MPEG/JCT-VC HDR anchors
Relationship between Y2020 and Y709 for a collection of 20 sequences
Source: COM16-C1030 / m37439 “Performance Investigation of high dynamic range and wide color gamut video coding techniques”

## Slide 4: Motivation
Motivation
  For HEVC and other existing codecs, spatial QP adaption is an appropriate way to handle the ST-2084 container
  However, QP adaptation has draw backs
    Main: Bit-rate overhead
    Limited granularity (8x8 in HEVC)
  JEM is a next generation codec and, so, should operate well with next generation content and containers
  Goal: Consider better support for luma adapted QP in JEM
Source: JCTVC-W0054 for anchor implementation details.

## Slide 5: Proposal
Proposal
  Instead of determining the ST-2084 QP adjustment at the encoder – infer the adjustment at the decoder
  Encoder transmits LUT to decoder in the bit-stream mapping mean to QP adjustment
  Decoder estimates mean value of reconstruction and determines the adjustment
Figure: Change in QP value as a function of the average luma value (est.).
Source: JCTVC-W0054

## Slide 6: Proposal
Proposal
  Estimate the mean of the reconstructed TU at the decoder
    Use reconstructed DC coefficient
    Mean of prediction
  Determine scale factor from LUT
  Scale the coefficients after the secondary transform
  Key issues
    Scaling applied to luma AC coefficients and all chroma coefficients
    Predicted value calculated on CU basis for inter-CU and PU basis for intra-CU
    De-blocking uses adjusted QP (CU QP plus average of scale factor within CU)

## Slide 7: Experimental Results
Experimental Results
  Implemented proposed technique into JEM 1.0
  Also, implemented luma QP adjustment method now used in JCTVC-HDR anchor to JEM 1.0. We use this as our anchor.
  Compared performance of the two methods
    Used HDR test sequences from MPEG/JCT-VC activity
    Used JEM 1.0 CTC except for the note below
  Note
    PSNR must be handled carefully with ST-2084 content
    To simplify the test, we configure the anchor and proposed encoders to generate nearly the same output sample values. This is done by coding with a CU/PU/TU size of 16x16. The 16x16 size was specified as part of the MPEG/JCT-VC activity.

## Slide 8: Experimental Results
 | All Intra | Y | U | V
class A | FireEaterClip4000r1 | -3.1% | -7.0% | 0.4%
 | Market3Clip4000r2 | -1.0% | -1.1% | -1.4%
 | SunRise | -2.4% | 1.0% | -2.8%
class B | BikeSparklers cut 1 | -2.1% | -1.0% | -1.9%
 | BikeSparklers cut 2 | -2.4% | -1.6% | 0.1%
 | GarageExit | -3.3% | -3.0% | -3.0%
class C | ShowGirl2Teaser | -2.7% | -1.6% | -2.6%
class D | StEM_MagicHour cut 1 | -2.4% | -1.3% | -1.9%
 | StEM_MagicHour cut 2 | -1.9% | -0.8% | -0.5%
 | StEM_MagicHour cut 3 | -2.1% | -1.1% | -1.5%
 | StEM_WarmNight cut 1 | -1.3% | -0.6% | -0.4%
 | StEM_WarmNight cut 2 | -1.8% | -0.1% | -1.9%
class G | BalloonFestival | -1.4% | -1.6% | -1.1%
class H | EBU_04_Start | -1.5% | -2.1% | -2.3%
 | EBU_06_Hurdles | -1.3% | -1.3% | -1.4%
Average BD rate |  | -2.0% | -1.6% | -1.5%
Average PSNR Difference |  | -0.02 | -0.01 | -0.01
All Intra Results Proposed vs JEM (with Delta QP)
 | RA | Y | U | V
class A | FireEaterClip4000r1 | -3.0% | -1.3% | -2.6%
 | Market3Clip4000r2 | -1.3% | -1.4% | -1.2%
 | SunRise | -1.4% | -1.2% | -5.0%
class B | BikeSparklers cut 1 | -2.0% | -0.4% | 0.0%
 | BikeSparklers cut 2 | -2.2% | -1.3% | -2.5%
 | GarageExit | -3.1% | -2.2% | -2.0%
class C | ShowGirl2Teaser | -2.3% | -1.0% | -2.8%
class D | StEM_MagicHour cut 1 | -1.8% | -0.4% | -1.4%
 | StEM_MagicHour cut 2 | -2.1% | -1.0% | -1.4%
 | StEM_MagicHour cut 3 | -2.0% | -1.1% | -0.2%
 | StEM_WarmNight cut 1 | -1.5% | 0.9% | 1.7%
 | StEM_WarmNight cut 2 | -1.8% | -0.3% | -2.2%
class G | BalloonFestival | -1.7% | -1.9% | -0.9%
class H | EBU_04_Start | -2.2% | -1.9% | -1.8%
 | EBU_06_Hurdles | -1.4% | -0.7% | -1.2%
Average BD rate |  | -2.0% | -1.0% | -1.6%
Average PSNR Difference |  | 0.01 | 0.01 | 0.00
Random Access Results Proposed vs JEM (with Delta QP)

## Slide 9
Conclusion
Proposed a change in the de-quantization and scaling process in JEM 1.0
Proposal motivated by recent work in MPEG/JCT-VC HDR activity
Gains of 2.0% for both AI and RA when re-creating HDR test simulations with JEM 1.0

## Slide 10: Dequantization and scaling for next generation containers
Jie Zhao, Andrew Segall, Seung-Hwan Kim and Kiran Misra