## Slide 1: Tiles coding improvement for Inter pictures by improved merge list at tile boundaries
JVET-C0026
S. Biplab Raut
Samsung R&D Institute Bangalore, India

## Slide 2: Introduction
Tiles provide parallel coding capability by partitioning a picture into rectangular sections.
Parallelism is achieved by disabling coding dependencies across tile boundaries.
This makes merge mode less favourable at tile boundaries.
In this contribution, a method is proposed to derive new temporal candidates for merge list
at tile boundaries that would benefit merge mode.
spatial neighbours unavailable across tile boundary
motion vector prediction is not possible across
tile boundary
Tile boundaries

## Slide 3: Proposed Merge List Modification
New temporal merge candidates derivation at tile boundaries of Inter picture
  Method applies to PUs with any unavailable spatial neighbours A1, B1, B0, A0, B2
  Reference picture with “collocated_ref_idx” as ref_idx is used
    Reference picture shall store motion information at minimum NxN block level
  Collocated blocks corresponding to unavailable spatial neighbours are fetched
  New temporal merge candidates are derived from the collocated blocks

## Slide 4: Proposed Merge List Modification
Merge List is modified with proposed order of new temporal merge candidates
  Add already available merge candidates to merge list in defined order
  Append new temporal candidates at the end of merge list
  Merge List inclusive of the new temporal candidates is used to find best merge candidate
  Modified Merge List at tile boundaries

## Slide 5: Objective Results
Results on JEM1.0 with 4 tiles:

## Slide 6: Objective Results
Results on JEM2.0 with 4 tiles :

## Slide 7: Conclusion
A modification for merge list derivation is proposed at tile boundaries to
improve tiles coding of Inter pictures.
Improvement of -0.06% reported for LDB and LDP on JEM1.0 with 4 tiles
Improvement of -0.02% and -0.04% reported for LDP and LDP on JEM2.0
with 4 tiles
This proposal can be further explored by JVET for its potential adoption