## Slide 1: Perceptual Quality Assessment Metric MS-SSIM
Author/ Email:
Hong Zhang, Xiang Ma, Yin Zhao, Haitao Yang
summer.zhanghong@huawei.com
maxiang6@huawei.com

## Slide 2: Motivation
Exist metric: MSE or PSNR
  Advantage
    Easy to compute and understand
    Has many desirable mathematical properties
  Problem
    may go to opposite direction of subjective quality
An additional reference metric which can work as an “alarm” is needed ,when PSNR fail

## Slide 3: SSIM & MS-SSIM
SSIM
MS-SSIM
  Reason for MS
    images contain structures that occur over a range of spatial scales
    HVS decomposes visual data into multiscale spatial channel early in the visual pathway

## Slide 4: Performance comparison of different metrics
Image Database | Measure | PSNR | SSIM | MS-SSIM
LIVE JPEG/JPEG2000 [3] | SCC | 0.901 | 0.936 | 0.966
 | KCC | - | - | -
TID2013[4-6] | SCC | 0.640 | 0.637 | 0.787
 | KCC | 0.470 | 0.464 | 0.608
A57[7] | SCC | 0.825 | 0.903 | -
 | KCC | - | - | -
LIVE2006[8-10] | SCC | 0.876 | - | 0.953
 | KCC | - | - | -
VCL@FER[11] | SCC | - | 0.911 | 0.923
 | KCC | - | 0.733 | 0.750
Video Database | Measure | PSNR | SSIM | MS-SSIM
LIVE [12-13] | SCC | 0.368 | 0.526 | 0.736
 | LCC | 0.404 | 0.544 | 0.744
LIVE Mobile [14-16] | SCC | 0.678 | 0.650 | 0.743
 | LCC | 0.691 | 0.664 | 0.708
MCL-V [17] | SCC | 0.464 | 0.648 | 0.623
 | LCC | 0.472 | 0.650 | 0.621
LCC: (Pearson) Linear Correlation Coefficient
SCC: Spearman Correlation Coefficient
KCC: Kendall Correlation Coefficient

## Slide 5: A: BasketballDrill (original)

## Slide 6: B: BasketballDrill(34.980dB, 0.973363)

## Slide 7: C: BasketballDrill(34.640dB, 0.974801)

## Slide 8: A: BQSquare (original)

## Slide 9: B: BQSquare (32.502dB, 0.982089 )

## Slide 10: C: BQSquare (32.036dB, 0.985329 )

## Slide 11: A: RaceHorses (original)

## Slide 12: B: RaceHorses (27.309dB, 0.931476)

## Slide 13: C: RaceHorses (27.206dB, 0.934179)

## Slide 14: Suggestions
  Add MS-SSIM into JEM as an additional quality metric for reference
Tool evaluation procedure for consideration: BD-rates based both PSNR and MS-SSIM are calculated
  PSNR & MS-SSIM goes to the same direction: rely on PSNR, as always
  PSNR & MS-SSIM goes to opposite direction: pay special attention, may require further analysis