## Slide 1: JVET-C0038 – EE2.5: Improvements on adaptive loop filter
Marta Karczewicz, Li Zhang, Wei-Jung Chien, Xiang Li

## Slide 2: Summary
Results of the EE 2.5 testing several modifications to the adaptive loop filter (ALF) in HM16.6 JEM-2.0 are presented.
  Diagonal gradients taken into consideration during classification.
  Geometric transformations of filter coefficients (diagonal, vertical flip and rotation) based on the classification results.
  Prediction from set of the fixed filters.
  Design and software clean ups, e.g.:
    Chroma filter shape is aligned with the luma 5x5 filter shape,
    Context coded bins used for ALF coefficients are replaced by by-pass coded bins with the exception of the on/off flag signalled on the CU level.
  Comparing to previous meeting submission in the software submitted to EE the fixed filter usage is enabled for all frame types.

## Slide 3: Results
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.4% | -0.5% | -0.2% | 97% | 111% | -0.9% | -0.7% | -0.4% | 103.4% | 102.5%
Class A2 | -0.7% | -1.4% | -1.0% | 99% | 111% | -1.3% | -0.4% | -0.6% | 104.2% | 103.0%
Class B | -0.6% | -0.2% | -0.4% | 99% | 113% | -1.0% | -0.3% | -0.6% | 103.4% | 99.3%
Class C | -1.4% | -0.1% | 0.1% | 97% | 105% | -1.2% | -0.2% | -0.1% | 102.1% | 108.1%
Class D | -1.5% | -0.5% | -0.6% | 98% | 107% | -1.4% | -0.7% | -0.8% | 102.8% | 108.3%
Class E | -1.9% | -1.4% | -1.5% | 96% | 105% |  |  |  |  | 
Overall | -1.0% | -0.6% | -0.6% | 98% | 109% | -1.2% | -0.5% | -0.5% | 103.2% | 104.0%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.8% | 0.9% | 0.9% | 101.6% | 101.9% | -0.9% | 0.8% | 0.6% | 106.6% | 107.0%
Class C | -0.9% | -0.3% | -0.1% | 102.3% | 105.4% | -1.2% | -0.2% | 0.4% | 104.3% | 105.0%
Class D | -1.5% | -0.6% | -0.9% | 102.1% | 102.9% | -1.8% | 0.1% | -0.5% | 103.6% | 105.0%
Class E | -1.1% | 1.0% | 0.7% | 105.4% | 100.9% | -2.5% | 0.0% | -0.1% | 107.3% | 102.2%
Overall (Ref) | -1.1% | 0.3% | 0.1% | 102.6% | 102.8% | -1.5% | 0.2% | 0.1% | 105.4% | 105.1%
Anchor: JEM-2.0 (SIMD on).
Test: Anchor + all proposed ALF modifications.

## Slide 4: Results
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.4% | -1.2% | -0.6% | 92% | 111% | -1.1% | -1.1% | -0.5% | 113% | 115%
Class A2 | -1.0% | -1.3% | -1.1% | 93% | 112% | -1.8% | -1.0% | -0.7% | 116% | 116%
Class B | -0.8% | -0.2% | -0.7% | 93% | 109% | -1.4% | -0.3% | -0.4% | 115% | 98%
Class C | -1.9% | -0.1% | 0.0% | 96% | 110% | -1.9% | 0.0% | 0.1% | 113% | 114%
Class D | -2.1% | -0.3% | -0.3% | 98% | 110% | -2.1% | -0.4% | -0.3% | 124% | 111%
Class E | -2.4% | -1.4% | -0.9% | 93% | 108% |  |  |  |  | 
Overall | -1.4% | -0.7% | -0.6% | 94% | 110% | -1.6% | -0.6% | -0.3% | 116% | 110%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -1.0% | 0.5% | 0.9% | 111% | 106% | -1.3% | 0.5% | 0.5% | 114% | 112%
Class C | -1.4% | 0.0% | 0.2% | 112% | 99% | -2.0% | -0.1% | 0.1% | 117% | 105%
Class D | -2.0% | 0.0% | -0.2% | 120% | 106% | -2.4% | -0.7% | -0.2% | 122% | 106%
Class E | -1.7% | 1.9% | 2.8% | 112% | 102% | -3.2% | 0.8% | 0.4% | 120% | 107%
Overall (Ref) | -1.5% | 0.5% | 0.8% | 114% | 103% | -2.1% | 0.1% | 0.2% | 118% | 108%
Anchor: HM16.6 with only ALF enabled (i.e., HM16.6 JEM-2.0 with all tools except ALF disabled, SIMD off).
Test: Anchor + modified ALF.

## Slide 5: Results
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.0% | 0.0% | 0.0% | 99% | 105% | 0.1% | 0.0% | 0.1% | 99% | 89%
Class A2 | 0.1% | 0.1% | 0.1% | 100% | 105% | 0.2% | 0.1% | 0.2% | 100% | 90%
Class B | 0.1% | 0.1% | 0.1% | 99% | 102% | 0.1% | 0.1% | 0.2% | 100% | 89%
Class C | 0.4% | 0.3% | 0.3% | 100% | 98% | 0.3% | 0.1% | 0.1% | 99% | 101%
Class D | 0.5% | 0.2% | 0.3% | 99% | 98% | 0.3% | 0.1% | -0.1% | 98% | 103%
Class E | 0.5% | 0.3% | 0.3% | 100% | 101% |  |  |  |  | 
Overall | 0.3% | 0.2% | 0.2% | 100% | 101% | 0.2% | 0.1% | 0.1% | 99% | 94%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.0% | -0.1% | 0.1% | 105% | 100% | 0.1% | 0.1% | 0.2% | 98% | 95%
Class C | 0.1% | 0.0% | 0.0% | 99% | 98% | 0.1% | -0.3% | -0.4% | 99% | 98%
Class D | 0.1% | -0.4% | -0.4% | 98% | 96% | 0.2% | -0.5% | 0.3% | 98% | 98%
Class E | 0.0% | 0.6% | 0.9% | 98% | 96% | 0.0% | 0.0% | -0.2% | 100% | 101%
Overall (Ref) | 0.1% | 0.0% | 0.1% | 100% | 98% | 0.1% | -0.2% | 0.0% | 99% | 98%
Anchor: JEM-2.0 (SIMD on) with all proposed ALF modifications.
Test: Anchor with disabling prediction from fixed filters.

## Slide 6: Results
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.0% | 0.5% | 0.2% | 99% | 104% | 0.0% | 0.7% | 0.4% | 100% | 102%
Class A2 | 0.0% | 1.4% | 1.0% | 99% | 103% | 0.0% | 0.3% | 0.6% | 100% | 101%
Class B | 0.0% | 0.2% | 0.3% | 100% | 101% | 0.1% | 0.9% | 1.0% | 100% | 100%
Class C | 0.1% | 0.2% | 0.0% | 98% | 98% | 0.1% | 0.9% | 0.7% | 98% | 100%
Class D | 0.0% | 1.5% | 1.8% | 98% | 94% | 0.0% | 1.4% | 1.5% | 99% | 99%
Class E | 0.2% | 1.3% | 1.4% | 99% | 100% |  |  |  |  | 
Overall | 0.1% | 0.8% | 0.7% | 99% | 100% | 0.0% | 0.9% | 0.8% | 100% | 100%
 | Low delay B Main10 |  |  |  |  | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.0% | -0.7% | -0.6% | 100% | 100% | 0.0% | -0.6% | -1.0% | 105% | 96%
Class C | 0.1% | 0.9% | 0.9% | 99% | 99% | 0.0% | 0.6% | 0.2% | 100% | 99%
Class D | 0.0% | 1.0% | 1.2% | 99% | 98% | 0.0% | 0.4% | 1.0% | 98% | 98%
Class E | 0.0% | -0.4% | -0.2% | 99% | 97% | 0.1% | 0.1% | 0.2% | 98% | 98%
Overall (Ref) | 0.0% | 0.2% | 0.3% | 99% | 98% | 0.0% | 0.1% | 0.0% | 101% | 98%
Anchor: JEM-2.0 (SIMD on) with all proposed ALF modifications.
Test: Anchor with disabling the change of chroma filter support.

## Slide 7
Backup slides

## Slide 8: Classification
For the luma component, 2x2 blocks are classified into 25 groups:
To reduce the number of bits required to represent the filter coefficients different classes can be merged.
Directionality in addition to horizontal and vertical gradient is calculated using diagonal gradients:

## Slide 9: Classification
To determine directionality ratio of horizontal and vertical gradient and ratio of diagonal gradients are used.
Texture (D=0): and
Horizontal/Vertical:
Diagonal:
Weak (D=1):
Strong (D=2):
Weak (D=3):
Strong (D=4):

## Slide 10: Geometric Transformation of Filter Coefficients
Geometric transformations are applied to filter coefficients f (k, l) depending on gradient values: , .
  Target aligning directionality of different regions.
  Equivalent to applying transformation to pixels in the filter support region.
Diagonal Flip
Vertical Flip
Rotation

## Slide 11: Fixed Filters and Clean Ups
To improve coding efficiency especially when temporal prediction is not available (intra frames), a set of 16 fixed filters is assigned to each class.
Even when the fixed filter is selected for a given class, the coefficients of the adaptive filter can still be sent for this class - the coefficients of the filter applied to the reconstructed image are sum of both sets of coefficients.
Other:
  Chroma filter shape aligned with luma filter shape.
  Context coded bins used for ALF coefficients have been replaced by by-pass coded bins with exception of on/off flag signalled on CU basis.