## Slide 1: EE1-related: NSST with reduced table size (JVET-D0056)
Oct 15, 2016
Joint Video Exploration Team (JVET)
DMC R&D Center
Kiho Choi, E. Alshina, C. Kim

## Slide 2: Summary
EE1-2: Improved non-separable secondary transform
  Coding performance: -1.07%@AI, -0.61%@RA (EnC:100%, DeC: 100%)
  Used table size: 10,368 Bytes  93,240 Bytes
Proposed: EE1-2 with reduced table size
  Coding performance: -0.75%@AI, -0.41%@RA (EnC:100%, DeC: 100%)
  Used table size: 10,368 Bytes  31,968 Bytes

## Slide 3: Analysis of NSST improvement
Table size of NSST in JEM3.0
  Overall table size: 10,368 Bytes
Table size of NSST in EE1
  Overall table size: 7,560 Bytes + 85,680 Bytes = 93,240 Bytes
JEM3.0 (NSST_4x4) |  |  |  |  |  |  | 
 | Type | Mode | #Value | Bits |  | Total | 
g_aiNsst4x4[12][3][16][16] | 12 | 3 | 256 | 9 | = | 10368 | bytes
EE1 (NSST_4x4) |  |  |  |  |  |  | 
 | Type | Mode | #Value | Bits |  | Total | 
g_NsstSrt4x4[35][3][16] (range: 0 - 15) | 35 | 3 | 16 | 4 | = | 840 | bytes
g_NsstHyGTPar4x4[35][3][64] (range: 0 - 255) | 35 | 3 | 64 | 8 | = | 6720 | bytes
EE1 (NSST_8x8) |  |  |  |  |  |  | 
 | Type | Mode | #Value | Bits |  | Total | 
g_NsstSrt8x8[35][3][64] (range: 0 - 63) | 35 | 3 | 64 | 6 | = | 5040 | bytes
g_NsstHyGTPar8x8[35][3][768] (range: 0 - 255) | 35 | 3 | 768 | 8 | = | 80640 | bytes

## Slide 4: Proposed method
Reduced table size with NSST improvement
  Changing intra mode context from 35 to 12
  Overall table size: 2,592 Bytes + 29,376 Bytes = 31,968 Bytes
EE1 (NSST_4x4) |  |  |  |  |  |  | 
 | Type | Mode | #Value | Bits |  | Total | 
g_NsstSrt4x4[12][3][16] (range: 0 - 15) | 12 | 3 | 16 | 4 | = | 288 | Bytes
g_NsstHyGTPar4x4[12][3][64] (range: 0 - 255) | 12 | 3 | 64 | 8 | = | 2304 | Bytes
EE1 (NSST_8x8) |  |  |  |  |  |  | 
 | Type | Mode | #Value | Bits |  | Total | 
g_NsstSrt8x8[12][3][64] (range: 0 - 63) | 12 | 3 | 64 | 6 | = | 1728 | Bytes
g_NsstHyGTPar8x8[12][3][768] (range: 0 - 255) | 12 | 3 | 768 | 8 | = | 27648 | Bytes
const UChar g_NsstLut[NUM_INTRA_MODE - 1] =
{//0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 64 65 66
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 17, 18, 19, 20, 21, 22, 23, 24, 25, 26, 27, 28, 29, 30, 31, 32, 33, 34, 33, 32, 31, 30, 29, 28, 27, 26, 25, 24, 23, 22, 21, 20, 19, 18, 17, 16, 15, 14, 13, 12, 11, 10, 9, 8, 7, 6, 5, 4, 3, 2};
const UChar g_NsstLut[NUM_INTRA_MODE - 1] =
{//0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 64 65 66
0 ,0 ,2 ,3 ,2 ,3 ,2 ,3 ,8 ,9 ,8 ,9 ,8 ,9,14,14,14,17,17,17,20,20,20,23,24,23,24,23,24,29,30,29,30,29,30,29,30,29,30,29,24,23,24,23,24,23,20,20,20,17,17,17,14,14,14 ,9 ,8 ,9 ,8 ,9 ,8 ,3 ,2 ,3 ,2 ,3 ,2}

## Slide 5: Conclusion
In this contribution, it is proposed to use reduced table size of EE1 NSST which shows less required table size while preserving coding performance.
It is proposed to use the reduced table size for NSST about 1/3 size of table of NSST in EE1.

## Slide 6: Thank You