## Slide 1: Co-projection-plane based motion compensated prediction for cubic format VR content (JVET-D0061)
Xiang Ma, Haitao Yang, Zhijie Zhao (Huawei)
Li Li, Houqiang Li (USTC)

## Slide 2: Contents
Motivations
Co-projection-plane (CPP) based motion compensated prediction for cubic format VR content
Experimental results
Conclusions

## Slide 3: Motivations
Due to the current frame work of coding, compression and display, the 360 degree/VR video content is represented by equirectangular format (ERP), cube map format (CMP), or icosahedron format (IHP) . These formats is further packed to a 2D picture.
Mapping process of CMP: the pixel value of M’ on the face ABCD is equal to pixel M, which is on the inscribed sphere surface, and M is the intersection point of OM’ and the sphere surface. Plane A’B’C’D’ is the projection plane of face ABCD. Each face has its own projection plane, which is the plane the face belongs to.

## Slide 4: Motivations
The cubic surface can be unfolded to a 2-D picture according to a cubic layout format.
Cubic surface
Irregular 2-D picture
Regular 2-D picture

## Slide 5: Motivations
There is texture discontinuity near the face boundary, which is marked by the red boxes. When motion compensated prediction (MCP) process is operated across the face boundary, pixel guided by motion vector from different face (or projection plane) of the current pixel will be directly referred, but this will affect the efficiency of MCP process.

## Slide 6: CPP based motion compensated prediction for cubic format
When the MCP process is operated across the face boundary, the new reference pixel value which is in the CPP of current pixel will be derived. E.g., the reference pixel T in the reference picture is not in the same face, which the current pixel P in current picture belongs to. In this case, the new reference pixel value of T is derived.
Current picture
Reference picture

## Slide 7: Derivation process
The pixel position of the new reference pixel in the cubic surface needs to be determined
A’B’C’D’ is the projection plane of Front face, and it is the CPP of the current pixel
H is the intersection point of OT and the face BCGF. The position of H is the position of the new reference pixel in the cubic surface
The position of the new reference pixel in the reference picture can be further derived as (1) and (2) with the layout information. is the cube edge length,
, . L denotes the length of a line.
(1)
(2)

## Slide 8: Derived reference pixels
The area near the face boundary of the new reference pixels shows less texture discontinuity compared to original reference pixels, which would improve the efficiency of MCP.
Original candidate reference pixels
New candidate reference pixels

## Slide 9: Test results
sequences | RA main |  |  | LDB main |  |  | LDP main |  | 
 | Y | U | V | Y | U | V | Y | U | V
AbyssGreatShark | -0.4 | -1.4 | -1.0 | -0.4 | -1.1 | -0.8 | -0.4 | -0.7 | -0.5
Bicyclist | -1.0 | -1.9 | -2.3 | -1.3 | -1.6 | -1.4 | -1.0 | -1.3 | -1.2
Glacier | -4.5 | -4.3 | -4.6 | -6.6 | -6.5 | -6.6 | -6.5 | -6.4 | -6.0
ParamotorTraining | -0.4 | -0.5 | -0.7 | -1.0 | -1.0 | -1.0 | -0.9 | -0.5 | -0.8
Skateboarding | 0.0 | -0.3 | -0.2 | 0.2 | 0.1 | 0.2 | 0.2 | 0.1 | 0.0
TimelapseBasejump | -0.1 | -0.3 | 0.0 | -0.2 | -0.7 | -0.1 | 0.2 | 0.1 | -0.2
TimelapseBuilding | -1.6 | -1.8 | -1.6 | -3.0 | -3.2 | -2.5 | -2.7 | -1.7 | -2.1
Average | -1.2 | -1.5 | -1.5 | -1.7 | -2.0 | -1.7 | -1.6 | -1.5 | -1.5
The BD-rate (%) performance of proposed method compared with HM16.6
Cubic format VR test sequences with 4x3 layout are tested. The test length of each sequence is 60 frames.
QPs are 22, 27, 32, 37.

## Slide 10: Conclusions
A co-projection-plane (CPP) based motion compensated prediction (MCP) method for cubic format Virtual Reality (VR) content is proposed.
Compared to HM16.6, the proposed method achieves 1.2%, 1.7%, 1.6% luma BD-rate reductions on average for RA, LDB and LDP configurations, respectively.
It is suggested to establish an EE on MCP for 360 degree VR content.