## Slide 1: Asymmetric Coding Units in QTBT
JVET-D0064
October 2016
F.Le Léannec, T.Poirier, F.Urban

## Slide 2: Introduction
  QTBT offers flexibility to divide the picture into CUs
    Quad-Tree followed by Binary-Tree decomposition
    No more PU or TU: Prediction Block=Transform Block=Coding Block
    Luma/Chroma coding tree separation
  Question raised:
    Can spatial topologies provided by QTBT be further improved?

## Slide 3: Proposal
  Extended set of Coding Unit sizes
    4 new Binary Tree Split modes: HOR_UP, HOR_DOWN, VER_LEFT, VER_RIGHT

## Slide 4: Binary-Tree Syntax arrangement
  BT Split mode Coding:
2 added flags

## Slide 5: JEM-3.0 Other Adaptations
  Transform
    EMT set of transform extended to CU sizes 12 and 24
      DCT-II, DCT-V, DCT-VIII, DST-I and DST-VII
      Partial Butterfly provided in the code for DCT-II
  Quantized Coefficients Entropy Coding
    Easy Adaptation: new CU sizes = superset of 4x4 Coding Groups
    Some contexts re-used from surrounding size : last significant coefficient XY and significant coefficient flag
  De-blocking
    Trivial adaptation of the recursive process (xDeblockCU) to new BT split modes

## Slide 6: JEM-3.0 Other Adaptations
  New block sizes (12, 24) introduced in Chroma
    Need to set MaxBTSizeISliceC to 64 (instead of 16 in QTBT test 3 config from Geneva)
    Allows CU size up to 32 in Chroma
    Impact on the JEM-3.0 behavior:

## Slide 7: Encoder Speed-Ups (1/2)
  Avoid Redundant RD searches between Symmetric and Asymmetric cases:
    Perfect match between ‘past’ and ‘present’ implies a normative modification:
      EmtCuFlag Context Model initially indexed by the CU QT depth (context_index=QT_depth)
      Now: EmtCuFlag Context Model indexed as a function of the CU spatial size
    One bug fix (ticket #29) brought to the code to ensure perfect match between rate cost estimation in the RDO and actual coding rate
  RSAF deactivated for CU size equal to
    Includes syntax and decoding process modifications
HOR+HOR
past
HOR_UP
present

## Slide 8: Encoder Speed-Ups (2/2)
  Heuristics:
    If( RDCost(HOR_SPLIT) > RDCost(NO_SPLIT) ) then disable asymmetric horizontal
    If( RDCost(VER_SPLIT) > RDCost(NO_SPLIT) ) then disable asymmetric vertical
    If( RDCost(HOR_SPLIT) > RDCost(VER_SPLIT) ) then disable asymmetric horizontal
    If( RDCost(VER_SPLIT) > RDCost(HOR_SPLIT) ) then disable asymmetric vertical
  Use of « Remove Redundant BT structure » in INTRA:
    Improved as follows
MinBTSize

## Slide 9: Performances over unchanged JEM-3.0
  Full RD search:
  With speed-ups:

## Slide 10: Performances over (JEM-3.0 + MaxBTSizeISliceC=64)
  Full RD search:
  With speed-ups:

## Slide 11: On trade-off between Encoding Time and Coding Efficiency
  One Intra Frame coded with:
    Several QTBT configurations (MaxBTDepthISliceL=3, 4, 5, 6)
    Several Asymmetric CU configurations (various values and other speed-ups)
  Coding Efficiency of QTBT is increased at equivalent coding runtime

## Slide 12: Conclusions
  QTBT framework has been enriched for increased flexibility
    4 new Binary Tree Split modes: HOR_UP, HOR_DOWN, VER_LEFT, VER_RIGHT
    Codec adaptation to support new CU sizes (12, 24)
  JEM-3.0 performance is improved with Asymmetric Coding in All-Intra
    1.54% gain in Luma with 407% coding time ratio
    1.16% gain in Luma with 217% coding time ratio
  No added complexity on the Decoder side
  Suggestion is to integrate the proposed tool in an EE on Coding Structures