## Slide 1: JVET-D0123: Enhanced Motion Vector Difference Coding
Jianle Chen, Wei-Jung Chien, Nan Hu, Vadim Seregin, Marta Karczewicz, Xiang Li
Qualcomm Incorporated

## Slide 2: Outline
Contribution
  Enlarged search range for RA configuration
  More accurate motion information during inter search stage
  Improved MVD coding
Results
  Encoder and configuration changes: 1.01%
  With proposed method: 1.55%

## Slide 3: Encode and configuration changes
Background
  In JVET CTC, search range of 64 luma sample with GOP size 16 in Random Access Configuration
  Very rough bits estimation is used for refIdx, interDir, AMVP idx, MVD during Motion Estimation stage
Suggestion
  Set search range as 256 luma sample
  Use more accurate bits estimation for motion related information during ME stage

## Slide 4: Enhanced MVD coding (1)
Adaptive motion vector accuracy in JEM
  1/16 pel for MV storage and motion compensation
  MVD signaling
    Switchable between ¼ pel and integer pel accuracy at CU level
Proposed
  MVD can be signaled in 4-pel accuracy
  Binarization and context modeling for MVD are dependent on the MVD precision and the POC distance between the current frame and the reference frame

## Slide 5: Enhanced MVD coding (2)
Syntax element | Context model/Binarization parmeter | Integer or four luma sample precision, or POC distance =1 | Quarter pel and POC distance > 1
abs_mvd_greater0_flag | CtxIdx | 0 | 0
abs_mvd_greater1_flag | CtxIdx | 1 | 2
abs_mvd_remaining_value (unary portion) | CtxIdx | 3 | 4
abs_mvd_remaining_value | Exp-Golomb Code Parameter | 1 | 2
Syntax element | Context model/Binarization parmeter | Integer or four luma sample precision, or POC distance =1 | Quarter pel and POC distance > 1
abs_mvd_greater0_flag | CtxIdx | 0 | 0
abs_mvd_greater1_flag | CtxIdx | 1 | 1
abs_mvd_remaining_value | Exp-Golomb Code Parameter | 1 | 1
JEM MVD coding
Proposed method

## Slide 6: Simulation results
Anchor: JEM3.1 with search range equal to 64
encoder-only changes + SR256
Proposed method + encoder-only changes + SR256