## Slide 1: AHG5: Improved fast encoding setting (JVET-E0023)
JVEt 5th Meeting: Geneva, CH, 12–20 Jan. 2017
Yoshiya Yamamoto, Tomohiro Ikai, Yukinobu Yasugi
SHARP Corporation

## Slide 2: Introduction
Early CU determination in QTBT
Related contributions in the last meeting
  JVET-D0053(Samsung) – changes SKIP_DEPTH from 3 to 2.
  JVET-D0095(SHARP) – early CU determination based on TemporalID(TID).
→We combined these two methods and modified it to use the distance to reference pictures instead of TID.
if (rpcBestCU->getSkipFlag(0) && (bTestHorSplit ¦¦ bTestVerSplit) && uiBTDepth>=SKIP_DEPTH) { // stop remaining partitioning process bTestHorSplit = bTestVerSplit = bQTSplit = false; }

## Slide 3: Proposed method
SKIP_DEPTH is changed by the picture distance
  If the picture distance <= 2, SKIP_DEPTH is set to 2, otherwise 3.
<Random Access>
I
B
B
B
B
B
B
B
B
TID = 0
TID = 1
TID = 2
TID = 4
TID = 3
SKIP_DEPTH = 2
SKIP_DEPTH = 3
4
2
1

## Slide 4: Proposed method
SKIP_DEPTH = 2
The picture distance is always 1 in Low-Delay configuration,  SKIP_DEPTH is always 2.
<Low-Delay B>
  If TID is used instead of the distance, SKIP_DEPTH is set to 3 (unchanged).
I
B
B
B
TID = 0
1
1
1

## Slide 5: Performance
Test A: SKIP_DEPTH = ( {picture_distance} <= 2)? 2: 3
 | Random Access Main 10 (Parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.18% | 0.04% | 0.11% | 91% | 100%
Class A2 | 0.24% | 0.04% | 0.01% | 86% | 88%
Class B | 0.27% | -0.13% | -0.14% | 88% | 99%
Class C | 0.24% | -0.01% | 0.05% | 89% | 102%
Class D | 0.20% | -0.13% | -0.03% | 87% | 104%
Class E |  |  |  |  | 
Overall (Ref) | 0.23% | -0.04% | -0.01% | 88% | 98%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.31% | 0.24% | 0.01% | 83% | 96%
Class C | 0.31% | 0.22% | 0.07% | 88% | 95%
Class D | 0.24% | -0.04% | 0.26% | 85% | 98%
Class E | 0.09% | 1.07% | 0.08% | 76% | 103%
Overall (Ref) | 0.25% | 0.32% | 0.10% | 83% | 98%

## Slide 6: Performance
Test B: SKIP_DEPTH = ( {picture_distance} <= 1)? 2: 3
 | Random Access Main 10 (Parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | -0.01% | 0.06% | 94% | 101%
Class A2 | 0.12% | 0.00% | -0.02% | 90% | 96%
Class B | 0.14% | -0.09% | -0.07% | 93% | 104%
Class C | 0.13% | -0.03% | -0.01% | 92% | 99%
Class D | 0.10% | -0.10% | -0.06% | 91% | 104%
Class E |  |  |  |  | 
Overall (Ref) | 0.12% | -0.05% | -0.02% | 92% | 101%

## Slide 7: Conclusion
The proposed method is to change the threshold for early CU determination depending on the picture distance.
The experimental results show better encoding time / performance balance than constant SKIP_DEPTH setting.
We suggest this proposal to be included in the next version of the JEM.

## Slide 9: Settings of SKIP_DEPTH
distance between pictures | SKIP_DEPTH |  | 
 | D0053 Set1 | TestA | TestB
4 > | 2 | 3 | 3
3 | 2 | 3 | 3
2 | 2 | 2 | 3
1 | 2 | 2 | 2
Table 2. SKIP_DEPTH settings